## Slide 1: Non-CE10: A CNN based in-loop filter for intra frame
Luhang Xu, Jianqing Zhu, Kimihiko Kazui
Fujitsu

## Slide 2: Outline
Proposed Method
Training details
Experiment Result
Conclusion

## Slide 3: Proposed Method
Replace the De-blocking filter
Y and UV share the same structure but different Parameters
  N=4, N is the sub-sampling convolution kernel size and stride.
  M=32, M is the based output depth for convolution kernel.

## Slide 4: Proposed Method
Residual block
  Four residual blocks in experiment.

## Slide 5: Proposed Method
Qstep is a corresponding parameter of QP.
A general quantizer is defined as:
  In VTM, Qstep will be doubled with the increment by 6 of Qp.
Qstep is approximated by g_quantScale in quant.cpp
  Qstep ranges from 1~228 and is normalized by /228.0 for input.

## Slide 6: Training details
Mandatory | Information in Training Stage |  | 
 | Basic Settings: |  | 
 |  | learning rate: | 1e-4
 |  | optimizer: | ADAM
 |  | batch size: | 500
 |  | epoch: | 400
 |  | loss function: | L2
 |  | training GPU: | GTX TITAN X
 |  | training time: | each model 30h
 |  | framework: | TensorFlow
Optional | Other Settings: |  | 
 |  | Patch size | 64x64
 |  | Dataset | DIV2K
 |  | QP set for generating training dataset | 22,27,32,37

## Slide 7: Experiment Result
Result for AI config (CPU)
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.91% | -0.16% | -2.45% | 103% | 1297%
Class A2 | -1.59% | -1.83% | -2.35% | 105% | 1068%
Class B | -1.11% | -2.42% | -3.87% | 103% | 1021%
Class C | -1.57% | -3.26% | -5.46% | 99% | 791%
Class E | -2.18% | -4.66% | -1.81% | 99% | 1204%
Overall | -1.44% | -2.51% | -3.39% | 102% | 1040%
Class D | -2.03% | -2.81% | -4.21% | 94% | 838%
Class F | 0.49% | -2.89% | -3.63% | 103% | 978%

## Slide 8: Subjective Quality
Class-E, sequence ‘Four people’ and Qp=37
(a) VTM-5.0
(b) Proposed

## Slide 9: Conclusion
Proposed a CNN filter for Intra frame
to replace De-blocking filter.
Control the filtering strength by Qstep.
Balance performance and speed.

## Slide 10
Thank you for your attention!