## Slide 1: JVET-O0158 Non-CE5: Deblocking based on DMVR refined motion K. Andersson, J. Enhorn (Ericsson)
Kenneth Andersson
Ericsson
2019-07-05

## Slide 2: Problem statement
Deblocking unaware of actual differences in motion since actual motion used for DMVR prediction is not used for deblocking
  Gives remaining block artifacts after deblocking
  Artifacts can also appear inside DMVR CU’s on boundaries of DMVR sub-blocks (16x16)

## Slide 3: Proposed solution
Use actial motion used for DMVR prediction for deblocking filtering
Deblock DMVR sub-block boundaries using VVC sub-block deblocking functionality

## Slide 4: Subjective example (ALF off)
Figure: Kimono, POC 133, RA QP 37, ALF OFF. Left: VTM-5.0, Right: Proposed

## Slide 5: Subjective example (ALF on)
Figure: Kimono, POC 137, RA QP 37, ALF ON. Left: VTM-5.0, Right: Proposed

## Slide 6: Objective results
 | Random access Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,09% | -0,06% | -0,02% | 100% | 103%
Class A2 | -0,04% | 0,04% | 0,00% | 100% | 104%
Class B | 0,00% | -0,02% | -0,02% | 101% | 102%
Class C | -0,03% | 0,03% | -0,10% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0,03% | 0,00% | -0,04% | 100% | 102%
Class D | -0,03% | 0,01% | 0,03% | 100% | 102%
Class F | 0,00% | 0,01% | 0,01% | 96% | 103%
 | Random access (ALF off) Over VTM-5.0 without ALF |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,18% | -0,01% | -0,02% | 103% | 102%
Class A2 | -0,07% | 0,01% | 0,04% | 104% | 104%
Class B | -0,04% | -0,02% | 0,00% | 103% | 102%
Class C | -0,03% | 0,00% | -0,02% | 103% | 101%
Class E |  |  |  |  | 
Overall | -0,07% | 0,00% | 0,00% | 103% | 102%
Class D | -0,04% | 0,03% | 0,01% | 100% | 100%
Class F | 0,00% | -0,02% | 0,01% | 105% | 102%

## Slide 7: Conclusion
Deblocking can work as expected if actual motion for DMVR prediction is used.
Benefits in subjective quality at BDR impact of -0.03%/-0.07% for RA.
The fix is to use actual DMVR motion for deblocking in combination with VVC sub-block deblocking functionality.
It is proposed include the fix for next version of VVC.
Thanks to Mediatek for cross-check