## Slide 1: JVET-O0159 Non-CE5: Deblocking tC table defined for 10-bit video K. Andersson, J. Enhorn (Ericsson)
Kenneth Andersson
Ericsson
2019-07-05

## Slide 2: Problem statement
Current tC table for deblocking filter is design for 8-bit video:
  For 10-bit video the tC table is upscaled which gives suboptimal variation of tC with QP
Current tC table:
  tC=[0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,1,1,1,1,1,1,1,1,1,2,2,2,2,3,3,3,3,4,4,4,5,5,6,6,7,8,9,10,11,13,14,16,18,20,22,25, 28, 31, 35, 39, 44, 50, 56, 63, 70, 79, 88, 99]
Upscaled tC table when video is encoded with 10-bits:
  tC*4= [0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,4,4,4,4,4,4,4,4,4,8,8,8,8,12,12,12,12,16,16,16, 20,20,24,24,28,32,36,40,44,52,56,64,72,80,88,100,112,124,140,156,176,200,224,252,280,316,352,396]

## Slide 3: Proposed solution
tC table adapted for 10 bit video:
  tC=[0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,3,4,4,4,4,5,5,6,6,7,7,8,9,9,10,11,13,14,15,17, 19,21,24,26,29,33,36,41,45,51,57,64,71,80,89,100,112,126,141,158,177,198,222,250,280,314,352,395]
Plot of tC versus quantization step size for VVC (black circle) and proposed (greed diamond).
Plot of tC versus QP for VVC (black circle) and proposed (greed diamond).

## Slide 4: Objective results
 | All intra Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,11% | 0,38% | 0,20% | 93% | 100%
Class A2 | 0,08% | 0,44% | 0,57% | 93% | 99%
Class B | 0,07% | 0,44% | 0,41% | 93% | 101%
Class C | 0,04% | 0,43% | 0,44% | 100% | 100%
Class E | 0,05% | 0,25% | 0,10% | 92% | 101%
Overall | 0,07% | 0,40% | 0,36% | 95% | 100%
Class D | 0,04% | 0,37% | 0,35% | 98% | 102%
Class F | 0,03% | 0,47% | 0,52% | 94% | 102%
 | Random access Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | -0,29% | 0,06% | 99% | 99%
Class A2 | -0,03% | -0,13% | -0,30% | 99% | 103%
Class B | -0,02% | -0,30% | -0,29% | 98% | 101%
Class C | -0,05% | -0,56% | -0,65% | 99% | 102%
Class E |  |  |  |  | 
Overall | -0,03% | -0,33% | -0,32% | 99% | 101%
Class D | -0,01% | -0,35% | 0,00% | 98% | 101%
Class F | 0,00% | -0,62% | -0,70% | 103% | 101%
 | Low delay B Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,06% | 0,11% | 0,11% | 99% | 103%
Class C | -0,07% | 0,07% | -0,07% | 102% | 100%
Class E | -0,16% | 0,17% | -0,09% | 97% | 101%
Overall | -0,09% | 0,11% | 0,00% | 99% | 101%
Class D | -0,09% | 0,07% | 0,07% | 102% | 100%
Class F | -0,11% | -0,24% | -0,28% | 101% | 99%
 | Low delay P Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,07% | 0,01% | -0,03% | 102% | 100%
Class C | -0,02% | -0,47% | -0,08% | 100% | 101%
Class E | -0,13% | 0,69% | -0,19% | 99% | 100%
Overall | -0,07% | 0,02% | -0,09% | 101% | 100%
Class D | -0,04% | -0,31% | 0,16% | 101% | 99%
Class F | -0,06% | -0,05% | 0,05% | 104% | 103%

## Slide 5: Conclusion
Since focus for VVC is rather 10-bit video than 8-bit video it make some sense to adapt the tC table for 10-bit video.
BDR impact of 0.07%/-0.09%/-0.03%/-0.07% for AI/RA/LD/LDP.
It is proposed update the tC table in next version of VVC.