## Slide 1: JVET-O0167: Non-CE4: On SbTMVP base motion data derivation
Jie “Jane” Zhao, Seung Hwan Kim
LG ELECTRONICS

## Slide 2: Introduction
In SbTMVP, base motion data is derived first and used to fill sub-CU’s motion data when sub-CU MV is not available.
Base motion and sub-CU motion data derivation are similar to TMVP and require temporal motion vector scaling.
It is asserted that a separate base motion data derivation process is unnecessary.
This contribution proposes to remove this separate base motion data derivation process by simply re-using one of the sub-CU’s motion data as base motion data.
This reduces SbTMVP complexity. No loss. There is even small gain.

## Slide 3: Background
SbTMVP predicts the motion vectors of the sub-CUs within the current CU in three steps:
Step 1: Obtain MV shift from neighbor A1

## Slide 4: Background
Step 2: Obtain base motion data from the corresponding block that covers the center of the collocated CU (with MV shift).
  If the corresponding block is not coded in inter mode, availableFlagSbCol is set as false and SbTMVP process stops.
  Otherwise, the motion information of the corresponding block is used to derive the base motion data.
Step 3: Obtain sub-CU motion information from corresponding block that covers the center sample of the collocated sub-CU.
  If motion data of sub-CU is not available, uses base motion data as the sub-CU’s motion data.
Both base motion and sub-CU motion data derivation are similar to TMVP and require temporal motion vector scaling for each list.

## Slide 5: Background
The MV derivation process for base motion data and sub-CU motion data are the same except they are having different block positions.
To obtain base motion vector, it needs a separate MV derivation process.
O indicates sample position for base motion data derivation
X indicates sample position for sub-CU motion data derivation

## Slide 6: Proposed Method
Why not make the sample position used for base motion data derivation same as one of the sub-Cu’s positon? Then we don’t need a separate derivation for base motion data
Center
Sub-CU
Top-left
Sub-CU
Option 1: Align with the sub-CU close to the center
  (numSbX>>1, numSbY>>1)
Option 2: Align with the top-left sub-CU

## Slide 7: Proposed method
Simply changing the sample position for deriving base motion data derivation from
  xCtr = xCb + ( cbWidth / 2 ) (8‑529)
  yCtr = yCb + ( cbHeight / 2 ) (8‑530)
To
  xCtr = xCb + ( numSbX >>1)*sbWidth (8‑529)
  yCtr = yCb + ( numSbY >>1)*sbHeight (8‑530)
Then if the location for sub-block MV derivation (xSb, ySb) is as the (xCt, yCtr), no need to derive the sub-block MV again.

## Slide 8: Proposed method
Alternative implementation: put this base motion vector assignment in the sub-block processing loop (reduce more lines in draft text).
Since there are no dependencies between sub-CUs, the sub-CU’s can be processed in any order.
If using the top-left sub-CU as base motion data, no need to change current processing order.
If using the center sub-CU as base motion data, sub-CU at (numSbX>>1, numSbY>>1) needs to be checked first. This can be easily done by arranging the loop index and sub-CU index.

## Slide 9: Experimental Results
If using center sub-CU for base motion data
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.19% | -0.09% | 100% | 100% |  |  |  |  | 
Class A2 | -0.01% | -0.04% | -0.04% | 100% | 100% |  |  |  |  | 
Class B | 0.02% | 0.05% | -0.01% | 100% | 100% | -0.01% | 0.20% | 0.17% | 99% | 95%
Class C | -0.01% | -0.01% | 0.00% | 100% | 98% | 0.01% | -0.05% | -0.25% | 99% | 96%
Class E |  |  |  |  |  | -0.01% | 0.03% | -0.25% | 100% | 101%
Overall | 0.00% | -0.03% | -0.03% | 100% | 100% | 0.00% | 0.08% | -0.08% | 99% | 97%
Class D | 0.01% | -0.03% | 0.04% | 100% | 99% | 0.01% | 0.02% | 0.64% | 100% | 102%
Class F | 0.00% | 0.01% | -0.01% | 100% | 100% | 0.03% | 0.24% | 1.18% | 100% | 98%

## Slide 10: Experimental Results
If using Top-left sub-CU for base motion data
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.15% | 0.03% | 100% | 100% |  |  |  |  | 
Class A2 | -0.01% | 0.05% | 0.07% | 99% | 100% |  |  |  |  | 
Class B | 0.02% | 0.07% | 0.05% | 100% | 101% | 0.01% | 0.28% | -0.13% | 99% | 95%
Class C | -0.02% | -0.03% | -0.04% | 100% | 99% | 0.02% | -0.05% | 0.06% | 100% | 97%
Class E |  |  |  |  |  | 0.12% | -0.06% | 0.14% | 100% | 99%
Overall | 0.00% | -0.01% | 0.03% | 100% | 100% | 0.04% | 0.09% | 0.00% | 100% | 97%
Class D | 0.01% | 0.02% | 0.09% | 100% | 99% | 0.01% | -0.08% | 0.63% | 100% | 100%
Class F | 0.00% | -0.02% | -0.05% | 100% | 100% | 0.07% | 0.23% | 0.41% | 100% | 98%

## Slide 11: Conclusion
Proposed a simplification to SbTMVP base motion data derivation by re-using one of the sub-CU’s motion data as base motion data.
It avoids a separate base motion data derivation process, and therefore removes the associated temporal motion vector scalings.
There is no loss, and even a tiny gain.
  RA: 0.00%, -0.03%, -0.03%
  LD: 0.00%, 0.08%, -0.08%
Propose to adopt this simplification into VVC draft and software (using the center sub-CU’s motion as base motion).
Thanks ByteDance for Cross-checking!