## Slide 1: JVET-O0194: On chroma-CU-related flags and coding information
Yin Zhao and Haitao Yang (Huawei)
JVET-O0194

## Slide 2: Introduction
Aspect 1: spec improvement (add chType to variables that may be different for luma CB and chroma CB at the same location)
  CuPredMode
  CqtDepth
  CbWidth, CbHeight, CbPosX, CbPosY
Aspect 2: simplify context models related to four flags
Flags | Context modeling dependency
pred_mode_ibc_flag | CuPredMode[xNbL][yNbL], CuPredMode[xNbA][yNbA] (in line buffer)
split_qt_flag | CqtDepth[xNbL][yNbL], CqtDepth[xNbA][yNbA]
split_cu_flag | CbHeight[xNbL][yNbL], CbWidth[xNbA][yNbA]
mtt_split_cu_vertical_flag | CbHeight[xNbL][yNbL], CbWidth[xNbA][yNbA]
JVET-O0194

## Slide 3: Aspect 1: resolve ambiguity in VVC draft 5
When separate tree is used, the following coding information may be different for luma CB and chroma CB at the same location (x,y)
  CuPredMode[x][y] (used 35 times in the spec)
  CqtDepth[x][y] (2)
  CbWidth[x][y] (9)
  CbHeight[x][y] (9)
  CbPosX[x][y] (6)
  CbPosY[x][y] (6)
To resolve ambiguity, the six variables should be extended with channel type
  CuPredMode[x][y] -> CuPredMode[chType][x][y]
  CqtDepth[x][y] -> CqtDepth[chType][x][y]
  …
  Luma: chType = 0; Chroma: chType = 1
  Related modifications are made on top of VVC draft 5 version 9 (c.f. JVET-N1001-v9_r1.docx)
JVET-O0194

## Slide 4: Some examples of the modification (1)
JVET-O0194

## Slide 5: Some examples of the modification (2)
JVET-O0194

## Slide 6: Aspect 2: simplification on context modeling
Neighbor-based ctx modeling for four flags
  pred_mode_ibc_flag, split_qt_flag, split_cu_flag, mtt_split_cu_vertical_flag
  6 bits per 4x4 in line buffer are needed for storing the variables for chroma CBs
Therefore, three tests were made to reduce line buffer
Flags | Context modeling dependency
pred_mode_ibc_flag | CuPredMode[xNbL][yNbL], CuPredMode[xNbA][yNbA] (in line buffer)
split_qt_flag | CqtDepth[xNbL][yNbL], CqtDepth[xNbA][yNbA]
split_cu_flag | CbHeight[xNbL][yNbL], CbWidth[xNbA][yNbA]
mtt_split_cu_vertical_flag | CbHeight[xNbL][yNbL], CbWidth[xNbA][yNbA]
 | Number of possible values | required bits
CuPredMode (for chroma CB in I slice) | 2: INTRA, IBC | 1
CqtDepth (for chroma CB in I slice) | 4: 1 (64x64) ~ 4 (8x8) | 2
CbWidth (for chroma CB in I slice) | 5: 4 ~ 64 | 3
JVET-O0194

## Slide 7: Test description and the coding results
 | Flags for chroma CBs | Dependency removal | Left neighbor | Above neighbor | BD-rate Y (AI) | BD-rate U (AI) | BD-rate V (AI) | BD-rate Y (RA) | BD-rate U (RA) | BD-rate V (RA)
Test 1 | pred_mode_ibc_flag | CuPredMode | x | x | 0.00% | -0.01% | 0.02% | 0.02% | -0.03% | 0.01%
 | split_qt_flag | CqtDepth | x | x |  |  |  |  |  | 
 | mtt_split_cu_vertical_flag | CbHeight, CbWidth | use | use |  |  |  |  |  | 
 | split_cu_flag | CbHeight, CbWidth | use | use |  |  |  |  |  | 
Test 2 | pred_mode_ibc_flag | CuPredMode | x | x | 0.06% | 0.23% | 0.25% | 0.02% | -0.02% | 0.11%
 | split_qt_flag | CqtDepth | x | x |  |  |  |  |  | 
 | mtt_split_cu_vertical_flag | CbHeight, CbWidth | x | x |  |  |  |  |  | 
 | split_cu_flag | CbHeight, CbWidth | x | x |  |  |  |  |  | 
Test 3 | pred_mode_ibc_flag | CuPredMode | x | x | 0.02% | 0.13% | 0.22% | 0.00% | 0.00% | -0.03%
 | split_qt_flag | CqtDepth | x | x |  |  |  |  |  | 
 | mtt_split_cu_vertical_flag | CbHeight, CbWidth | x | x |  |  |  |  |  | 
 | split_cu_flag | CbHeight, CbWidth | use | x |  |  |  |  |  | 
Test 1 reduces 3 bits/4x4
Test 2 reduces 6 bits/4x4
Test 3 reduces 6 bits/4x4 -> suggestion for adopting this simplification method
JVET-O0194

## Slide 8: Draft Text for test 3
mtt_split_cu_vertical_flag
JVET-O0194

## Slide 9: Conclusion
Extend the six variables with chType to resolve the ambiguity in spec
Simplify the context modeling of flags related to chroma CBs
  reduce the line buffer by 6 bits per 4x4
  0.02% / 0.13% / 0.22% in AI
  0.00% / 0.00% / -0.03% in RA
Suggestion for adopting the spec fix and Test 3.
Thanks to Hikvision for the cross-check.
JVET-O0194