## Slide 1: Non-CE6: LFNST simplification based on the methods proposed in CE6-2.1a (JVET-O0209)
Moonmo Koo, Junghak Nam, Jaehyun Kim, Mehdi Salehifar, and Seung Hwan Kim

## Slide 2: Summary [1/2]
The features proposed in CE6-2.1a
  Max. 16 LFNST coefficients (a)
    For 4xN or Nx4 TU (N≥16), LFNST is allowed in only top-left 4x4 block.
  Additional zero-out of primary transform coefficients
    When 4x4 LFNST is applied (b)
    When 8x8 LFNST is applied (c)
  Change of the region where non-zero coefficients are counted (d)
    The additional zero-out is also taken account.
    Enables the existence check of non-zero coeff. easier with last coeff. position.
(b)
(c)

## Slide 3: Summary [2/2]
Test description and experimental results
  Basically, the feature (b) is disabled in all the five tests.
  Test 1 is the same as ones discovered in several other proposals.
  Compensation of 0.04% coding loss with 3% encoding time (CE6-2.1a vs. Test 2)
    Additionally, 0.11% loss in low QP for CE6-2.1a almost disappears in Test 2/3/4/5.
  Minor perf. difference between normative change vs. non-normative one
    Test 2 vs. Test 3, and Test 4 and Test 5
Thanks to KDDI and InterDigital for cross-checking
Test | Description | AI |  |  | RA |  | 
 |  | BD-rate | EncT | DecT | BD-rate | EncT | DecT
CE6-2.1a | (a)+(b)+(c)+(d) | 0.06% | 90% | 99% | 0.02% | 97% | 100%
Test 1 | (a) | 0.02% | 100% | 100% | 0.01% | 100% | 100%
Test 2 | (c)+(d) | 0.02% | 93% | 98% | 0.01% | 99% | 100%
Test 3 | (c) | 0.03% | 94% | 100% | 0.02% | 99% | 100%
Test 4 | (a)+(c)+(d) | 0.04% | 92% | 98% | 0.03% | 99% | 100%
Test 5 | (a)+(c) | 0.05% | 93% | 100% | 0.02% | 99% | 100%
(a) Max. 16 LFNST coefficients
(b) Additional zero-out of primary transform coefficients when 4x4 LFNST is applied
(c) Additional zero-out of primary transform coefficients when 8x8 LFNST is applied
(d) Change of the region where non-zero coefficients are counted

## Slide 4: Conclusion
Discussion
  How the proposed zero-out scheme is to be configured
    Coding loss vs. encoding time reduction
    Test 2/4 seem to be better trade-off than CE6-2.1a.
    Even disabling the feature (b) does not incur any complications in spec text.
  Whether normative changes due to the zero-out is necessary or not
    As far as our tests are concerned, normative changes would not be necessary.
    But, in the case of CE6-2.1a, normative change seems to be vital (0.12% coding gain in AI).
  Complexity reduction due to the proposed features
    Generally, zero-out may help complexity reduction.
    The encoder side reduction can be realized either normatively or non-normatively.
    It should be further discussed whether the zero-out would be essential in decoder implementation.
Conclusion
  It is recommended that the most beneficial decision should be made based on test results in this proposal together with those of CE6-2.1a from multiple perspectives.

## Slide 5: Appendix – All experimental results
Test | Desc. | AI |  |  | RA |  |  | RA /w inter-MTS on |  |  | AI 100frs, low-QP |  | 
 |  | BD-rate | EncT | DecT | BD-rate | EncT | DecT | BD-rate | EncT | DecT | BD-rate | EncT | DecT
CE6-2.1a | (a)+(b)+(c)+(d) | 0.06% | 90% | 99% | 0.02% | 97% | 100% | 0.02% | 97% | 99% | 0.11% | 83% | 102%
Test 1 | (a) | 0.02% | 100% | 100% | 0.01% | 100% | 100% | 0.02% | 100% | 100% | 0.01% | 100% | 100%
Test 2 | (c)+(d) | 0.02% | 93% | 98% | 0.01% | 99% | 100% | 0.03% | 99% | 100% | 0.00% | 92% | 100%
Test 3 | (c) | 0.03% | 94% | 100% | 0.02% | 99% | 100% | 0.02% | 99% | 100% | 0.01% | 92% | 101%
Test 4 | (a)+(c)+(d) | 0.04% | 92% | 98% | 0.03% | 99% | 100% | 0.03% | 99% | 101% | 0.01% | 91% | 100%
Test 5 | (a)+(c) | 0.05% | 93% | 100% | 0.02% | 99% | 100% | 0.04% | 99% | 101% | 0.02% | 91% | 101%

## Slide 6: Appendix – Some of spec text differences between Test 2 and CE6-2.1a
8.7.4 Transformation process for scaled transform coefficients
……
The variables nonZeroW and nonZeroH are derived as follows:
If lfnst_idx[ xTbY ][ yTbY ] is not equal to 0, the following applies:
nonZeroW = ( nTbW == 4 | | nTbH == 4 ) ? 4 : 8
nonZeroH = ( nTbW == 4 | | nTbH == 4 ) ? 4 : 8
Otherwise, the following applies:
nonZeroW = Min( nTbW, ( trTypeHor > 0 ) ? 16 : 32 ) (8‑967)
nonZeroH = Min( nTbH, ( trTypeVer > 0 ) ? 16 : 32 ) (8‑968)
……
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
……
numSbCoeff = 1 << ( log2SbW + log2SbH )
lastScanPos = numSbCoeff
lastSubBlock = ( 1 << ( log2TbWidth + log2TbHeight − ( log2SbW + log2SbH ) ) ) − 1
do {
if( lastScanPos = = 0 ) {
lastScanPos = numSbCoeff
lastSubBlock− −
}
lastScanPos− −
xS = DiagScanOrder[ log2TbWidth − log2SbW ][ log2TbHeight − log2SbH ] [ lastSubBlock ][ 0 ]
yS = DiagScanOrder[ log2TbWidth − log2SbW ][ log2TbHeight − log2SbH ] [ lastSubBlock ][ 1 ]
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ lastScanPos ][ 0 ]
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ lastScanPos ][ 1 ]
} while( ( xC != LastSignificantCoeffX ) ¦ ¦ ( yC != LastSignificantCoeffY ) )
if( ( lastSubBlock > 0 && log2TbWidth >= 3 && log2TbHeight >= 3 ) ¦ ¦
( lastScanPos > 7 && ( log2TbWidth == 2 ¦ ¦ log2TbHeight == 3 ) && log2TbWidth == log2TbHeight ) ) {
lfnstZeroOutSigCoeffFlag = 1
}
……
}
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
……
numSbCoeff = 1 << ( log2SbW + log2SbH )
lastScanPos = numSbCoeff
lastSubBlock = ( 1 << ( log2TbWidth + log2TbHeight − ( log2SbW + log2SbH ) ) ) − 1
do {
if( lastScanPos = = 0 ) {
lastScanPos = numSbCoeff
lastSubBlock− −
}
lastScanPos− −
xS = DiagScanOrder[ log2TbWidth − log2SbW ][ log2TbHeight − log2SbH ] [ lastSubBlock ][ 0 ]
yS = DiagScanOrder[ log2TbWidth − log2SbW ][ log2TbHeight − log2SbH ] [ lastSubBlock ][ 1 ]
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ lastScanPos ][ 0 ]
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ lastScanPos ][ 1 ]
} while( ( xC != LastSignificantCoeffX ) ¦ ¦ ( yC != LastSignificantCoeffY ) )
if( ( lastSubBlock > 0 && log2TbWidth >= 2 && log2TbHeight >= 2 ) ¦ ¦
( lastScanPos > 7 && ( log2TbWidth == 2 ¦ ¦ log2TbHeight == 3 ) && log2TbWidth == log2TbHeight ) ) {
lfnstZeroOutSigCoeffFlag = 1
}
……
}
[ Test 2 ]
[ CE6-2.1a ]
8.7.4 Transformation process for scaled transform coefficients
……
The variables nonZeroW and nonZeroH are derived as follows:
nonZeroW = Min( ( lfnst_idx[ xTbY ][ yTbY ] > 0 && nTbW >= 8 && nTbH >= 8 ) ? 8 : nTbW, ( trTypeHor > 0 ) ? 16 : 32 ) (8‑967)
nonZeroH = Min( ( lfnst_idx[ xTbY ][ yTbY ] > 0 && nTbW >= 8 && nTbH >= 8 ) ? 8 : nTbH , ( trTypeVer > 0 ) ? 16 : 32 ) (8‑968)
……