## Slide 1: JVET-O0216: Non-CE5: Modification of ALF coefficient signalling
Anand Meher Kotra, Semih Esenlik, Biao Wang, Han Gao, Elena Alshina

## Slide 2: ALF coefficient signalling in VTM-5.0
Alf Coefficients are signalled using Kth order Exp golomb codes
Alf Luma filter coefficients are predicted from fixed filters
alf_luma_min_eg_order_minus1 | ue(v)
for( i = 0; i < 3; i++ ) | 
alf_luma_eg_order_increase_flag[ i ] | u(1)
if( alf_luma_coeff_delta_flag ) { | 
for( sfIdx = 0; sfIdx <= alf_luma_num_filters_signalled_minus1; sfIdx++ ) | 
alf_luma_coeff_flag[ sfIdx ] | u(1)
} | 
for( sfIdx = 0; sfIdx <= alf_luma_num_filters_signalled_minus1; sfIdx++ ) { | 
if( alf_luma_coeff_flag[ sfIdx ] ) { | 
for ( j = 0; j < 12; j++ ) { | 
alf_luma_coeff_delta_abs[ sfIdx ][ j ] | uek(v)
if( alf_luma_coeff_delta_abs[ sfIdx ][ j ] ) | 
alf_luma_coeff_delta_sign[ sfIdx ][ j ] | u(1)
} | 
} | 
} | 
if( alf_chroma_filter_signal_flag ) { | 
alf_chroma_clip_flag | u(1)
alf_chroma_min_eg_order_minus1 | ue(v)
for( i = 0; i < 2; i++ ) | 
alf_chroma_eg_order_increase_flag[ i ] | u(1)
for( j = 0; j < 6; j++ ) { | 
alf_chroma_coeff_abs[ j ] | uek(v)
if( alf_chroma_coeff_abs[ j ] > 0 ) | 
alf_chroma_coeff_sign[ j ] | u(1)
} | 
Table 1. alf_luma_coeff_delta_abs and alf_chroma_coeff_abs are signalled using Kth order Exponential golomb codes in VTM-5.0

## Slide 3: Proposal
Signal ALF coefficients using fixed 3rd oder Exp. Golomb codes
Advantage:
  Removal of unnecessary syntax elements with no BD-Rate impact
  Simplifies the encoder logic of determining K in the Kth order Exp. Golomb codes.
ue3(v) is 3rd order Exp. Golomb code
alf_luma_min_eg_order_minus1 | ue(v)
for( i = 0; i < 3; i++ ) | 
alf_luma_eg_order_increase_flag[ i ] | u(1)
if( alf_luma_coeff_delta_flag ) { | 
for( sfIdx = 0; sfIdx <= alf_luma_num_filters_signalled_minus1; sfIdx++ ) | 
alf_luma_coeff_flag[ sfIdx ] | u(1)
} | 
for( sfIdx = 0; sfIdx <= alf_luma_num_filters_signalled_minus1; sfIdx++ ) { | 
if( alf_luma_coeff_flag[ sfIdx ] ) { | 
for ( j = 0; j < 12; j++ ) { | 
alf_luma_coeff_delta_abs[ sfIdx ][ j ] | uek(v) ue3(v)
if( alf_luma_coeff_delta_abs[ sfIdx ][ j ] ) | 
alf_luma_coeff_delta_sign[ sfIdx ][ j ] | u(1)
} | 
} | 
} | 
if( alf_chroma_filter_signal_flag ) { | 
alf_chroma_clip_flag | u(1)
alf_chroma_min_eg_order_minus1 | ue(v)
for( i = 0; i < 2; i++ ) | 
alf_chroma_eg_order_increase_flag[ i ] | u(1)
for( j = 0; j < 6; j++ ) { | 
alf_chroma_coeff_abs[ j ] | uek(v) ue3(v)
if( alf_chroma_coeff_abs[ j ] > 0 ) | 
alf_chroma_coeff_sign[ j ] | u(1)
} | 

## Slide 4: CTC QPs (22, 27, 32, 37)

## Slide 5: High QPs (32, 37, 42, 47)

## Slide 6: Low QPs (12, 17, 22, 27)

## Slide 7: Conclusion
Substitute Kth order Exp. Golomb codes with fixed 3rd order Exp. Golomb codes for signalling ALF coefficients
Advantage:
  Removal of unnecessary syntax elements with no BD-Rate impact
  Simplifies the encoder logic of determining K in the Kth order Exp. Golomb codes.
Thank you MediaTek for cross check (JVET-O0786)

## Slide 8
Thank You
www.huawei.com