## Slide 1: JVET-O0232: CE2-related: No-latency LMCS Chroma Residual Scaling for Single tree and Dual tree
J. Zhao, S. Paluri, S. Kim
LG ELECTRONICS

## Slide 2: Introduction
In the LMCS, Chroma residual scale depends on corresponding luma block, and causes high latency of Chroma processing
This contribution proposes to use a single chroma scale factor per picture. Benefits are:
  No dependency on luma block; Able to be applied to dual tree (Intra slices) as well.
  Reduces complexity,
Results:
 | Apply to single tree (as in VTM5): | Also apply to Dual tree (Intra Slices)
AI |  | 0.06%, -0.62%, -0.75%
RA | -0.02%, -0.08%, -0.04% | 0.01%, -0.61%, -0.57%
LD | 0.00%, 0.16%, 0.07% | -0.02%, -0.36%, -0.34%

## Slide 3: Background
Chroma residual scaling depends on the average of corresponding luma block, which causes latency of CRS.
Due to the dependency, in VVC5, CRS is turned off for Intra slices (with dual tree). But even for Inter slice (with single tree), the latency is still high for large TUs.
Chroma residual scale factor is determined by:
  Compute avgY‘ in reshaped domain.
    If block is intra, compute average of predicted luma values;
    If block is inter, forward map the block to reshaped domain, then calculate the average.
  Determine the index of the piecewise linear model to which avgY' belongs in the inverse mapping.
  = cScaleInv[], which is the slope (in fixed point representation) of the piece in the inverse mapping. is a constant value for the entire chroma block.

## Slide 4: Proposed Method (Motivation)
Observations: For SDR sequences, the middle portion of LMCS forward mapping and inverse mapping are close to straight line.
Figure below shows actual LMCS mapping of MarketPlace. (16 bins, 17 pivot points, lmcs_min_bin_idx=1 and LmcsMaxBinIdx=14)

## Slide 5: Proposed method
Chroma scaling factor is inverse slope of a piece. Since slope variations among pieces are small, we propose to use a single chroma residual scaling factor for the entire picture.
  The single scale factor can be derived from the overall LMCS model. It only needs to be generated once when LMCS luma model is received.
Benefits of single chroma residual scale are no latency and low complexity
  Not depending on the corresponding luma block, therefore no latency.
  Can be applied to intra slices (dual tree) as well.
  The steps to map luma block and calculate avgY, and get piece index that avgY belongs can all be removed.
The single scale factor may be inferred at decoder or signalled from encoder.

## Slide 6: Infer Single Chroma Scaling Factor
The single chroma scaling factor can be inferred at the decoder based on linear mapping of the luma LMCS model.
In our test, we simply connect the pivot points at lmcs_min_bin_idx and (LmcsMaxBinIdx +1 ) with a straight line and derive the scaling factor from this linear line.
This linear line is equally divided into bins, and each bin has the same scale.

## Slide 7: Signal the Single Chroma scale factor
Alternatively, the scale factor may be signalled to decoder, It has more flexibility to adjust the luma and chroma bit allocation.
Can be signalled with similar syntax as existing LMCS model
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_delta_cw_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinIdx; i++ ) { | 
lmcs_delta_abs_cw[ i ] | u(v)
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 
lmcs_delta_abs_cw_linear | u(v)
if ( lmcs_delta_abs_cw_linear ) > 0 ) | 
lmcs_delta_sign_cw_linear_flag | u(1)
} | 

## Slide 8: Experimental Results
In all our tests, the single scale factor is derived from the linear line by connecting the pivot points at lmcs_min_bin_idx and (LmcsMaxBinIdx +1 )
Inferring or signaling the scale factor have same BD-rate result ( only difference are the signalling bits). So only one set of results is showing.
Two set of tests:
  Applying proposed to single tree only, i.e. Inter slices (as in VTM5)
  Applying proposed to both dual tree (Intra) and single tree (Inter) slices.

## Slide 9: Results of applying to single tree (as in VTM5)
No loss. Tiny gain in RA.
Result of Proposed CRS applying to single tree
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.20% | -0.05% | 101% | 101% |  |  |  |  | 
Class A2 | 0.01% | -0.22% | -0.27% | 100% | 101% |  |  |  |  | 
Class B | -0.01% | -0.08% | -0.03% | 100% | 101% | 0.02% | 0.13% | 0.08% | 100% | 101%
Class C | -0.05% | 0.11% | 0.13% | 100% | 101% | -0.02% | 0.24% | 0.42% | 99% | 100%
Class E |  |  |  |  |  | 0.00% | 0.09% | -0.40% | 99% | 100%
Overall | -0.02% | -0.08% | -0.04% | 100% | 101% | 0.00% | 0.16% | 0.07% | 100% | 100%
Class D | 0.01% | 0.17% | 0.25% | 100% | 100% | 0.02% | 0.11% | 1.35% | 99% | 99%
Class F | -0.01% | 0.20% | 0.16% | 101% | 101% | -0.08% | 0.18% | 0.16% | 100% | 100%

## Slide 10: Result of also applying to dual tree
In VTM5, CRS is disabled for Intra slices (dual tree)
Applying CRS to intra slices balances luma and chroma quality better.
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 CTC |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.20% | -0.28% | 101% | 101%
Class A2 | -0.09% | 0.67% | 0.81% | 101% | 102%
Class B | 0.06% | -0.51% | -0.63% | 100% | 102%
Class C | 0.16% | -1.27% | -1.44% | 98% | 97%
Class E | 0.17% | -1.61% | -2.09% | 99% | 98%
Overall | 0.06% | -0.62% | -0.75% | 100% | 100%
Class D | 0.07% | -0.40% | -0.65% | 99% | 97%
Class F | 0.28% | -1.32% | -1.46% | 99% | 99%

## Slide 11: Result of also applying to Dual tree
Applying CRS to intra slices improves Chroma quality.
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.20% | -0.05% | 100% | 101% |  |  |  |  | 
Class A2 | 0.01% | -0.22% | -0.27% | 100% | 101% |  |  |  |  | 
Class B | 0.00% | -0.50% | -0.40% | 100% | 101% | 0.01% | 0.23% | -0.21% | 100% | 101%
Class C | 0.02% | -1.35% | -1.39% | 100% | 99% | -0.03% | 0.19% | 0.43% | 99% | 101%
Class E |  |  |  |  |  | -0.05% | -2.09% | -1.60% | 100% | 102%
Overall | 0.01% | -0.61% | -0.57% | 100% | 101% | -0.02% | -0.36% | -0.34% | 100% | 101%
Class D | 0.03% | -0.78% | -0.86% | 100% | 100% | -0.04% | -0.03% | 1.13% | 99% | 98%
Class F | 0.18% | -1.13% | -1.12% | 100% | 100% | -0.01% | -0.36% | -0.34% | 101% | 102%

## Slide 12: Supplemental result on HDR PQ
For HDR PQ content, HDR CTC anchor has luma Delta QP on and LMCS off. It is suggested on CE2 to use LMCS on and LQP off as 2nd anchor.
The bit allocation between these two anchors are very different. Comparing to HDR CTC anchor, LMCS on has gain on luma while more losses on Chroma.
The loss on chroma is partially because Chroma residual scaling is disabled for intra slices.
VTM5 LMCS on (LQP off) vs. HDR Anchor (LQP on)
 | Over vtm5 HDR Anchor (LQP1 LMCS0) |  |  |  |  |  |  |  |  | 
 | All Intra: BD-rate |  |  |  |  | Random Access: BD-rate |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV
Average HDR-B | 8.08% | -2.06% | -1.64% | 14.15% | 8.34% | 6.26% | -1.79% | -1.60% | 14.12% | 6.85%

## Slide 13: Supplemental result on HDR PQ content: Applying to Single Tree
Top table is relative to CTC anchor (LQP=1 LMCS=0). Bottom table is relative to LMCS=1 , LQP=0
The proposed CRS makes the luma/chroma bit allocation a little bit closer to HDR PQ CTC anchor. With the flexibility of signalling CRS factor, encoder may use other CRS factor to adjust luma and chroma bit balance.
 | Over vtm5 HDR Anchor (LQP1 LMCS0) |  |  |  |  |  |  |  |  | 
 | All Intra: BD-rate |  |  |  |  | Random Access: BD-rate |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV
Average HDR-B |  |  |  |  |  | 5.88% | -1.72% | -1.52% | 12.27% | 4.01%
 | Over vtm5 HDR LMCS1 LQP0 |  |  |  |  |  |  |  |  | 
 | All Intra: BD-rate |  |  |  |  | Random Access: BD-rate |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV
Average HDR-B |  |  |  |  |  | -0.39% | 0.07% | 0.08% | -1.83% | -3.03%

## Slide 14: Supplemental result on HDR PQ content: Also Applying to Dual Tree
Top table is relative to CTC anchor (LQP=1 LMCS=0). Bottom table is relative to LMCS=1 , LQP=0
Enabling CRS for Intra slices has gain on chroma and makes the luma/chroma bit allocation closer to HDR PQ CTC anchor.
 | Over vtm5 HDR Anchor (LQP1 LMCS0) |  |  |  |  |  |  |  |  | 
 | All Intra: BD-rate |  |  |  |  | Random Access: BD-rate |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV
Average HDR-B | 5.42% | -1.61% | -1.14% | 7.02% | -0.97% | 3.59% | -1.40% | -1.20% | 5.74% | -3.51%
 | Over vtm5 HDR LMCS1 LQP0 |  |  |  |  |  |  |  |  | 
 | All Intra: BD-rate |  |  |  |  | Random Access: BD-rate |  |  |  | 
 | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV | DE100 | PSNRL100 | wPsnrY | wPsnrU | wPsnrV
Average HDR-B | -2.66% | 0.45% | 0.51% | -5.95% | -8.14% | -2.67% | 0.39% | 0.41% | -7.38% | -9.95%

## Slide 15: Conclusion
Proposed chroma residual scale with single scale factor removes the dependency on luma block. Therefore eliminates the latency problem. Allow CRS able to be applied to intra slices (dual tree) too.
Reduces complexity. the steps to map and get average of luma block, and to identify piece index can all be removed.
Better balance on luma, chroma, with even small gain.
 | Apply to single tree (as in VTM5): | Also apply to Dual tree (Intra Slices)
AI |  | 0.06%, -0.62%, -0.75%
RA | -0.02%, -0.08%, -0.04% | 0.01%, -0.61%, -0.57%
LD | 0.00%, 0.16%, 0.07% | -0.02%, -0.36%, -0.34%

## Slide 16: Conclusion
Suggest to adopt the proposed method to VVC text and software
  Single chroma scaling factor per picture (either inferred or signalled)
  Enabling CRS for intra slices (dual tree)
Thanks Dolby for Cross-checking (JEVT-O0745)!