## Slide 1: JVET-O0233: Linear LMCS
J. Zhao, S. Kim
LG ELECTRONICS

## Slide 2: Introduction
This contribution proposes a simplified version of LMCS for SDR, referred as linear LMCS, with only one linear piece between the start and end flat pieces.
Reduces the complexity of luma inverse mapping and chroma residual scaling. Remove dependency of chroma residual scaling on luma.
Results: only small loss, preserve most of the gain
AI | 0.05%, 0.93%, 1.05%
RA | 0.04%, -0.05%, -0.07%
LD | 0.11%, -0.16%, -0.29%

## Slide 3: Background
LMCS has two main components:
  In-loop mapping of the luma component based on adaptive piecewise linear models
  For the chroma components, luma-dependent chroma residual scaling is applied.
LMCS is represented as 16-piece PWL models. For bins before lmcs_min_bin_idx and after LmcsMaxBinIdx, the codeword is 0, so they are flat.
For each of the 16 bin, a scale factor and an inverse scale factor are derived. Inverse scale factor derivation requires up to 16 divisions.
  LmcsPivot[ 0 ] = 0; for( i = 0; i <= 15; i++ ) { …. InvScaleCoeff[ i ] = OrgCW * (1 << 11) / lmcsCW[ i ] }
Chroma residual scaling depends on corresponding luma block. This dependency causes latency in chroma processing.

## Slide 4: Motivations
Figure below shows actual LMCS mapping of MarketPlace 1st frame RA qp37. (16 bins, 17 pivot points, lmcs_min_bin_idx=1 and LmcsMaxBinIdx=14)
Observations: For many SDR sequences, the middle portion of LMCS mapping is close to straight line. Variations are small.

## Slide 5: Proposed method
Propose a simplified LMCS model for SDR with a linear line between LMCS beginning and end flat pieces.
The linear LMCS can be regarded as a special case of current 16-piece PWL LMCS model with all bins in the middle portion having the same codeword.

## Slide 6: Proposed method
Benefits:
There is only one scale and inverse scale for the non-flat region. So they only need to be calculated once. It reduces the number of divisions of calculating the inverse scale factor to only 1.
For chroma residual scaling, there is only one scale factor per picture, therefore it removes dependency on corresponding luma block, eliminates latency and reduces complexity. This has also been shown in our proposal JVET-O0232 “No-latency LMCS Chroma Residual Scaling for Single tree and Dual tree” as well.
Smaller signalling overhead, make it feasible to frequent update of LMCS model and potentially get more gains.

## Slide 7: Encoder decision linear mapping
Encoder decides the linear mapping.
  In our test, we mainly reused the existing LMCS encoder-side parameter estimation, and did a linear approximation to the PWL mapping determined by current LMCS encoder algorithm.
  The Linear mapping is determined by minimizing the weighted error between the straight connection and the PWL mapping. Weight is based on histogram.
  Pivot at lmcs_min_bin_idx is not changed, only adjusted the pivot at LmcsMaxBinIdx+1.

## Slide 8: Signal the linear LMCS
Linear LMCS is targeted to SDR content. It is not applied to HDR content. Indicated by flag
If the linear flag is true, only one set of lmcsCW[i] information is signaled. This saves the signalling overhead, and makes more frequent update of LMCS model feasible.
lmcs_data () { | Descriptor
lmcs_min_bin_idx | ue(v)
lmcs_delta_max_bin_idx | ue(v)
lmcs_is_linear_flag | u(1)
lmcs_delta_cw_linear_prec_minus1 | ue(v)
for ( i = lmcs_min_bin_idx; i <= LmcsMaxBinEnd; i++ ) { | 
lmcs_delta_abs_cw[ i ] | 
if ( lmcs_delta_abs_cw[ i ] ) > 0 ) | 
lmcs_delta_sign_cw_flag[ i ] | u(1)
} | 

## Slide 9: Experimental Results
SDR CTC
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 CTC |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 1.57% | 2.12% | 102% | 101%
Class A2 | -0.09% | 1.90% | 1.93% | 102% | 102%
Class B | 0.13% | 1.31% | 1.41% | 100% | 102%
Class C | 0.06% | -0.49% | -0.54% | 99% | 99%
Class E | 0.03% | 0.56% | 0.64% | 100% | 99%
Overall | 0.05% | 0.93% | 1.05% | 101% | 101%
Class D | 0.03% | -0.43% | -0.68% | 99% | 100%
Class F | 0.00% | 0.01% | 0.00% | 100% | 101%

## Slide 10: Results
Loss of linear LMCS is small. That means Code word variations among the pieces are not the main contributor to the gain of LMCS tool on SDR, the min and max indices and overall code word resulted in majority of the gain.
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.39% | 0.62% | 101% | 101% |  |  |  |  | 
Class A2 | -0.14% | 0.62% | 0.52% | 100% | 101% |  |  |  |  | 
Class B | 0.04% | -0.25% | -0.22% | 100% | 101% | 0.14% | 0.15% | -0.17% | 100% | 101%
Class C | 0.20% | -0.65% | -0.83% | 99% | 99% | 0.16% | -0.24% | -0.45% | 99% | 102%
Class E |  |  |  |  |  | -0.02% | -0.59% | -0.29% | 100% | 103%
Overall | 0.04% | -0.05% | -0.07% | 100% | 100% | 0.11% | -0.16% | -0.29% | 100% | 102%
Class D | 0.00% | 0.05% | 0.18% | 99% | 100% | 0.02% | -0.44% | 0.60% | 99% | 101%
Class F | 0.17% | -0.41% | -0.44% | 100% | 100% | 0.14% | 0.01% | 0.27% | 100% | 103%

## Slide 11: Conclusion
Proposed linear LMCS is a simplified version of LMCS, and achieves most of the gain of LMCS
Reduce complexity of inverse scaling and chroma residual scaling, remove dependency of Chroma residual scaling.
Smaller signaling overhead to make it feasible for more frequent update of LMCS.
Suggest to adopt the option of linear LMCS to VVC text and software
Thanks Inter Digital for Cross-checking!