## Slide 1: JVET-O0249 Merge Modes Signaling
Han Huang, Wei-Jung Chien, Vadim Seregin, and Marta Karczewicz (Qualcomm)
Chi-Wei Hsu, Yu-Wen Huang and Shawmin Lei (MediaTek)

## Slide 2: Outline
Proposal:
  Disable TPM if width or height is larger than 64
  Merge mode signaling modification: 3 groups
Benefits:
  Parsing simplification
  Text simplification
  Coding gain
    CTC: {-0.08%, -0.12%, -0.19%} in RA and {-0.06%, 0.09%, 0.02%} in LDB
    High QP: {-0.24%, -0.35%, -0.39%} in RA and {-0.38%, -0.55%, -0.65} in LDB

## Slide 3: Proposal
MMVD
Subblock merge
TPM
CIIP
subblock_merge_flag
regular_merge_flag
Regular merge
ciip_merge_flag
mmvd_merge_flag
Regular merge
MMVD
Subblock merge
CIIP
TPM
regular_merge_flag
mmvd_merge_flag
subblock_merge_flag
ciip_merge_flag
1. Disable TPM if width or height is larger than 64
2. Merge mode signaling modification

## Slide 4: Parsing simplification
syntax | present conditions
ciip_merge_flag | (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth < 128 && cbHeight < 128 && ( cbWidth * cbHeight ) >= 64) ¦¦ (sps_triangle_enabled_flag && slice_type = = B)
subblock_merge_flag | MaxNumSubblockMergeCand > 0 && cbWidth > 8 && cbHeight > 8 && ((sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth < 128 && cbHeight < 128) ¦¦ (sps_triangle_enabled_flag && slice_type = = B))
mmvd_merge_flag | sps_mmvd_enabled_flag && ( cbWidth * cbHeight ) >= 64 && ((MaxNumSubblockMergeCand > 0 && cbWidth > 8 && cbHeight > 8) ¦¦ ((sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth < 128 && cbHeight < 128) ¦¦ (sps_triangle_enabled_flag && slice_type = = B)))
regular_merge_flag | sps_mmvd_enabled_flag ¦¦ (( cbWidth * cbHeight ) >= 64 && ((MaxNumSubblockMergeCand > 0 && cbWidth > 8 && cbHeight > 8) ¦¦ ((sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth < 128 && cbHeight < 128) ¦¦ (sps_triangle_enabled_flag && slice_type = = B))))
syntax | present conditions
ciip_merge_flag | (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0) && sps_triangle_enabled_flag && slice_type = = B
subblock_merge_flag | MaxNumSubblockMergeCand > 0 && cbWidth > 8 && cbHeight > 8
mmvd_merge_flag | sps_mmvd_enabled_flag
regular_merge_flag | ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 && ((sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0) ¦¦ (sps_triangle_enabled_flag && slice_type = = B))

## Slide 5: Text simplification
regular_merge_flag[ x0 ][ y0 ] equal to 1 specifies that regular merge mode or merge mode with motion vector difference is used to generate the inter prediction parameters of the current coding unit. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered coding block relative to the top-left luma sample of the picture. regular_merge_flag[ x0 ][ y0 ] equal to 0 specifies that combined inter-picture merge and intra-picture prediction or triangular shape based motion compensation is used to generate the inter prediction paramters.
When regular_merge_flag[ x0 ][ y0 ] is not present, it is inferred to 1. as follows:
If all the following conditions are true, regular_merge_flag[ x0 ][ y0 ] is inferred to be equal to 1:
sps_mmvd_enabled_flag is equal to 0.
general_merge_flag[ x0 ][ y0 ] is equal to 1.
cbWidth*cbHeight is equal to 32.
Otherwise, regular_merge_flag[ x0 ][ y0 ] is inferred to be equal to 0.

## Slide 6: Text simplification
mmvd_merge_flag[ x0 ][ y0 ] equal to 1 specifies that merge mode with motion vector difference is used to generate the inter prediction parameters of the current coding unit. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered coding block relative to the top-left luma sample of the picture. mmvd_merge_flag[ x0 ][ y0 ] equal to 0 specifies that the regular merge mode is used to generate the inter prediction paramters.
When mmvd_merge_flag[ x0 ][ y0 ] is not present, it is inferred to be equal to 0.as follows:
If all the following conditions are true, mmvd_merge_flag[ x0 ][ y0 ] is inferred to be equal to 1:
sps_mmvd_enabled_flag is equal to 1.
general_merge_flag[ x0 ][ y0 ] is equal to 1.
cbWidth*cbHeight is equal to 32.
regular_merge_flag[ x0 ][ y0 ] is equal to 0.
Otherwise, mmvd_merge_flag[ x0 ][ y0 ] is inferred to be equal to 0.

## Slide 7: Text simplification
ciip_flag[ x0 ][ y0 ] specifies whether the combined inter-picture merge and intra-picture prediction is applied for the current coding unit. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered coding block relative to the top-left luma sample of the picture. The variable MergeTriangleFlag[ x0 ][ y0 ], which specifies whether triangular shape based motion compensation is used to generate the prediction samples of the current coding unit, when decoding a B slice is set equal to ciip_flag[ x0 ][ y0 ] ? 0 : 1.
When ciip_flag[ x0 ][ y0 ] is not present, it’s set equal to regular_merge_flag[ x0 ][ y0 ] ? 0 : (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0).
When ciip_flag[ x0 ][ y0 ] is equal to 1, the variable IntraPredModeY[ x ][ y ] with x = xCb..xCb + cbWidth − 1 and y = yCb..yCb + cbHeight − 1 is set to be equal to INTRA_PLANAR.
The variable MergeTriangleFlag[ x0 ][ y0 ], which specifies whether triangular shape based motion compensation is used to generate the prediction samples of the current coding unit, when decoding a B slice is derived as follows:
If all the following conditions are true, MergeTriangleFlag[ x0 ][ y0 ] is set equal to 1:
sps_triangle_enabled_flag is equal to 1.
slice_type is equal to B.
general_merge_flag[ x0 ][ y0 ] is equal to 1.
MaxNumTriangleMergeCand is greater than or equal to 2.
cbWidth * cbHeight is greater than or equal to 64.
regular_merge_flag[ x0 ][ y0 ] is equal to 0.
mmvd_merge_flag[ x0 ][ y0 ] is equal to 0.
merge_subblock_flag[ x0 ][ y0 ] is equal to 0.
ciip_flag[ x0 ][ y0 ] is equal to 0.
Otherwise, MergeTriangleFlag[ x0 ][ y0 ] is set equal to 0.

## Slide 8: Test results
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.31% | -0.14% | 105% | 104%
Class A2 | -0.09% | 0.00% | -0.16% | 98% | 100%
Class B | -0.05% | -0.12% | -0.29% | 101% | 103%
Class C | -0.07% | -0.07% | -0.10% | 98% | 98%
Class E |  |  |  |  | 
Overall | -0.08% | -0.12% | -0.19% | 100% | 101%
Class D | -0.01% | -0.08% | 0.17% | 102% | 102%
Class F | -0.02% | 0.06% | 0.08% | 101% | 105%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.04% | 0.10% | 0.26% | 98% | 105%
Class C | -0.02% | 0.09% | 0.14% | 99% | 100%
Class E | -0.15% | 0.07% | -0.54% | 96% | 112%
Overall | -0.06% | 0.09% | 0.02% | 98% | 105%
Class D | -0.11% | 0.01% | 0.99% | 100% | 103%
Class F | 0.03% | 0.31% | -0.71% | 102% | 104%
CTC
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.31% | -0.71% | -0.17% | 102% | 100%
Class A2 | -0.29% | -0.25% | -0.43% | 95% | 98%
Class B | -0.17% | -0.32% | -0.50% | 99% | 100%
Class C | -0.24% | -0.21% | -0.40% | 96% | 96%
Class E |  |  |  |  | 
Overall | -0.24% | -0.35% | -0.39% | 98% | 99%
Class D | -0.14% | -0.47% | -0.06% | 101% | 99%
Class F | -0.17% | -0.13% | -0.12% | 100% | 102%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18% | -0.46% | -0.09% | 96% | 103%
Class C | -0.34% | -0.30% | -0.78% | 97% | 101%
Class E | -0.77% | -1.02% | -1.44% | 94% | 113%
Overall | -0.38% | -0.55% | -0.65% | 96% | 105%
Class D | -0.71% | 0.32% | -0.36% | 100% | 103%
Class F | -0.04% | 0.17% | -0.60% | 98% | 103%
High QP {32, 37, 42, 47}

## Slide 9: Test results
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.15% | 0.06% | 104% | 103%
Class A2 | -0.03% | 0.12% | 0.02% | 98% | 100%
Class B | 0.00% | 0.03% | -0.03% | 100% | 102%
Class C | -0.01% | -0.04% | -0.04% | 97% | 98%
Class E |  |  |  |  | 
Overall | -0.02% | 0.00% | 0.00% | 100% | 101%
Class D | 0.00% | 0.00% | 0.00% | 106% | 112%
Class F | 0.02% | 0.02% | 0.03% | 100% | 103%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.19% | -0.03% | 97% | 104%
Class C | 0.04% | -0.10% | -0.07% | 99% | 99%
Class E | 0.07% | 0.11% | -0.26% | 97% | 107%
Overall | 0.03% | 0.07% | -0.10% | 98% | 103%
Class D | -0.01% | 0.02% | 0.11% | 106% | 113%
Class F | 0.03% | -0.25% | -0.23% | 99% | 104%
Modification 1 only: disable TPM if width or height larger than 64

## Slide 10
THANK YOU!