## Slide 1
JVET-O0258:Non-CE8: Adaptive single/dual tree with IBC simplification
Weijia Zhu, Jizheng Xu, Li Zhang

## Slide 2: Motivation
The dual tree coding structure is employed on intra slices in the design and enabled in the CTC.
Dual tree may not be always efficient compared with single tree coding structure, especially for 4:4:4 sequences.
  2x2 block level block vector checking and sample copying in the current chroma IBC design of intra slices introduce too much complexity for both hardware and software implementation.

## Slide 3: Proposed method
Propose :
  Adaptively switch between dual tree and single tree at CTU-level for I-slice.
    A slice level flag introduced to control whether to enable this method for I-slice.
    A flag is signalled at CTU level to indicate whether the single tree or dual tree is applied.
      Only signaled for I slices
  Disable chroma IBC when dual tree coding structure is used for a CTU.
Encoder optimization
  Use the percentage of matching blocks in the current slice to determine the slice level flag
    If the percentage is smaller than 20%, the slice level flag is determined as 0
  Use the percentage of matching blocks in the current CTU to determine whether the dual tree is enabled
    If the percentage is larger than 75%, the dual tree is disabled in the current CTU
  The MIP flag, MTS flag, RST index of dual tree are reused for the single tree coding.

## Slide 4: Simulation Results
The simulation is conducted followed the CE8 test condition
VTM5 is employed as the benchmark
4 sets of simulations are tested
  1) Test #1: Test conditions of 4:2:0 sequences in CE8.
    Anchor: VTM5 with dual tree enabled
    Tested: The proposed method
  2) Test #2: Test conditions of 4:2:0 sequences in CE8.
    Anchor: VTM5 with dual tree disabled.
    Tested: The proposed method
  3) Test #3: Test conditions of 4:4:4 sequences in CE8.
    Anchor: VTM5 with dual tree enabled
    Tested: The proposed method
  4) Test #4: Test conditions of 4:4:4 sequences in CE8.
    Anchor: VTM5 with dual tree disabled
    Tested: The proposed method

## Slide 5: Simulation Results-Cont.
Test #1
vs. VTM dualtree
 | AI |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | 0.00% | 0.05% | -0.09% | 106% | 95%
F | -0.01% | 0.90% | 1.44% | 126% | 100%
TGM | -1.31% | 0.42% | -0.79% | 143% | 98%
 | RA |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | 0.00% | 0.00% | -0.04% | 103% | 96%
F | -0.20% | 0.30% | 0.66% | 110% | 101%
TGM | -0.10% | 0.29% | -0.19% | 108% | 100%
 | LDB |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | 0.00% | 0.00% | -0.02% | 102% | 100%
F | 0.05% | -0.17% | -0.75% | 104% | 98%
TGM | -0.02% | 0.33% | -0.19% | 103% | 99%

## Slide 6: Simulation Results-Cont.
Test #2
vs. VTM singletree
 | AI |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | -0.41% | -10.81% | -11.34% | 65% | 102%
F | -0.80% | -4.80% | -6.22% | 89% | 101%
TGM | -0.54% | -1.63% | -1.83% | 105% | 99%
 | RA |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | -0.14% | -5.32% | -5.86% | 100% | 102%
F | -0.59% | -2.14% | -3.23% | 102% | 107%
TGM | -0.24% | -0.75% | -0.86% | 104% | 104%
 | LDB |  |  |  | 
 | Y | U | V | Enc | Dec
CTC | -0.08% | -2.32% | -3.32% | 101% | 104%
F | -0.08% | -0.44% | -1.03% | 102% | 104%
TGM | -0.03% | -0.21% | -0.31% | 103% | 103%

## Slide 7: Simulation Results-Cont.
Test #3, vs. VTM dualtree
AI | Y | U | V | EncT | DecT
TGM 1080p | -6.35% | -7.66% | -7.87% | 150% | 88%
TGM 720p | -3.33% | -3.67% | -3.20% | 161% | 99%
Animation | 0.17% | 0.20% | 0.21% | 102% | 102%
Mixed content | -1.75% | -1.72% | -1.66% | 160% | 95%
Camera-Captured content | 0.02% | -0.02% | -0.05% | 103% | 103%
Overall | -2.91% | -3.34% | -3.26% | 140% | 96%
RA | Y | U | V | EncT | DecT
TGM 1080p | -2.06% | -2.85% | -2.90% | 108% | 106%
TGM 720p | -2.34% | -2.52% | -2.36% | 114% | 111%
Animation | 0.08% | 0.15% | 0.13% | 103% | 107%
Mixed content | -1.24% | -1.63% | -1.33% | 112% | 104%
Camera-Captured content | -0.02% | -0.05% | 0.01% | 103% | 104%
Overall | -1.41% | -1.75% | -1.65% | 109% | 107%
LDB | Y | U | V | EncT | DecT
TGM 1080p | -0.32% | -0.60% | -0.64% | 105% | 101%
TGM 720p | -0.38% | -0.47% | -0.64% | 106% | 111%
Animation | 0.03% | 0.08% | -0.03% | 103% | 102%
Mixed content | -0.16% | 0.16% | 0.04% | 106% | 101%
Camera-Captured content | 0.01% | 0.08% | -0.17% | 104% | 103%
Overall | -0.21% | -0.23% | -0.36% | 105% | 104%

## Slide 8: Simulation Results-Cont.
Test #4, vs. VTM singletree
AI | Y | U | V | EncT | DecT
TGM 1080p | -0.17% | -0.02% | 0.01% | 101% | 102%
TGM 720p | -0.45% | -0.24% | -0.30% | 105% | 107%
Animation | 0.21% | 1.76% | 2.57% | 62% | 107%
Mixed content | -0.05% | -0.18% | 0.12% | 109% | 103%
Camera-Captured content | -1.58% | -2.43% | -2.64% | 57% | 106%
Overall | -0.36% | -0.19% | -0.06% | 90% | 105%
RA | Y | U | V | EncT | DecT
TGM 1080p | 0.00% | -0.03% | -0.06% | 104% | 106%
TGM 720p | -0.52% | 0.49% | 0.49% | 103% | 112%
Animation | -0.17% | 1.69% | 2.02% | 97% | 108%
Mixed content | -0.12% | -0.07% | 0.24% | 106% | 104%
Camera-Captured content | -1.57% | -1.62% | -1.96% | 98% | 105%
Overall | -0.39% | 0.12% | 0.17% | 102% | 107%
LDB | Y | U | V | EncT | DecT
TGM 1080p | 0.00% | 0.13% | 0.02% | 105% | 103%
TGM 720p | -0.04% | 0.28% | 0.22% | 104% | 112%
Animation | 0.02% | -0.51% | -0.26% | 102% | 103%
Mixed content | -0.10% | 0.40% | 0.28% | 107% | 101%
Camera-Captured content | -0.15% | -0.16% | -0.41% | 103% | 104%
Overall | -0.05% | 0.10% | 0.03% | 105% | 105%

## Slide 9: More info - disable dual-tree chroma IBC in VTM5.0
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
Class F | 0.05% | 0.21% | 0.40% | 101% | 105%
TGM | 1.77% | 2.51% | 2.83% | 101% | 100%
 | Random Access Main 10 |  |  |  | 
Class F | 0.09% | 0.58% | 0.49% | 102% | 107%
TGM | 0.65% | 0.97% | 0.95% | 102% | 104%
 | Low delay B Main10 |  |  |  | 
Class F | 0.01% | 0.12% | 0.06% | 103% | 104%
TGM | 0.06% | 0.11% | 0.22% | 100% | 104%

## Slide 10: Conclusions
Proposed a scheme of adaptive CTU-level dual tree
  Chroma IBC is totally removed in the dual tree
Recommend adopting the proposed scheme to the next version of VVC.