## Slide 1
AHG8: Adaptive Resolution Change (JVET-O0303)
Broadcom Inc.
Peisong Chen, Tim Hellman, Brian Heng, Wade Wan, Minhua Zhou

## Slide 2: Benefits of Adaptive Resolution Change
Seamlessly adapt video resolution to user preference and bandwidth variation.
Bit rate savings compared to inserting intra pictures.
There is no intra picture beating effect.

## Slide 3: Design Principle
Reuse existing motion compensation interpolators
Do not introduce new processing blocks
Do not need to pre-scale reference pictures in memory.
Transparent to other functional modules such as DPB management, motion vector predictor, deblocker, etc.

## Slide 4: Down Scale and Up Scale
Down scale ratio not larger than 2
Up scale ratio not less than 1/8
Ref 1
Ref 0
Current
down scale
up scale

## Slide 5: Flexible Scaling Design
Scaling factors is determined by picture sizes.
X/Y scaling factors are independent of each other.
Each block can use a different scaling factor.
When encoding motion vectors, they are normalized to the size of the current picture.
Instead of scaling the reference pictures to the resolution of the current picture, motion vectors are scaled during motion compensation.

## Slide 6: Reference Location Derivation
Scaling factors is determined by the picture sizes
Reference location mapping with motion vector scaling
Step Size
,
x_step = ( hori_scale_fp + 8) >> 4,
y_step = ( vert_scale_fp + 8) >> 4.

## Slide 7: Example
Horizontal scaling factor of 3:5
Vertical scaling factor of 1:2

## Slide 8: Interaction with Other Coding Tools
When slice_temporal_mvp_enabled_flag is equal to 1, the collocated picture used for temporal motion vector prediction shall have the same size as the present picture.
For a coding block of the current picture, if the size of the current picture is different from the size of List0 or List1 reference picture, BDOF and DMVR shall be turned off for that coding block.
For a coding block of the current picture using affine mode, if the size of the current picture is different from the size of List0 or List1 reference picture, the existing affine fallback mode shall be triggered for that coding block.

## Slide 9: Software
The current design has been implemented on top of VTM-5.0.
It supports resolution changes within the range of [1/8, 2].
Horizontal and vertical directions with different scaling ratios are supported.

## Slide 10: Some Coding Results

## Slide 11: Summary
Proposes a flexible scaling mechanism to support adaptive resolution change with the following characteristics:
  Reference picture scaling is realized implicitly in motion compensation interpolators
  No need to scale reference pictures in memory
  No new processing blocks

## Slide 12
Thanks InterDigital for cross-check

## Slide 13
Thank You