## Slide 1: JVET-O0313 CE4-related: On conditions for enabling PROF
Yu-Ciao Yang, Po-Han Lin
Gothenburg, SE
July 2019

## Slide 2: Introduction
In the current design of CE4-2.1 software, there are 2 conditions on PROF in decoder. If one of the following conditions is true, PROF is disabled.
  Condition 1: Control point motion vectors are all equal.
  Condition 2: The size of reference block bounding box exceed a pre-defined threshold.
If PROF is enabled, the following steps are applied:
  Step 1) Derive sample motion vector difference ΔV(i, j). ΔV(i, j) is rounded by the following equation before calculated prediction refinement, the shift is related to the position precision, affine parameter precision and ΔV precision.
  Step 2) Derive spatial gradient.
  Step 3) Derive prediction refinement and generate the final prediction.
ΔV is rounded to zero if abs( ΔV ) <= abs( 1<<( shift-1 ) )

## Slide 3: Proposed Condition
According to the characteristics of the affine model (rotate, zoom in, zoom out) of an affine sub-block, the maximum value of ΔV appears in the 4 corners in an affine sub-block.
The coordinate of 4 corners relative to the center of 4x4 fractional interpolation block are (-6, -6), (6, -6), (-6, 6), (6, 6), respectively. The ΔV of the 4 corners are list as follows.
To determine the maximum ΔV of the 4 corners, the 4 equations can be simplified as follows.
To decide whether to enable PROF, if the following condition is true, PROF is disabled.
  None of ΔmaxVx and ΔmaxVy is greater than abs( 1<<( shift-1 ) )

## Slide 4: Simulation results
Table 1 shows the probability of disabling PROF by conditions.
  Condition 1: Control point motion vectors are all equal.
  Condition 2: The size of reference block bounding box exceed a pre-defined threshold.
  Condition 3 (Proposed): None of ΔmaxVx and ΔmaxVy is greater than the rounding threshold.
Test 1: Apply Condition 3 on top of CE4-2.1.a and remove Condition 1.
Test 2: Apply Condition 3 on top of CE4-2.1.b and remove Condition 1.
 | Disabling Probability |  | 
 | Condition 1 | Condition 2 | Condition 3
CE4-2.1.a RA | 23.6598% | 0.5819% | 0.0000%
CE4-2.1.b RA | 25.1501% | 0.6250% | 0.0000%
Test 1 RA | 0.0000% | 0.5819% | 34.8713%
Test 2 RA | 0.0000% | 0.6156% | 33.8086%
CE4-2.1.a LB | 21.1411% | 0.6298% | 0.0000%
CE4-2.1.b LB | 21.7222% | 0.5716% | 0.0000%
Test 1 LB | 0.0000% | 0.6298% | 33.9609%
Test 2 LB | 0.0000% | 0.6154% | 30.3716%
Table 1. Probability of Disabling PROF of Affine Luma Blocks.

## Slide 5: Simulation results
 | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over CE4-2.1.a |  |  |  |  | Over CE4-2.1.a |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100% |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 99% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Summary of experimental results (Test 1 over CE4-2.1.a)
 | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over CE4-2.1.b |  |  |  |  | Over CE4-2.1.b |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | -0.03% | 100% | 100% |  |  |  |  | 
Class A2 | 0.00% | -0.08% | 0.05% | 100% | 100% |  |  |  |  | 
Class B | 0.00% | 0.02% | -0.04% | 100% | 100% | 0.03% | 0.01% | 0.06% | 100% | 99%
Class C | -0.02% | 0.02% | -0.02% | 100% | 100% | -0.03% | -0.18% | 0.30% | 100% | 100%
Class E |  |  |  |  |  | 0.06% | -0.47% | -0.62% | 100% | 99%
Overall | -0.01% | 0.00% | -0.02% | 100% | 100% | 0.02% | -0.17% | -0.03% | 100% | 99%
Class D | -0.01% | 0.01% | -0.01% | 100% | 100% | 0.03% | -0.44% | 0.28% | 100% | 99%
Class F | -0.01% | 0.03% | -0.04% | 100% | 100% | -0.02% | -0.01% | 0.37% | 100% | 99%
Summary of experimental results (Test 2 over CE4-2.1.b)

## Slide 6: Conclusion
This contribution proposes conditionally disabling PROF on the affine blocks which may not benefit of applying PROF.
  The condition can skip around 34% PROF process of affine mode without coding performance change on top of CE4-2.1.a
It is suggested to adopt this proposal into the next version of VVC Working Draft.
Thanks InterDigital for crosscheck

## Slide 7: Thank you!