## Slide 1: Non-CE3: Unification of intra interpolation filter selection
Jinho Lee
jinosoul@etri.re.kr
[JVET-O0341]

## Slide 2: Intra interpolation filter selection
MDIS condition for regular intra in VTM5
  Based on block size and intra prediction mode
    The variable nTbS = ( Log2(nTbW) + Log2(nTbH) ) >> 1.
    The variable minDistVerHor = Min( Abs( predModeIntra − 50 ), Abs( predModeIntra − 18 ) )
    If minDistVerHor > intraHorVerDistThres[ nTbS ], filterFlag = 1 (Gaussian) otherwise, filterFlag = 0 (cubic)
Interpolation filter selection based on MRL/ISP/Regular
  Different condition from MDIS condition in ISP
 | nTbS = 2 | nTbS = 3 | nTbS = 4 | nTbS = 5 | nTbS = 6 | nTbS = 7
intraHorVerDistThres[ nTbS ] | 16 | 14 | 2 | 0 | 0 | 0
Intra angular mode | MRL | ISP | Regular
Integer sample copy modes | Cubic (fractional sample position 0) |  | 
Other angular modes | Cubic | Cubic (Mode ≥ 34 && W ≤ 8) or (Mode < 34 && H ≤ 8) | Cubic or Gaussian (MDIS condition)
 |  | Gaussian (otherwise) | 

## Slide 3: Unification of filter selection
Method1
  Remove condition for ISP
  Unification with regular
Intra prediction mode | MRL | Regular/ISP
Integer sample copy modes | Cubic (fractional sample position 0) | 
Other angular modes | Cubic | Cubic or Gaussian (MDIS condition)
Intra prediction mode | MRL/ISP | Regular
Integer sample copy modes | Cubic (fractional sample position 0) | 
Other angular modes | Cubic | Cubic or Gaussian (MDIS condition)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | -0.04% | 100% | 100%
Class A2 | 0.00% | -0.07% | -0.03% | 99% | 100%
Class B | 0.00% | -0.06% | 0.02% | 100% | 100%
Class C | 0.01% | -0.09% | 0.11% | 100% | 100%
Class E | 0.00% | -0.06% | -0.09% | 100% | 100%
Overall | 0.00% | -0.06% | 0.00% | 100% | 100%
Class D | 0.01% | 0.06% | -0.03% | 99% | 100%
Class F | 0.01% | 0.07% | 0.09% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.21% | 0.08% | 100% | 100%
Class A2 | 0.02% | 0.09% | 0.01% | 100% | 100%
Class B | 0.02% | -0.04% | -0.20% | 100% | 100%
Class C | -0.02% | -0.20% | -0.10% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | -0.09% | -0.08% | 100% | 100%
Class D | 0.03% | -0.07% | 0.16% | 100% | 100%
Class F | 0.00% | 0.01% | 0.09% | 100% | 100%
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.04% | 0.04% | 100% | 100%
Class A2 | 0.00% | -0.01% | 0.00% | 99% | 100%
Class B | 0.00% | -0.06% | 0.01% | 100% | 100%
Class C | 0.00% | 0.00% | 0.03% | 100% | 100%
Class E | -0.01% | 0.00% | -0.06% | 100% | 100%
Overall | 0.00% | -0.01% | 0.01% | 100% | 100%
Class D | 0.01% | 0.08% | 0.01% | 100% | 100%
Class F | -0.01% | -0.02% | -0.03% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.04% | 0.13% | 100% | 100%
Class A2 | 0.00% | -0.06% | 0.06% | 100% | 100%
Class B | 0.02% | -0.01% | -0.09% | 100% | 100%
Class C | -0.02% | -0.23% | -0.19% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | -0.09% | -0.04% | 100% | 100%
Class D | 0.07% | -0.07% | 0.17% | 101% | 100%
Class F | 0.00% | 0.17% | 0.11% | 101% | 100%
Method2
  Remove condition for ISP
  Unification with MRL

## Slide 4: Conclusions
Experimental results
Unification methods of intra interpolation filter selection are proposed to reduce complexity without loss
Suggest to adopt in VTM6
Thank InterDigital for cross-check
Proposal |  | Y | U | V | EncT | DecT
M1 (Unification with regular) | AI | 0.00% | -0.06% | 0.00% | 100% | 100%
 | RA | 0.00% | -0.09% | -0.08% | 100% | 100%
M2 (Unification with MRL) | AI | 0.00% | -0.01% | 0.01% | 100% | 100%
 | RA | 0.01% | -0.09% | -0.04% | 100% | 100%