## Slide 1: JVET-O0345: Non-CE3: MIP simplification
Chang-Hao Yau, Ching-Chieh Lin, Chun-Lung Lin
Gothenburg, SE
Jul 2019

## Slide 2: Introduction
There are three stages in the current MIP.
  Downsampling
  Matrix-vector multiplication
  Upsampling

## Slide 3: Observation 1
The size for storing MIP parameters is large
  Total 7.92 Kilobyte
    S0 for 4x4 block
    S1 for 4x8, 8x4 and 8x8 blocks
    S2 for the rest blocks
Sets | Numbers of parameters | Memory size (Kilobyte) | Percentage
S0 | 1440 | 1.80 | 22.73
S1 | 1440 | 1.80 | 22.73
S2 | 3456 | 4.32 | 54.55
Total | 6336 | 7.92 | 

## Slide 4: Proposed Method 1
Removal of MIP on 4X4 block
  Save 22.73% storage
  0.02% luma loss
  0.02% and 0.01% chroma gain
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.04% | -0.01% | 100% | 100%
Class A2 | 0.00% | 0.01% | -0.01% | 99% | 100%
Class B | 0.01% | 0.00% | 0.04% | 100% | 100%
Class C | 0.06% | 0.02% | -0.01% | 100% | 100%
Class E | 0.03% | -0.10% | -0.08% | 100% | 100%
Overall | 0.02% | -0.02% | -0.01% | 100% | 100%
Class D | 0.11% | 0.25% | 0.00% | 100% | 99%
Class F (optional) | 0.04% | 0.04% | 0.21% | 99% | 100%

## Slide 5: Observation 2
The top and left boundary of the block have different downsampling processes.
  One of the boundaries needs to downsample twice for S2
An example of MIP processing for a 16X16 block in the current design

## Slide 6: Proposed Method 2
Unification of the downsampling process
  The reference samples for upsampling use the original reference samples.
  The reference samples for matrix-vector multiplication are using the outputs of one-step downsampling processes.
An example of MIP processing for a 16X16 block in the proposed method 2

## Slide 7: Results of Method 2
0.01% luma gain
0.09% chroma gain
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.11% | -0.07% | 100% | 95%
Class A2 | -0.01% | -0.09% | -0.11% | 100% | 98%
Class B | -0.02% | -0.08% | 0.03% | 101% | 96%
Class C | 0.00% | -0.08% | 0.10% | 100% | 97%
Class E | -0.01% | -0.07% | -0.03% | 101% | 96%
Overall | -0.01% | -0.09% | 0.00% | 101% | 96%
Class D | 0.01% | 0.12% | -0.20% | 102% | 101%
Class F (optional) | 0.00% | 0.05% | 0.04% | 101% | 97%

## Slide 8: Combination of Method 1 + Method 2
Without luma change of BD-rate
0.07% and 0.05% chroma gain
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.08% | -0.07% | 99% | 100%
Class A2 | -0.02% | -0.10% | -0.05% | 99% | 100%
Class B | -0.01% | -0.08% | -0.10% | 99% | 100%
Class C | 0.05% | -0.05% | 0.03% | 99% | 100%
Class E | 0.01% | -0.03% | -0.06% | 99% | 100%
Overall | 0.00% | -0.07% | -0.05% | 99% | 100%
Class D | 0.12% | 0.14% | 0.15% | 99% | 100%
Class F (optional) | 0.02% | 0.09% | 0.20% | 99% | 100%

## Slide 9: Conclusions
Two methods are proposed for MIP simplification
  Method 1: removal of MIP on 4X4 block
    Save 22.73% storage
    0.02% luma loss, 0.02% and 0.01% chroma gain
  Method 2: unification of the downsampling process
    Use one-step downsampling and reduce the number of conditional checks
    0.01% luma gain, 0.09% and 0.00% chroma gain
  Combination of method 1 and 2
    0.00% luma gain, 0.07% and 0.05% chroma gain
It is recommended to adopt the proposed methods into VTM 6.0.
Thanks MediaTek for cross-checking

## Slide 10: Thank You