## Slide 1
CE6-related: LFNST with one mode
JVET-O0350

## Slide 2: JVET-O0350 / LFNST with one mode
LFNST maps each intra prediction mode to one of four classes
Each class has two alternative transforms
  Encoder selects which one to use (if LFNST is active for the CU)
  1 bit flag signaled in the bitstream
Proposal
  Don’t send the flag, but alternate the transform selection for consecutive intra prediction modes
  “Hides” the flag in the parity of the intra prediction mode
Introduction

## Slide 3: JVET-O0350 / LFNST with one mode
8.7.4.3 Low frequency non-separable transformation matrix derivation process
Inputs to this process are:
a variable nTrS specifying the transform output length,
a variable predModeIntra specifying the intra prediction mode for LFNST set selection,
a variable lfnstIdx specifying the LFNST index for transform selection in the selected LFNST set.
The variable lfnstIdx specifying the LFNST index for transform selection in the selected LFNST set is specified as follows:
lfnstIdx = predModeIntra % 2
Effective specification change

## Slide 4: JVET-O0350 / LFNST with one mode
Simulation results
 |  |  | AI Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10 % | 0.79 % | 0.87 % | 83 % | 99 %
Class A2 | 0.03 % | 0.56 % | 0.56 % | 82 % | 100 %
Class B | 0.08 % | 0.76 % | 0.95 % | 83 % | 101 %
Class C | 0.09 % | 0.62 % | 0.85 % | 83 % | 99 %
Class E | 0.10 % | 0.71 % | 0.75 % | 85 % | 98 %
Overall | 0.08 % | 0.69 % | 0.82 % | 83 % | 99 %
Class D | 0.02 % | 0.75 % | 0.60 % | 84 % | 98 %
Class F | 0.06 % | 0.49 % | 0.42 % | 90 % | 97 %
 |  |  | RA Main10 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.17 % | 0.36 % | 0.57 % | 95 % | 100 %
Class A2 | 0.07 % | 0.31 % | 0.40 % | 96 % | 99 %
Class B | 0.06 % | 0.70 % | 0.67 % | 95 % | 101 %
Class C | 0.04 % | 0.49 % | 0.29 % | 95 % | 101 %
Class E |  |  |  |  | 
Overall | 0.08 % | 0.50 % | 0.49 % | 95 % | 100 %
Class D | 0.04 % | 0.56 % | 0.62 % | 95 % | 100 %
Class F | 0.04 % | 0.46 % | 0.39 % | 95 % | 101 %