## Slide 1
JVET-O0363
Context Reduction for intra MPM related syntax element
Hikvision
Liying Xu, Xiaoqiang Cao, Fangdong Chen, Li Wang
Notes: Hi, everyone. I amd Xu Liying from hikvision. Here, I’d like to introduce you a method to construct merge candidate list under P configuration for merge mode under the configuration of P slice.

## Slide 2: Outline
Introduction
Proposed Method
Experimental Results
Conclusion
Notes: The PPT would be shown from four aspects. Firstly, introduction. Then, proposed method. Thirdly, experimental results. At last, conclusion.

## Slide 3: Introduction
The syntax intra_luma_not_planar_flag represents if the intra prediction mode is Planar or not.
In the current scheme, intra_luma_not_planar_flag is coded by CABAC with two contexts depending on the coding mode.
Syntax element | Bin Idx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
intra_luma_not_planar_flag[ ][ ] | intra_subpartitions_mode_flag | na | na | na | na | na

## Slide 4: Proposed
Method1
  In the proposed scheme, intra_luma_not_planar_flag is coded by CABAC with one context.
Method2
  In the proposed scheme, intra_luma_not_planar_flag is coded by Bypass.
Syntax element | Bin Idx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
intra_luma_not_planar_flag[ ][ ] | 0 | na | na | na | na | na
Syntax element | Bin Idx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
intra_luma_not_planar_flag[ ][ ] | bypass | na | na | na | na | na

## Slide 5: Experimental Results
Results for Proposed Method1 VS VTM 5.0
Thank Sharp for the crosscheck.

## Slide 6: Experimental Results
Results for Proposed Method2 VS VTM 5.0
Thank Sharp for the crosscheck.

## Slide 7: Conclusion
This contribution proposes to reduce the number of CABAC contexts.
The modification almost has no impact on the coding efficiency, it is recommendable to be adopted in the next version of VTM.

## Slide 8
Thank you！