## Slide 1
JVET-O0371
On 1xN and 2xN sub-partitions in ISP
Hikvision
Yucheng Sun, Liying Xu, Xiaoqiang Cao
Notes: Hi, everyone. I amd Xu Liying from hikvision. Here, I’d like to introduce you a method to construct merge candidate list under P configuration for merge mode under the configuration of P slice.

## Slide 2: Outline
Introduction
Proposed Method
Experimental Results
Conclusion
Notes: The PPT would be shown from four aspects. Firstly, introduction. Then, proposed method. Thirdly, experimental results. At last, conclusion.

## Slide 3: Background
When applying vertical split in ISP mode, 4xN coding block will be partitioned into 4 1xN sub-blocks and 8xN coding block will be partitioned into 4 2xN sub-blocks, which requires additional buffering for storage and make the transform part more complex.

## Slide 4: Proposed
Method1
  In this part, prediction is processed at least with 4 pixels in a width step for 4xN and 8xN. Besides, 2xN is removed which is replaced by 1xN using more partition.
Coding block sizes | ISP Vertical split | 
 | Prediction region sizes | Transform sizes
4xN (N ≥ 8) | 4xN | 1xN
8xN (N ≥ 4) | 4xN | 1xN

## Slide 5: Proposed
Transform part modification
1D column inverse transform
Shift1
1D row inverse transform
Shift2
Regular transform
1D column inverse transform
Shift3
ISP 1xN transform (parallel)

## Slide 6: Proposed
Method2
  In this part, prediction is processed as a whole block for 4xN and 8xN. Besides, 2xN is removed which is replaced by 1xN using more partition.
Coding block sizes | ISP Vertical split | 
 | Prediction region sizes | Transform sizes
4xN (N ≥ 8) | 4xN | 1xN
8xN (N ≥4) | 8xN | 1xN

## Slide 7: Experimental Results
Results for Proposed Method1 VS VTM 5.0
Thank Kwai for the crosscheck.

## Slide 8: Experimental Results
Results for Proposed Method2 VS VTM 5.0
Thank Kwai for the crosscheck.

## Slide 9: Conclusion
This contribution proposes address the issue that caused by 1xN and 2xN sub-partition.
For intra prediction part, we apply intra prediction on the whole ISP block or half block, just the same as regular intra block or large ISP block.
For transform part, we apply half transform (only horizon transform) instead regular 2D transform, which generally save half the cycles in transform processing.

## Slide 10
Thank you！