## Slide 1: JVET-O0372: A Simplification for MTS Index Signaling
Alican Nalci, Hilmi E. Egilmez, Amir Said,
Muhammed Coban, Vadim Seregin and Marta Karczewicz
  Qualcomm Inc.
Date: 7/5/19
Gothenburg, SE

## Slide 2: Multiple Transform Selection (MTS)
MTS (or primary transform) is used for residual coding (intra/inter blocks).
In VTM-5.0, MTS index is context coded:
Bin index “0” corresponds to a selection of DCT-2 (applied both horizontally and vertically).
This bin is encoded based on the CU-level quad tree depth (5 contexts).
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
tu_mts_idx[ ][ ] | cqtDepth (5 contexts) | 6 | 7 | 8 | na | na

## Slide 3
Remove the quad-tree depth dependency when signaling the MTS index.
In this case, whether a DCT-2 or an alternative transform applied is context coded with the same context index of ‘0’ regardless of the quad-tree depth.
Proposal: Remove CU Level Quad-Tree Depth Dependency
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
tu_mts_idx[ ][ ] | cqtDepth (5 contexts) 0 | 6 | 7 | 8 | na | na

## Slide 4
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.04% | 0.03% | 100% | 102%
Class A2 | 0.00% | -0.05% | -0.04% | 102% | 106%
Class B | 0.00% | -0.05% | 0.01% | 101% | 100%
Class C | 0.00% | -0.11% | -0.03% | 101% | 101%
Class E | -0.01% | -0.04% | -0.05% | 101% | 103%
Overall | 0.00% | -0.06% | -0.01% | 101% | 102%
Class D | 0.00% | 0.05% | -0.12% | 100% | 98%
Class F | -0.01% | 0.02% | 0.06% | 100% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.15% | 0.11% | 102% | 103%
Class A2 | 0.01% | -0.05% | -0.07% | 98% | 99%
Class B | 0.00% | 0.06% | -0.11% | 100% | 102%
Class C | -0.04% | -0.36% | -0.08% | 99% | 97%
Class E |  |  |  |  | 
Overall | -0.01% | -0.12% | -0.05% | 100% | 100%
Class D | -0.05% | 0.19% | -0.07% | 100% | 102%
Class F | -0.05% | 0.13% | -0.06% | 98% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.04% | 0.14% | 99% | 98%
Class C | 0.04% | -0.01% | 0.05% | 99% | 94%
Class E | 0.01% | -0.20% | 0.56% | 100% | 97%
Overall | 0.02% | -0.04% | 0.22% | 100% | 96%
Class D | 0.04% | -0.07% | 0.09% | 101% | 99%
Class F | -0.06% | -0.11% | 0.40% | 96% | 95%
Results: Over VTM-5.0 under CTC conditions

## Slide 5
In this contribution, a simplification for MTS index signaling is proposed.
This approach removes the CU level quad-tree depth dependency for MTS index coding.
Also reduces the number of MTS contexts by 5.
Thanks to Samsung for crosscheck.
Conclusion