## Slide 1
JVET-O0377
Context Reduction for CCLM related Syntax Element
Hikvision
Liying Xu, Xiaoqiang Cao, Fangdong Chen, Li Wang
Notes: Hi, everyone. I amd Xu Liying from hikvision. Here, I’d like to introduce you a method to construct merge candidate list under P configuration for merge mode under the configuration of P slice.

## Slide 2: Outline
Introduction
Proposed Method
Experimental Results
Conclusion
Notes: The PPT would be shown from four aspects. Firstly, introduction. Then, proposed method. Thirdly, experimental results. At last, conclusion.

## Slide 3: Background
The syntax intra_chroma_pred_mode represents the chroma pred mode.
In the current scheme, intra_chroma_pred_mode is coded as the following table.
Syntax element | Bin Idx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 0 | 0 | bypass | bypass | na | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 0 | 0 | 1 | 2 | bypass | bypass | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 1 | 0 | 1 | 2 | 2 | na | na

## Slide 4: Proposed
Method1
  In the proposed scheme, intra_chroma_pred_mode is coded as the following Table. The third and forth bin is coded by bypass.
Syntax element | Bin Idx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 0 | 0 | bypass | bypass | na | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 0 | 0 | 1 | bypass | bypass | bypass | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 1 | 0 | 1 | bypass | bypass | na | na

## Slide 5: Experimental Results
Results for Proposed Method1 VS VTM 5.0
Thank Sharp for the crosscheck.

## Slide 6: Conclusion
This contribution proposes to reduce the number of CABAC contexts.
The modifications almost have no impact on the coding efficiency, it is recommendable to be adopted in the next version of VTM.

## Slide 7
Thank you！