## Slide 1: JVET-O0389 On Supporting 64x64 Chroma Transform Unit
Fujitsu
15th JVET meeting, Gothenburg, 2019/7/3-12
Notes: p0.
それではよろしくお願いします。
活動報告と題しまして江崎が発表します。

## Slide 2: Background
The adoption of N0671 brought the 64x64 transform for chroma for 4:4:4 and 4:2:2 case.
In VTM-5.0, the maximum luma TU size is 64×64 and the maximum chroma TU size is 32×32 for 4:2:0 case.
A 128x128 inter CU in 4:2:0 format will be tiled with four 64x64 luma TUs and four 32x32 chroma TUs for Cb and Cr respectively.
Usually, for large block-size CU, large block-size transforms with high-frequency coefficients zero-out brings benefit on coding efficiency.

## Slide 3: Proposed method
In P and B slices, maximum transform TB for both luma and chroma is up to 64x64.
  For large block-size CUs( >= 128x128), maximum transform TB for both luma and chroma is 64x64.
  For the other size CUs( < 128x128), maximum transform TB for luma is 64x64; maximum transform TB for chroma is 32x32.
128x128
64x64
Luma CU
Chroma CUs
64x64
64x64
64x64
64x64
Luma TUs
64x64
Chroma TUs
64x64
64x64
128x64
64x32
Luma CU
Chroma CUs
64x64
64x64
Luma TUs
Chroma TUs
64x32
Four 32x32
64x128
32x64
Luma CU
Chroma CUs
64x64
64x64
Luma TUs
Chroma TUs
64x64
Four 32x32
CU >= 128x128
CU < 128x128

## Slide 4: Transform core
The transform process for 64x64 chroma TUs is exactly same as that for luma TUs.

## Slide 5: Possible Data processing order
for a 128x128 CU
    Processing order
Transform core and internal buffer can be shared between luma and chroma TU.
  No dependency between luma and chroma for inter CU.
Y0
Y1
Y2
Y3
Luma TUs
Cb
Chroma TUs
Cr
Y0
Cb
Cr
Y1
Y2
Y3
Y0
Cb
Cr
Y1
Y2
Y3
Y0
Cb
Cr
Y1
Y2
Y3
Y0
Cb
Cr
Y1
Y2
Y3
128x128 CU
Case 0
Case 1
Case 2
Case 3

## Slide 6: Simulation Results
Test condition on top of VTM5.0:
  maximum transform TB 64x64 for both luma and chroma is supported for 128x128 CUs in P and B slices
  Processing order : Case 0
    Y0->Cb->Cr->Y1->Y2->Y3
  Results from cross-checker （JVET-O0704）
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 102%
Class A2 | 0.00% | 0.00% | 0.00% | 101% | 101%
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 101% | 101%
Class E | 0.00% | 0.00% | 0.00% | 101% | 101%
Overall | 0.00% | 0.00% | 0.00% | 101% | 101%
Class D | 0.00% | 0.00% | 0.00% | 101% | 107%
Class F | 0.00% | 0.00% | 0.00% | 100% | 101%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.51% | -0.35% | 100% | 100%
Class A2 | 0.02% | -0.14% | -0.02% | 100% | 100%
Class B | 0.01% | -0.14% | -0.22% | 100% | 100%
Class C | -0.01% | -0.04% | -0.01% | 101% | 103%
Class E |  |  |  |  | 
Overall | 0.00% | -0.19% | -0.15% | 100% | 101%
Class D | 0.00% | 0.00% | 0.00% | 101% | 104%
Class F | 0.01% | -0.01% | -0.06% | 101% | 104%

## Slide 7: Conclusion
The maximum transform unit size of chroma components up to 64x64 is supported for 128x128 inter CU.
0.2% coding gain on chroma.
Transform core and buffer are shared between Luma and chroma.
This idea can be applied on other large block size inter CU or even intra CU (separate chroma tree) to keep the restriction of maximum TB for Luma and chroma in 4:4:4, 4:2:2 and 4:2:0 identical.
Suggest to adopt this proposal and as a start point of continue study on other cases.
Thank Tencent for crosschecking.

## Slide 8
Notes: 以上で発表を終わります。
ご清聴ありがとうございました。