## Slide 1
CE3-related: Sampling point extension for CCLM(JVET-O0412)
T. Tsukuba, Y. Yagasaki, M. Ikeda, T. Suzuki

## Slide 2: Summary
We propose to increase CCLM sampling points from 4 to 8 for large blocks
While keeping the worst-case as VTM5, it provides coding gains
-0.11% / -0.56% / -0.58% at AI and -0.07% / -0.53% / -0.56% at RA
VTM5
Proposal

## Slide 3: Introduction: CCLM at VTM5
VTM5 adopt new CCLM algorithm. It reduces complexity by limiting at most 4 neighbouring chroma samples and their corresponding down-sampled luma samples as figure 1. With these 4 points, estimation equation Y = α x + β are derived as figure 2.
Figure 1: Sampling points for the CCLM in VTM5
Figure 2: α, β derivation in VTM5

## Slide 4: Proposal Overview
Since larger blocks have more processing time than smaller ones, we propose to increase neighbouring chroma samples and their corresponding down-sampled luma samples for larger blocks as figure 3.
Figure 3: Illustration of the proposed sampling points for larger blocks

## Slide 5: Complexity Study 1
Number of operations of “α & β derivation process” based on number of sample points per block
Sample points per block | # of Swap (A) | # of Add & Shift (B) | Total (A)+(B)
4 | 4 | 12 | 16
6 | 11 | 12 | 23
8 | 16 | 12 | 28
10 | 23 | 12 | 35
12 | 30 | 12 | 42
16 | 40 | 12 | 52

## Slide 6: Complexity Study 2
Total number of operations at 64x64 region coded with one block size
Luma Block size | # of sampling points per block | # of operations (A) | # of blocks in 64x64 region (B) | Total # of operations (A) * (B)
4x4 | 4 | 16 | 256 | 4096
8x8 | 4 | 16 | 64 | 1024
 | 8 | 28 | 64 | 1792
16x16 | 4 | 16 | 16 | 256
 | 8 | 28 | 16 | 448
 | 16 | 52 | 16 | 832
32x32 | 4 | 16 | 4 | 64
 | 8 | 28 | 4 | 112
 | 16 | 52 | 4 | 208
64x64 | 4 | 16 | 1 | 16
 | 8 | 28 | 1 | 28
 | 16 | 52 | 1 | 52

## Slide 7: Combination of blocks with 4 points, 8points and 16 points
We select several combinations of “number of points” and “block size” while keeping the worst-case, i.e., luma 4x4 block has at most 4 points for all combination from A to E.
Combination | Luma 4x4 | Luma 8x8 | Luma 16x16 | Luma 32x32 | Luma 64x64
VTM5.0 | 4 points | 4 points | 4 points | 4 points | 4 points
A | 4 | 4 | 4 | 8 | 8
B | 4 | 4 | 4 | 8 | 16
C | 4 | 4 | 8 | 8 | 8
D | 4 | 4 | 8 | 8 | 16
E | 4 | 8 | 8 | 8 | 8

## Slide 8: β derivation in CE3-1.1
In VTM5 and are derived as figure above
The CE3-3.1 is derived using both luma and chroma averaged values (xC, yC) as shown above.
VTM5
We test β derivation methods in VTM5 and CE3-1.1.
(α derivation remains same as VTM5)

## Slide 9: Experimental results for several options
Combination tested | Luma 4x4 | Luma 8x8 | Luma 16x16 | Luma 32x32 | Luma 64x64 | Y | Cb | Cr
VTM5.0 | 4 | 4 | 4 | 4 | 4 | 0.00% | 0.00% | 0.00%
A | 4 | 4 | 4 | 8 | 8 | -0.05% | -0.25% | -0.25%
B | 4 | 4 | 4 | 8 | 16 | -0.05% | -0.23% | -0.20%
C | 4 | 4 | 8 | 8 | 8 | -0.06% | -0.34% | -0.32%
D | 4 | 4 | 8 | 8 | 16 | -0.05% | -0.33% | -0.29%
E | 4 | 8 | 8 | 8 | 8 | -0.06% | -0.42% | -0.42%
BD-Rate of AI for several combinations of sampling point extension &
β derivation in VTM5

## Slide 10: Experimental results for several options
Combination tested | Luma 4x4 | Luma 8x8 | Luma 16x16 | Luma 32x32 | Luma 64x64 | Y | Cb | Cr
VTM5.0 | 4 | 4 | 4 | 4 | 4 | 0.00% | 0.00% | 0.00%
A + CE3 β | 4 | 4 | 4 | 8 | 8 | -0.09% | -0.33% | -0.31%
B + CE3 β | 4 | 4 | 4 | 8 | 16 | -0.09% | -0.30% | -0.29%
C + CE3 β | 4 | 4 | 8 | 8 | 8 | -0.11% | -0.50% | -0.48%
D + CE3 β | 4 | 4 | 8 | 8 | 16 | -0.11% | -0.46% | -0.47%
E + CE3 β | 4 | 8 | 8 | 8 | 8 | -0.11% | -0.56% | -0.58%
BD-Rate of AI for several combinations with sampling point extension &
β derivation in CE3-3.1

## Slide 11: E+ CE3 β BD-Rate of AI
E+ CE3 β BD-Rate of AI

## Slide 12: E+ CE3 β BD-Rate of AI (Cross check results from ETRI)
E+ CE3 β BD-Rate of AI (ETRI)

## Slide 13: E+ CE3 β BD-Rate of RA
E+ CE3 β BD-Rate of RA

## Slide 14: E+ CE3 β BD-Rate of RA (Cross check results from ETRI)
E+ CE3 β BD-Rate of RA (ETRI)

## Slide 15: Conclusion
This proposal presents sampling point extension for CCLM.
While keeping the worst-case as VTM5.0, the sampling point extension provides coding gains.
We think coding gain vs. additional cost is reasonable. So, we recommend considering that the proposed extension is included into next version of test model.
Thanks ETRI for cross checking!

## Slide 17: D+ CE3 β BD-Rate of AI
D+ CE3 β BD-Rate of AI

## Slide 18: C+ CE3 β BD-Rate of AI
C+ CE3 β BD-Rate of AI