## Slide 1: JVET-O0414 Non-CE4 : Symmetric-MVD control considering the reference picture type
N. Park, H. Jang, J. Nam, J. Lim, S. Kim

## Slide 2: Introduction
Symmetric-MVD (SMVD)
  Allows to derive L1_MVD from L0_MVD without signaling of the L1_MVD
  L1_MVD is set to mirrored L0_MVD (without scaling operation)
  Precisely derived when both reference pictures are similar and the movement is constant in certain direction
When mixed STRP and LTRP are used for derivation.
MVD of the reference list 0
MVD of the reference list 1
Current picture
L0 reference picture
(LTRP)
L1 reference picture
(STRP)
L0_MVD
L1_MVD = -L0_MVD

## Slide 3: Proposed methods
To enhance the accuracy of the MVD, two schemes are proposed considering the reference picture type
  Method I: SMVD process is restricted when the current picture has mixed reference picture type
  Method II : SMVD process is more restricted where the SMVD is not allowed when the current picture refers to LTRP
 |  | SMVD |  | Method I |  | Method II | 
L0 | L1 | L0 MVD | L1 MVD | L0 MVD | L1 MVD | L0 MVD | L1 MVD
short | short | MVD | (-1) MVD | MVD | (-1) MVD | MVD | (-1) MVD
long | long | MVD | (-1) MVD | MVD | (-1) MVD | - | -
short | long | MVD | (-1) MVD | - | - | - | -
long | short | MVD | (-1) MVD | - | - | - | -

## Slide 4: Proposed methods
Method I : SMVD process is restricted when the current picture has mixed reference picture type
if( sps_smvd_enabled_flag && inter_pred_idc[ x0 ][ y0 ] = = PRED_BI && !inter_affine_flag[ x0 ][ y0 ] && RefIdxSymL0 > −1 && RefIdxSymL1 > −1 ) | 
sym_mvd_flag[ x0 ][ y0 ] | ae(v)
The variable RefIdxSymLX with X being 0 and 1 is derived as follows:
The variable currPic specifies the current picture.
RefIdxSymL0 is set equal to −1.
For each index i with i = 0..NumRefIdxActive[ 0 ] − 1, the following applies:
  When all of the following conditions are true, RefIdxSymL0 is set to i:
    DiffPicOrderCnt( currPic, RefPicList[ 0 ][ i ] ) > 0,
    DiffPicOrderCnt( currPic, RefPicList[ 0 ][ i ] ) < DiffPicOrderCnt( currPic, RefPicList[ 0 ][ RefIdxSymL0 ] ) or RefIdxSymL0 is equal to −1.
……
When RefIdxSymL0 is not equal to −1 and RefIdxSymL1 is not equal to −1, the following applies.
  If RefPicList[ 0 ][ RefIdxSymL0 ] is a long-term reference picture and RefPicList[ 1 ][ RefIdxSymL1 ] is a short-term reference picture, RefIdxSymL0 and RefIdxSymL1 are set equal to -1
  Otherwise, if RefPicList[ 0 ][ RefIdxSymL0 ] is a short-term reference picture and RefPicList[ 1 ][ RefIdxSymL1 ] is a long-term reference picture, RefIdxSymL0 and RefIdxSymL1 are set equal to -1

## Slide 5: Proposed methods
  Method II : SMVD process is more restricted where the SMVD is not allowed when the current picture refers to LTRP
The variable RefIdxSymLX with X being 0 and 1 is derived as follows:
The variable currPic specifies the current picture.
RefIdxSymL0 is set equal to −1.
For each index i with i = 0..NumRefIdxActive[ 0 ] − 1, the following applies:
  When all of the following conditions are true, RefIdxSymL0 is set to i:
    DiffPicOrderCnt( currPic, RefPicList[ 0 ][ i ] ) > 0,
    DiffPicOrderCnt( currPic, RefPicList[ 0 ][ i ] ) < DiffPicOrderCnt( currPic, RefPicList[ 0 ][ RefIdxSymL0 ] ) or RefIdxSymL0 is equal to −1,
    RefPicList[ 0 ][ i ] is a short-term-reference picture
RefIdxSymL1 is set equal to −1.
For each index i with i = 0..NumRefIdxActive[ 1 ] − 1, the following applies:
  When all of the following conditions are true, RefIdxSymL1 is set to i:
    DiffPicOrderCnt( currPic, RefPicList[ 1 ][ i ] ) < 0,
    DiffPicOrderCnt( currPic, RefPicList[ 1 ][ i ] ) > DiffPicOrderCnt( currPic, RefPicList[ 1 ][ RefIdxSymL1 ] ) or RefIdxSymL1 is equal to −1.
    RefPicList[ 1 ][ i ] is a short-term-reference picture
……
if( sps_smvd_enabled_flag && inter_pred_idc[ x0 ][ y0 ] = = PRED_BI && !inter_affine_flag[ x0 ][ y0 ] && RefIdxSymL0 > −1 && RefIdxSymL1 > −1 ) | 
sym_mvd_flag[ x0 ][ y0 ] | ae(v)

## Slide 6: Conclusion
Thanks to InterDigital (JVET-O0730) for crosscheck
Symmetric-MVD control method considering reference picture type are proposed.
  Proposed scheme I : SMVD process is restricted when the current picture has mixed reference picture type
  Proposed scheme II : SMVD process is more restricted where the SMVD is not allowed when the current picture refers to LTRP
No changes in coding performance and run-time.
It is recommended to consider this method in the next VTM.