## Slide 1: JVET-O0415 Non-CE4 : Fix of POC distance condition for MMVD
N. Park, H. Jang, J. Nam, J. Lim, S. Kim

## Slide 2: Introduction
MVD derivation process of the MMVD
mMvdL0 = MmvdOffset
mMvdL1 = MmvdOffset
currPocDiffL0 !=
currPocDiffL1
abs(currPocDiffL0) >=
abs(currPocDiffL1)
Yes
No
refPicList0 != LTRP &&
refPicList1 != LTRP
mMvdL0 = MmvdOffset
mMvdL1 = ScaleFactor * MmvdOffset
mMvdL0 = MmvdOffset
mMvdL1 = (-1) * MmvdOffset
refPicList0 != LTRP &&
refPicList1 != LTRP
mMvdL0 = ScaleFactor * MmvdOffset
mMvdL1 = MmvdOffset
mMvdL0 = (-1) * MmvdOffset
mMvdL1 = MmvdOffset
Yes
Yes
No
Yes
No
No

## Slide 3: Proposed methods
Remove the comparing process of the POC distance
  Method I : when the current picture refers one or more long-term reference picture (LTRP).
  Method II : in all cases.
 |  |  | MMVD |  | Method I |  | Method II | 
L0 | L1 | POC | L0 Offset | L1 Offset | L0 Offset | L1 Offset | L0 Offset | L1 Offset
short | short | Same | Offset | Offset | Offset | Offset | Offset | Offset
 |  | Diff (L0>=L1) | Offset | Scaled | Offset | Scaled | Offset | Scaled
 |  | Diff (L0 < L1) | Scaled | Offset | Scaled | Offset | Offset | Scaled
long | long | Same | Offset | Offset | Offset | Offset | Offset | Offset
 |  | Diff (L0>=L1) | Offset | (-1) Offset | Offset | (-1) Offset | Offset | (-1) Offset
 |  | Diff (L0<L1) | (-1) Offset | Offset | Offset | (-1) Offset | Offset | (-1) Offset
short | long | Same | N/A | N/A | N/A | N/A | N/A | N/A
 |  | Diff (L0>=L1) | Offset | (-1) Offset | Offset | (-1) Offset | Offset | (-1) Offset
 |  | Diff (L0<L1) | (-1) Offset | Offset | Offset | (-1) Offset | Offset | (-1) Offset
long | short | Same | N/A | N/A | N/A | N/A | N/A | N/A
 |  | Diff (L0>=L1) | Offset | (-1) Offset | Offset | (-1) Offset | Offset | (-1) Offset
 |  | Diff (L0<L1) | (-1) Offset | Offset | Offset | (-1) Offset | Offset | (-1) Offset

## Slide 4: Proposed methods
Method I : Remove the comparing process of the POC distance when the current picture refers one or more LTRP
mMvdL0 = MmvdOffset
mMvdL1 = MmvdOffset
currPocDiffL0 !=
currPocDiffL1
abs(currPocDiffL0) >=
abs(currPocDiffL1)
Yes
No
mMvdL0 = MmvdOffset
mMvdL1 = ScaleFactor * MmvdOffset
mMvdL0 = ScaleFactor * MmvdOffset
mMvdL1 = MmvdOffset
refPicList0 != LTRP &&
refPicList1 != LTRP
mMvdL0 = MmvdOffset
mMvdL1 = (-1) * MmvdOffset
Yes
Yes
No
No

## Slide 5: Proposed methods
Method II : Remove the comparing process of the POC distance in all Case
mMvdL0 = MmvdOffset
mMvdL1 = MmvdOffset
currPocDiffL0 !=
currPocDiffL1
Yes
No
mMvdL0 = MmvdOffset
mMvdL1 = ScaleFactor * MmvdOffset
refPicList0 != LTRP &&
refPicList1 != LTRP
mMvdL0 = MmvdOffset
mMvdL1 = (-1) * MmvdOffset
Yes
No

## Slide 6: Experimental results
Simulation results
  Anchor : VTM5.0
  Method I : Remove the comparing process of the POC distance when the current picture refers one or more LTRP
    No Changes in coding performance and run-time
  Method II : Remove the comparing process of the POC distance in all Case
    The coding loss is negligible in RA configuration.
    Minor coding loss except ClassE(“Johnny” sequence only) in LB configuration.
 | Random access Main10 |  |  |  |  | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  |  | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.24% | 0.07% | 100% | 100% |  |  |  |  | 
Class A2 | -0.01% | 0.01% | 0.01% | 100% | 102% |  |  |  |  | 
Class B | 0.03% | 0.11% | 0.02% | 100% | 100% | 0.01% | 0.21% | -0.04% | 101% | 102%
Class C | 0.00% | -0.03% | -0.02% | 100% | 98% | 0.03% | 0.04% | -0.17% | 100% | 99%
Class E |  |  |  |  |  | 0.19% | 0.01% | -0.54% | 99% | 99%
Overall | 0.01% | -0.02% | 0.02% | 100% | 100% | 0.06% | 0.10% | -0.21% | 100% | 101%
Class D | 0.02% | -0.04% | 0.08% | 99% | 98% | 0.04% | -0.14% | 0.74% | 100% | 96%
Class F | 0.01% | 0.02% | -0.01% | 100% | 99% | -0.07% | 0.13% | -0.62% | 99% | 100%

## Slide 7: Conclusion
Thanks to Bytedance (JVET-O0868 ) for crosscheck
Comparing process of the POC distance for MVD derivation in MMVD scheme is restricted
  Method I) when a current block refers one or more long-term reference picture
  Method II) in all cases
Using the proposed method I, meaningless condition in case of LTRP is removed.
Using the proposed method II, the number of the condition is reduced to 2 in all cases.
It is recommended to consider this method in the next VTM.