## Slide 1: [JVET-O0419] AHG6: Wrap-around spatial merge candidate for inter prediction
ETRI (Electronics and Telecommunications Research Institute)
KWU (Kwangwoon University)

## Slide 2: Introduction
WD5
  Spatial merge candidates in merge list
    At most 5 spatial candidates can be available
    The merge candidates out of the picture boundary, such as B2, B1, A0 and A1, are excluded from the merge list
CU
CU
Picture boundary
B2
CU
A0
A1
B1
Figure 1. Position of spatial merge candidates in WD5
Figure 2. Example of unavailable candidates

## Slide 3: Introduction
Characteristics of ERP/PERP 360 video
  The boundaries of the picture which highlighted in red shown the figure below connected to each other
  The motion vectors around the boundaries show higher similarity than non-360 video

## Slide 4: Proposed Method
Wrap-around spatial merge candidate
  Adding or subtracting sps_ref_wraparound_offset from the position of the out-of-boundary candidate in the horizontal direction
  In the figure below, A0 and A1 are not used for the proposed method
    Because motion vectors, ‘wrap-around A0’ and ‘wrap-around A1’, are unavailable
A0
A1
A0
A1

## Slide 5: Decoding Process
8.5 Decoding process for coding units coded in inter prediction mode
  8.5.2 Derivation process for motion vector components and reference indices
    8.5.2.2 Derivation process for luma motion vectors for merge mode
if( availableFlagA_1 )
mergeCandList[i++] = A_1
if( availableFlagB_1 )
mergeCandList[i++] = B_1
else
if( sps_ref_warparound_enabled_flag )
if( availableFlag(B_1 - sps_ref_warparound_offset) )
mergeCandList[i++] = B_1
if( availableFlagB_0 )
mergeCandList[i++] = B_0
if( availableFlagA_0 )
mergeCandList[i++] = A_0
if( availableFlagB_2 )
mergeCandList[i++] = B_2
else
if( sps_ref_warparound_enabled_flag )
if( availableFlag(B_2 + sps_ref_warparound_offset) )
mergeCandList[i++] = B_2
if( availableFlagCol )
mergeCandList[i++] = Col

## Slide 6: Experimental Results
Table 1. RD performance of VTM5.0 with 360Lib-9.1 in RA configuration
 |  | Random Access |  |  |  | 
Reference: VTM-5.0 |  | Over VTM-5.0 |  |  |  | 
Tested: Proposed |  | Y | U | V | EncT | DecT
S1 | SkateboardInLot |  |  |  |  | 
 | ChairLift | -0.13% | 0.01% | -0.18% | 99% | 100%
 | KiteFlite |  |  |  |  | 
 | Harbor | -0.01% | -0.04% | -0.02% | 100% | 99%
 | Trolley | -0.03% | -0.07% | 0.03% | 101% | 99%
 | GasLamp | -0.02% | -0.02% | -0.05% | 100% | 100%
S2 | Balboa |  |  |  |  | 
 | Broadway |  |  |  |  | 
 | Landing2 |  |  |  |  | 
 | BranCastle2 |  |  |  |  | 
Overall |  |  |  |  |  | 

## Slide 7: Conclusion
This contribution proposes a wrap-around spatial merge candidate for inter prediction to improve the coding efficiency of 360 video
Experimental results show that the proposed method yields BD-rate gain of 0.xx%, 0.xx%, and 0.xx% for three color components on average over VTM5.0 with 360Lib-9.1
It is suggested to consider to adopt the proposed method in the VVC