## Slide 1: JVET-O0425 Non-CE5: Supplementary results on alternative filter sets for Adaptive Loop Filter
Jonathan Taquet Patrice Onno Christophe Gisquet Guillaume Laroche

## Slide 2: JVET-O0425 Non-CE5: Supplementary results on alternative filter sets for Adaptive Loop Filter
Jonathan Taquet Patrice Onno Christophe Gisquet Guillaume Laroche
2019-07-01

## Slide 3: Introduction
ALF/APS in VTM-5.0
  Up to 1 Luma filter set per APS
    Up to 25 Luma filters per filter set
      12 ( coefficients + clipping indexes )
  Up to 1 Chroma filter per APS
      6 ( coefficients + clipping indexes )
  Memory used for storing filters (per APS):
    1 x 25 x 12 x ( 8 bits + 2 bits ) + 1 x 6 x ( 8 bits + 2 bits ) = 3000 bits + 60 bits = 3060 bits
ALF/APS in CE5-4.3
  Up to 2 Luma filter sets can be signaled per APS
  Up to 8 Chroma filters can be signaled per APS
  Memory used for storing filters (per APS):
    2 x 25 x 12 x ( 8 bits + 2 bits ) + 8 x 6 x ( 8 bits + 2 bits ) = 6000 bits + 480 bits = 6480 bits
Memory for storing filters may become an issue for a decoder because many APS may be accessed in a single Slice

## Slide 4: Proposed changes in JVET-O0425
Remove Luma filter set prediction/derivation from fixed filter sets (Test1)
  Allow to reduce the number of filters to store in memory with next tests
  [Also suggested in JVET-O0669]
ALF/APS
  Up to 2 Luma filter sets can be signaled per APS (as in CE5-4.3)
    + Limit the maximum number of filters per filter set
  Up to 8 Chroma filters can be signaled per APS (as in CE5-4.3)
Limit the maximum number of filters in each alternative Luma filter set
  Test2: Limit first and second Luma filter sets to 7 and 3 filters respectively
    (7 + 3) x 12 x ( 8 bits + 2 bits ) + 8 x 6 x ( 8 bits + 2 bits ) = 1200 bits + 480 bits = 1680 bits
  Test4: Limit first and second Luma filter sets to 7 and 1 filters respectively
    (7 + 1) x 12 x ( 8 bits + 2 bits ) + 8 x 6 x ( 8 bits + 2 bits ) = 960 bits + 480 bits = 1440 bits
Or keep same flexibility as VTM-5.0 by keeping same number of filters in the first alternative filter set
  Test3: Limit first and second Luma filter sets to 25 and 3 filters respectively
    (25 + 3) x 12 x ( 8 bits + 2 bits ) + 8 x 6 x ( 8 bits + 2 bits ) = 3360 bits + 480 bits = 3840 bits
  Test5: Limit first and second Luma filter sets to 25 and 1 filters respectively
    (25 + 1) x 12 x ( 8 bits + 2 bits ) + 8 x 6 x ( 8 bits + 2 bits ) = 3120 bits + 480 bits = 3600 bits

## Slide 5: Test1 (informative): Remove Luma filter set prediction/derivation from fixed filter sets
YUV = (14*Y+U+V)/16

## Slide 6: Results
Results over VTM-5.0: 25 Luma filters (3060 bits / APS)
  CE5-4.3: 25 and 25 Luma filters (6480 bits / APS)
  Test2: Limit to 7 and 3 Luma filters (1680 bits / APS), no fixed filter prediction
  Test3: 25 and limit to 3 Luma filters (3840 bits / APS), no fixed filter prediction
  Test4: Limit to 7 and 1 Luma filters (1440 bits / APS), no fixed filter prediction
  Test5: 25 and limit to 1 Luma filters (3600 bits / APS), no fixed filter prediction
  YUV = (14*Y+U+V)/16

## Slide 7: Conclusion
Proposed changes enable good coding gains/complexity trade-off, and better memory compromise for storing APS filters.
Consider one of Test2, Test3, Test4 or Test5 for an adoption in VTM-6.0.
Thanks to KDDI for cross-checking Tests 2, 3, 4 and 5.

## Slide 8: Thank you for your attention.

## Slide 9: Detailed results

## Slide 10: Test2: Limit to 7 and 3 filters
YUV = (14*Y+U+V)/16

## Slide 11: Test3: Limit to 25 and 3 filters
YUV = (14*Y+U+V)/16

## Slide 12: Test4: Limit to 7 and 1 filters
YUV = (14*Y+U+V)/16

## Slide 13: Test5: Limit to 25 and 1 filters
YUV = (14*Y+U+V)/16