## Slide 1: [Non-CE8] IBC prediction improvement
Akhil Konda
Anubhav Singh
Chirag Pujara
Raj Narayana Gadde

## Slide 2: Motivation
Similar pattern can occur in left, topleft, top blocks with equal probability in screen content video
Above image shows a small region from one of the SCC content
  More similarity is observed in top block
Compression efficiency can be improved by using more similar blocks/CTU as
reference
Figure 1: Snapshot from SC_Console_1920x1080-60_8bit sequence (top CTU is optimal choice)

## Slide 3: Proposed Method
Current IBC design in VVC 5.0 considers left CTU for prediction
Proposed method uses either the top or left CTU as a reference
Hash based matching is used to choose one among top/left CTU
Figure 2: 4x4 block matching
Current CTU
Left CTU
Top CTU

## Slide 4: Choosing candidate CTU
To determine the reference CTU among left or top for the current CTU
  For each 4x4 blocks in the current CTU precomputed hash values are used to find a match either in top or left CTU
  Match counter would be incremented every time there is a match in the corresponding CTUs
  CTU with higher value of match counter would be chosen as a reference

## Slide 5: Signalling
One bit flag at a CTU level is coded to indicate the reference CTU (top or left)
Flag is coded with bypass mode of CABAC

## Slide 6: Results
 | All Intra Main10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.75% | -0.76% | -0.79% | 103% | 99%
TGM | -4.39% | -4.21% | -4.25% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.52% | -0.65% | -0.42% | 104% | 104%
TGM | -1.91% | -1.84% | -1.90% | 102% | 103%
Results for class F and SCC for AI and RA configurations as compared to VTM 5.0

## Slide 7: Conclusion
Proposed method uses top CTU along with left CTU as a candidate reference
A less complex method to arrive at the optimal reference CTU and its signalling is proposed
-4.39% and -0.75% Luma BD-BR gain has been observed for Class SCC and Class F contents respectively for AI case with similar decoding time
-1.91% and -0.52% Luma BD-BR gain has been observed for Class SCC and Class F contents respectively for RA case
It is recommended to adopt the proposed method for improved IBC prediction

## Slide 8: Thank You