## Slide 1: [Non-CE8]: Flipping of reference blocks for Intra Block Copy (IBC)
Anubhav Singh
Akhil Konda
Chirag Pujara
Raj Narayana Gadde

## Slide 2: Motivation
Intra Block Copy (IBC) gives a significant gain for Screen content (Class F & Class TGM) owing to repetitive pattern within a frame
Rigid shapes and patterns may exist in different orientations within the same frame
As per our analysis some blocks/ CUs only differ in terms of their orientations
Example from SlideShow_1280x720_20.yuv, It shows the flipped version being used as reference

## Slide 3: Current pipeline
Current IBC pipeline
  For each block
    Find merge candidate based match
    Find the hash based match
    If not successful, Iterate over all the blocks in given search range and find the best match based on SATD
Current pipeline doesn’t consider any other orientation of reference block other than the original
If the reference block differs from the current block in orientation only, it may result in high SATD. This will result in less optimal prediction

## Slide 4: Proposed Method
In the current pipeline, Instead of using only the original block as prediction reference, three more versions of the reference block are introduced
Total four variations are evaluated for each block to find the best match
The reference blocks are flipped along horizontal and/or vertical axis
Flipping process for reference block (a) Original block (b) Flipped along horizontal axis (c) Flipped along vertical axis and (d) Flipped along both axes

## Slide 5: Proposed Method (Contd…)
As Screen content, generally has fixed and rigid shapes, finding a match in one of these becomes more probable
The proposal includes encoding orientation flag at CU level
Orientation flag is binarized with FL and encoded using single context model
Example: Flipped reference block along with original
00 -> no flipping
01 -> flipped along vertical axis
10 -> flipped along horizontal axis
11 -> flipped along both the axes
Fixed Length (FL) binarization of orientation signal

## Slide 6: Results
BD rate gain for Luma component in case of AI is as follows
  -1.14% for Class F sequence
  -1.35% for Class SCC sequence
 | All Intra Main10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -1.14% | -1.24% | -1.19% | 142% | 102%
TGM | -1.35% | -1.32% | -1.25% | 129% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.73% | -0.74% | -0.58% | 116% | 108%
TGM | -0.35% | -0.10% | -0.17% | 114% | 107%

## Slide 7: Conclusion
The proposed method doesn’t introduce significant decoding complexity (~2-3%)
We observed the following gain without explicit signalling
  -2.02% for Class F sequences & -3.67% for Class TGM sequences for AI case
Efficient coding of orientation flag (currently fixed length binarization) can help in increasing the gain
It is recommended to adopt the proposed method for improved IBC prediction

## Slide 8: Thank You