## Slide 1: [AHG17] Signaling of uniform virtual boundaries
Amith DSouza

## Slide 2: Signalling of Virtual boundaries
Virtual boundaries are currently signalled in VVC as follows
pic_parameter_set_rbsp( ) { | 
… | 
pps_loop_filter_across_virtual_boundaries_disabled_flag | u(1)
if( pps_loop_filter_across_virtual_boundaries_disabled_flag ) { | 
pps_num_ver_virtual_boundaries | u(2)
for( i = 0; i < pps_num_ver_virtual_boundaries; i++ ) | 
pps_virtual_boundaries_pos_x[ i ] | u(v)
pps_num_hor_virtual_boundaries | u(2)
for( i = 0; i < pps_num_hor_virtual_boundaries; i++ ) | 
pps_virtual_boundaries_pos_y[ i ] | u(v)
} | 
… | 
} | 
Each individual virtual boundary is signalled as the absolute distance from the top-left sample
As a result, the number of bits required to signal the virtual boundaries could potentially be very large

## Slide 3: Signalling of Virtual boundaries (Contd…)
The bits required to signal virtual boundaries depends on the size of the frame
For eg., for a resolution of 3072x2048 (cubemap), the number of bits required to signal a single horizontal virtual boundary would be
Num_bits = 1 + Ceil( Log2( 2048 ) − 3 ) + 2 + 2 = 1 + 8 + 2 + 2 = 13 bits
As a worst case scenario, with 3 vertical and 3 horizontal virtual boundaries, the number of bits required would increase to 56 bits
Num_bits = 1 + 3xCeil(Log2(2048) − 3) + 3xCeil(Log2(3072) − 3) + 2 + 2
= 1 + 24 + 27 + 2 + 2 = 56 bits

## Slide 4: Proposed Signalling
An alternate signalling scheme is proposed as below
pic_parameter_set_rbsp( ) { | Descriptor
… | 
pps_loop_filter_across_virtual_boundaries_disabled_flag | u(1)
if( pps_loop_filter_across_virtual_boundaries_disabled_flag ) { | 
pps_num_ver_virtual_boundaries | u(2)
pps_uniform_ver_virtual_boundaries | u(1)
if(!pps_uniform_ver_virtual_boundaries) { | 
for( i = 0; i < pps_num_ver_virtual_boundaries; i++ ) { | 
pps_virtual_boundaries_pos_x[ i ] | u(v)
} | 
} | 
pps_num_hor_virtual_boundaries | u(2)
pps_uniform_hor_virtual_boundaries | u(1)
if(!pps_uniform_hor_virtual_boundaries) { | 
for( i = 0; i < pps_num_hor_virtual_boundaries; i++ ) { | 
pps_virtual_boundaries_pos_y[ i ] | u(v)
} | 
} | 
} | 
… | 
} | 
pps_uniform_ver_virtual_boundaries and pps_uniform_hor_virtual_boundaries are used to signal the number of uniform virtual boundaries
In case of uniform virtual boundaries present, the number of bits required would be constant unlike before

## Slide 5: Proposed Signalling (Contd…)
Similarly, the position of the horizontal virtual boundaries is computed as below
If pps_uniform_ver_virtual_boundaries equal to 1
for (i=0;i< pps_num_ver_virtual_boundaries ;i++)
PpsVirtualBoundariesPosX[i] = (i + 1) * (((pic_width_in_luma_samples >> 3)/(pps_num_ver_virtual_boundaries + 1)) << 3)
Otherwise,
PpsVirtualBoundariesPosX[i] = pps_virtual_boundaries_pos_x[ i ] * 8
The position of the vertical virtual boundaries is computed as below
If pps_uniform_hor_virtual_boundaries equal to 1
for (i=0;i< num_uni_hor_virtual_boundaries;i++)
PpsVirtualBoundariesPosY[i] = (i + 1) * (((pic_height_in_luma_samples >> 3)/(pps_num_hor_virtual_boundaries + 1)) << 3)
Otherwise
PpsVirtualBoundariesPosY[i] = pps_virtual_boundaries_pos_y[ i ] * 8

## Slide 6: Proposed (vs) Current
A comparison of the bits required in case of 3072x2048 frame is given below
Num of virtual boundaries | Bits required With Current Syntax | Bits required With Modified Syntax | Reduction in bits
1 vertical, 0 horizontal | 1 + 2 + 2 + 9 = 14 | 1 + 1 + 2 + 1 + 2 = 7 | 7
0 vertical, 1 horizontal | 1 + 2 + 8 + 2 = 13 |  | 6
1 vertical, 1 horizontal | 1 + 2 + 8 +2 + 9 = 22 |  | 15
3 vertical, 3 horizontal (worst case) | 1 + 2 + (3 * 8) + 2 + (3 * 9) = 56 |  | 49

## Slide 7: Conclusion
It has been shown that the number of bits required would be significantly reduced in case of uniform virtual boundaries
It is recommended to adopt the modified syntax as proposed

## Slide 8: Thank You