## Slide 1: /JVET-O0451 Subjective Comparison of VVC and HEVC/
15th JVET Meeting: Gothenburg, SE, 3–12 July 2019

## Slide 2: Introduction: Context & Motivations
VVC is reaching the CD stage soon
Important to compare its level of performance
  relative to HEVC
Formal subjective test organised by b<>com, INSA and Orange
HD and UHD resolutions in SDR
SAMVIQ methodology
Notes: The VVC project is close to Committee Draft (CD) stage, so we thought that it is the right time to assess its quality performance with respect to HEVC. A formal subjective test has been carried-out by b<>com Orange and INSA. We consider video in Standard Dynamic Range in HD 1080p and UHD 4K resolution and we use the SAMVIC methodology.
SAMVIQ : Subjective Assessment of Multimedia Quality
CD : Committee Draft

## Slide 3: Subjective Test Methodology
Samviq evaluation protocol
  recommended for the subjective assessment of multimedia applications
  Used in the past for the comparison of HEVC vs AVC (m29210)
  Uses a continuous scale for quality levels
Score | Quality
0-20 | Bad
20-40 | Poor
40-60 | Fair
60-80 | Good
80-100 | Excellent
Notes: SAMVIC for Subjective Assessment Methodology for Video Quality is recommended for subjective assessment of multimedia applications, it offers the possibility to view the videos many times, and adjust the score. It has also used in the past to compare HEVC with respect to AVC in contribution m29210. SAMVIC defines a continuous scale for quality levels from 0 to 100 where quality area from 0 to 20 refers to bad quality, ….

## Slide 4: Sequences
7 video sequences
  SDR in UHD resolution (3840x2160)
  Different bit-depths and frame rates
  10 seconds duration
  Different sources: CTC, 4EVER-2 project
Down-sampled to HD resolution
  Filter of the SHM
Sequence | Resolution | Duration | Frame rate | Bit-depth | Source
AerialCrowd2 | HD/UHD | 10s | 30 | 10 | Huawei
CatRobot1 | HD/UHD | 10s | 60 | 10 | b<>com
CrowdRun | HD/UHD | 10s | 50 | 8 | SVT
DaylightRoad | HD/UHD | 10s | 60 | 10 | Huawei
Drums2 | HD/UHD | 10s | 50 | 10 | b<>com
HorseJumping | HD/UHD | 10s | 50 | 10 | 4EVER-2
Sedof | HD/UHD | 10s | 60 | 8 | 4EVER-2
Notes: We start with 13 sequences, then we selected 7 that are representative of natural scenes, span will the 2D spatio-temporal plane. The video are in UHDp resolution, in different bit-depths and frame rates, of 10 second duration. The are from differnt sources some from VVC CTC and 4-Ever Franch project.

## Slide 5: Sequences

## Slide 6: Coding configuration
Codecs HM-16.20 (anchor) & VTM-5.0
Following the CTC
  Random access
  1s random access period
  main10 for HEVC
Nine realistic rates selected
  Cover the range for HD & UHD services
A per sequence rate selection was operated
  After encoding and informal viewing
  objective: covers the quality range
    from fair to excellent (avoid non practical quality ranges)
    5 rates are retained for each sequence
Rate (Kbps) | 1080 (HD) | 2160 (UHD)
R1 | 500 | 1000
R2 | 1000 | 2000
R3 | 1500 | 3000
R4 | 2000 | 4000
R5 | 3000 | 6000
R6 | 4000 | 8000
R7 | 6000 | 12000
R8 | 8000 | 16000
R9 | 10000 | 20000
Notes: We use the HM-16.20 and VTM-5 as reference software for HEVC and VVC to encode the videos in Random Access coding configuration and Intra period of 1 second. We first selected Nice realistic range of bitrates for HD and UHD resolutions, the bitrates are given in this table that goes from 5K to 10M for HD and 1Mbps to 20bps for UHD. After an informal viewing, we select 5 bitrates that cover the quality scales from fair to Excellent.

## Slide 7: Objective Evaluation
Objective quality metrics
  PSNR, MS-SSIM & VMAF
  BD-Rate
Notes: We first performed an objective evaluation with three classical metrics including PSNR, MS-SSIM and VMAF and associated BD-rate.

## Slide 8: Aerial Crowd (PSNR)
Notes: A review quickly the PSNR scores, this figure gives the PSNR versus the bitrate for VVC in red and HEVC in blue, dotted line refers to UHD and solid line to HD resolution. VVC offers always higher PSNR quality with -24 and -27 bitrate reduction for this sequence.

## Slide 9: CatRobot (PSNR)

## Slide 10: CrowdRun (PSNR)

## Slide 11: DaylightRoad (PSNR)

## Slide 12: Drums2 (PSNR)

## Slide 13: HorseJumping (PSNR)

## Slide 14: Sedof (PSNR)

## Slide 15: BD-Rate Performance
Resolution | BD-rate (PSNR) | BD-rate (VMAF)
HD | -31.24% | -35.18%
UHD | -34.42% | -40.44%

## Slide 16: Subjective test
Organised at INSA Rennes
  Controlled environment PAVIM Lab IUT-R BT.500-13 Rec.
  Loewe 4K OLED display (Loewe Bild 7.55) – 55 inches
  5 bitrates x 7 sequences x 2 res. x 2 codecs + 2 ref. x 7 x 2 res.= 168
  4 sessions of 20 minutes : 2 sessions HD & 2 sessions UHD

## Slide 17: Subjective Test HD
23 subjects,
17 retained for statistical analysis
  after post-screening based on Pearson / Spearman correlations

## Slide 18: HD AerialCrowd
BD-Rate (MOS): -32%
Fair quality area
Good quality area

## Slide 19: HD CatRobot
BD-Rate (MOS): -48%
-50%
Excellent quality area
Notes: 50% bitrate gain
Increase the guality for the same bitrate from Good area to Excellent Area or from Fair area to Good Area quality.

## Slide 20: HD CrowdRun
BD-Rate (MOS): -34%
~-40%
Good quality area

## Slide 21: HD DaylightRoad
BD-Rate (MOS): -50%
-50%
Good quality area

## Slide 22: HD Drums2
BD-Rate (MOS): -35%
~-33%
Excellent quality area

## Slide 23: HD HorseJumping
BD-Rate (MOS): -37%
Fair quality area
Good quality area

## Slide 24: HD Sedof
BD-Rate (MOS): -19%

## Slide 25: Subjective Test UHD
21 subjects,
19 retained for statistical analysis
  after post-screening based on Pearson / Spearman correlations

## Slide 26: UHD AerialCrowd2
BD-Rate (MOS): -41%
Fair quality area
Good quality area

## Slide 27: UHD CatRobot1
BD-Rate (MOS): -47%
-50%
Excellent quality area

## Slide 28: UHD CrowdRun
BD-Rate (MOS): -35%
Poor quality area
Fair quality area
Fair quality area
Good quality area

## Slide 29: UHD DaylightRoad

## Slide 30: UHD Drums2
BD-Rate (MOS): -39%
~-50%
Good quality area

## Slide 31: UHD HorseJumping
BD-Rate (MOS): -45%
-33%
Good quality area

## Slide 32: UHD Sedof
BD-Rate (MOS): -21%

## Slide 33: BD-Rate Performance
Resolution | BD-rate (PSNR) | BD-rate (VMAF) | BD-rate (MOS)
HD | -31.24% | -35.18% | -36%
UHD | -34.42% | -40.44% | -40%

## Slide 34: Findings
VVC significantly outperforms HEVC
  for HD and UHD
  for all video clips
BD-Rate improvement consistent with those measured under the CTCs
Current VTM close to offer 40% of bit reduction over HEVC

## Slide 35
/wassim.hamidouche@insa-rennes.fr/