## Slide 1
JVET-O0465
Non-CE6: Simplified SBT mode coding

## Slide 2: JVET-O0465: Simplified SBT mode coding
VTM-5.0 Sub-Block Transform (SBT) mode is signaled with 4 flags
  cu_sbt_flag indicates the use of SBT for a given INTER CU
  cu_sbt_quad_flag indicates the type of CU partitioning into TUs: symmetric or asymmetric
  cu_sbt_horizontal_flag indicates the split orientation: horizontal or vertical
  cu_sbt_pos_fag indicates which TU has non-zero residual
The 4 bins are context-based coded
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
cu_sbt_flag | ( cbWidth * cbHeight < 256 ) ? 1 : 0 | na | Na | na | na | na
cu_sbt_quad_flag | 0 | na | Na | na | na | na
cu_sbt_horizontal_flag | ( cbWidth = = cbHeight ) ? 0 : ( cbWidth < cbHeight ) ? 1 : 2 | na | Na | na | na | na
cu_sbt_pos_flag | 0 | na | Na | na | na | na
… | … | … | … | … | … | …

## Slide 3: JVET-O0465: Simplified SBT mode coding
Proposal:
  Context-based code of the first bin cu_sbt_flag (as in VTM-5.0)
  Bypass code the three other bins:
    cu_sbt_quad_flag
    cu_sbt_horizontal_flag
    cu_sbt_pos_fag
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
cu_sbt_flag | ( cbWidth * cbHeight < 256 ) ? 1 : 0 | na | Na | na | na | na
cu_sbt_quad_flag | Bypass | na | Na | na | na | na
cu_sbt_horizontal_flag | Bypass | na | Na | na | na | na
cu_sbt_pos_flag | Bypass | na | Na | na | na | na
… | … | … | … | … | … | …

## Slide 4: JVET-O0465: Simplified SBT mode coding
Results:
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.17% | 0.09% | 97% | 102%
Class A2 | 0.01% | -0.02% | 0.07% | 99% | 104%
Class B | 0.02% | 0.01% | -0.01% | 94% | 101%
Class C | 0.01% | -0.17% | -0.13% | 94% | 94%
Class E |  |  |  |  | 
Overall | 0.01% | -0.08% | -0.01% | 96% | 100%
Class D | 0.02% | -0.12% | 0.24% | 97% | 91%
Class F | 0.03% | 0.02% | 0.01% | 98% | 97%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.23% | 0.24% | 103% | 105%
Class C | 0.05% | -0.25% | -0.21% | 104% | 114%
Class E | -0.02% | 0.10% | -0.14% | 104% | 110%
Overall | 0.02% | 0.04% | 0.00% | 104% | 109%
Class D | -0.06% | -0.69% | 0.35% | 103% | 111%
Class F | 0.04% | -0.04% | 0.06% | 108% | 110%

## Slide 5: JVET-O0465: Simplified SBT mode coding
Conclusion
  Propose to signal SBT mode with 1 context-based coded flag and 3 bypass flags
  Very small impact on the coding efficiency
  Suggestion: adopt in VTM-6
  We thank ByteDance for cross-checking this contribution