## Slide 1
Non-CE3: Simplified MRL and ISP mode coding
JVET-O0467

## Slide 2: JVET-O0467: Simplified MRL and ISP mode coding
VTM-5.0 MRL (Multiple Reference Line) mode:
  2 bins are used to signal the reference line (intra_luma_ref_idx syntax element):
    First bin indicates the reference line is different from the default one (index 0)
    If true, second bin indicates if the reference line index is equal to 1 or 3
    Both bins are context-based coded
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
intra_luma_ref_idx[ ][ ] | 0 | 1 | na | na | na | Na
… | … | … | … | … | … | …

## Slide 3: JVET-O0467: Simplified MRL and ISP mode coding
Proposal 1:
  Bypass coding of the second bin of intra_luma_ref_idx
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
intra_luma_ref_idx[ ][ ] | 0 | bypass | na | na | na | Na
… | … | … | … | … | … | …

## Slide 4: JVET-O0467: Simplified MRL and ISP mode coding
Results:
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.00% | 0.04% | 102% | 101%
Class A2 | 0.00% | -0.05% | -0.02% | 102% | 103%
Class B | 0.01% | -0.06% | 0.03% | 100% | 105%
Class C | 0.01% | -0.07% | 0.04% | 97% | 103%
Class E | 0.01% | -0.09% | -0.04% | 100% | 101%
Overall | 0.01% | -0.06% | 0.01% | 100% | 103%
Class D | 0.00% | 0.08% | -0.04% | 102% | 108%
Class F | 0.00% | -0.04% | 0.02% | 101% | 104%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.16% | 0.07% | 103% | 103%
Class A2 | 0.04% | 0.10% | -0.01% | 101% | 102%
Class B | 0.02% | -0.02% | -0.03% | 101% | 107%
Class C | -0.04% | -0.10% | -0.19% | 101% | 103%
Class E |  |  |  |  | 
Overall | 0.01% | -0.05% | -0.05% | 102% | 104%
Class D | 0.03% | -0.02% | 0.05% | 101% | 102%
Class F | 0.02% | 0.11% | 0.11% | 98% | 99%

## Slide 5: JVET-O0467: Simplified MRL and ISP mode coding
VTM-5.0 ISP (Intra sub-partition) mode coding:
  2 flags are used to signal ISP mode:
    intra_subpartitions_mode_flag indicates the use of ISP
    intra_subpartitions_split_flag indicates the horizontal or vertical split orientation
    Both flags are context-based coded
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
intra_subpartitions_mode_flag | 0 | na | na | na | na | Na
intra_subpartitions_split_flag | 0 | na | na | na | na | Na
… | … | … | … | … | … | …

## Slide 6: JVET-O0467: Simplified MRL and ISP mode coding
Proposal 2:
  Bypass coding of the flag intra_subpartitions_split_flag
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
… | … | … | … | … | … | …
intra_subpartitions_mode_flag | 0 | na | na | na | na | Na
intra_subpartitions_split_flag | bypass | na | na | na | na | Na
… | … | … | … | … | … | …

## Slide 7: JVET-O0467: Simplified MRL and ISP mode coding
Results (Proposals 1 + 2):
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | -0.02% | 103% | 104%
Class A2 | 0.02% | -0.02% | -0.05% | 102% | 104%
Class B | 0.02% | -0.01% | 0.05% | 102% | 109%
Class C | 0.02% | 0.00% | 0.08% | 98% | 103%
Class E | 0.02% | 0.04% | 0.02% | 101% | 104%
Overall | 0.02% | 0.00% | 0.02% | 101% | 105%
Class D | 0.01% | 0.32% | -0.07% | 99% | 104%
Class F | 0.03% | 0.05% | 0.08% | 102% | 106%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.19% | 0.13% | 101% | 104%
Class A2 | 0.05% | 0.19% | 0.15% | 102% | 108%
Class B | 0.00% | -0.09% | -0.09% | 100% | 107%
Class C | -0.01% | -0.02% | -0.09% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0.01% | -0.04% | 0.00% | 101% | 105%
Class D | 0.05% | -0.17% | 0.12% | 99% | 98%
Class F | 0.01% | -0.17% | 0.24% | 100% | 102%

## Slide 8: JVET-O0467: Simplified MRL and ISP mode coding
Conclusion
  Proposal 1: code the second bin of MRL index in bypass mode
  Proposal 2: code the flag intra_subpartitions_split_flag in bypass mode
  Very small impact on the coding efficiency
  Suggestion: adopt in VTM-6
  We thank ByteDance for cross-checking this contribution