## Slide 1: Independent layer concepts clarifications and improvements for immersive media use cases
JVET-O0471
Emmanuel Thomas (TNO)

## Slide 2: Outline
An analysis of the independent layer concept as understood from the VVC Draft v5.
Proposed clarifications for the definitions of coded picture and the scope of the layer id.
Proposed modifications to better support immersive media use cases as originally motivated by JVET-N0278 [1] (layer concept at JVET 14th) which are:
  Relaxing constraints on coded layer video sequence start picture alignment
  Removing layer ordering by increased value of NuhLayerId in access unit

## Slide 3: 1. Layers in VVC Draft v5
coded video sequence (CVS): A sequence of access units that consists, in decoding order, of a CVSS access unit, followed by zero or more access units that are not CVSS access units, including all subsequent access units up to but not including any subsequent access unit that is a CVSS access unit.
access unit: A set of NAL units that are associated with each other according to a specified classification rule, are consecutive in decoding order, and contain exactly one coded picture for each present layer access unit.
layer: A set of VCL NAL units that all have a particular value of NuhLayerId and the associated non-VCL NAL units.
layer access unit: A set of NAL units for which the VCL NAL units all have a particular value of NuhLayerId, that are associated with each other according to a specified classification rule, that are consecutive in decoding order, and that contain exactly one coded picture.
coded layer video sequence (CLVS): A sequence of layer access units that consists, in decoding order, of a CLVSS layer access unit, followed by zero or more layer access units that are not CLVSS layer access units, including all subsequent layer access units up to but not including any subsequent layer access unit that is a CLVSS layer access unit.
coded picture: A coded representation of a picture comprising VCL NAL units with a particular value of NuhLayerId within an access unit and containing all CTUs of the picture.

## Slide 4: 1. Layers in VVC Draft v5
Conceptual model of VVC bitstream

## Slide 5: 1. Layers in VVC Draft v5
Bitstream view of CVS and CLVS

## Slide 6: 2. Proposed clarifications: coded picture
coded picture: A coded representation of a picture comprising VCL NAL units with a particular value of NuhLayerId within an access unit and containing all CTUs of the picture.
Does particular mean the same value ? Isn’t a coded picture part of a layer access unit?
coded picture: A coded representation of a picture comprising VCL NAL units with the same value of NuhLayerId within a layer access unit and containing all CTUs of the picture.

## Slide 7: 2. Proposed clarifications: layer id scope
nuh_layer_id_plus1 semantic is defined but the scope of the id is unclear.
It seems that the scope of is the bitstream given the bitstream extraction description.
To avoid any ambiguity, it is proposed to clarify the scope of the NuhLayerId to be the bitstream.

## Slide 8: 3. Proposed changes: relaxing start pictures
Normative statement (7.4.2.4.3)
"The first access unit of a CVS is a CVS start access unit, wherein each present layer access unit is a CLVS start layer access unit, which is either an IRAP layer access unit with NoIncorrectPicOutputFlag equal to 1 or a GRA layer access unit with NoIncorrectPicOutputFlag equal to 1."
Normative statement (7.4.2.4.3)
"It is a requirement of bitstream conformance that, when present, each layer access unit in the next access unit after an access unit that contains an end of sequence NAL unit or an end of bitstream NAL unit shall be an IRAP layer access unit, which may be an IDR layer access unit or a CRA layer access unit, or a GRA layer access unit. "

## Slide 9: 3. Proposed changes: relaxing start pictures
This mandates that all the layers have aligned start pictures anywhere in the bitstream.
This mandates that all the CLVS are stopped and restarted whenever one CLVS has ended.

## Slide 10: 3. Proposed changes: relaxing start pictures
In the context of immersive media, as pointed in JVET-N0278 [1], the MPEG output document N18134 mentions that:
  an “Object” is defined as a visual element that is independently decodable and represented by its own fully conformant bitstream.
Proposal
  Relaxing constraint on CLVS start picture alignment anywhere but in the first access unit of the first CVS and relaxing the constraint on the alignment of the end of CLVS.

## Slide 11: 3. Proposed changes: relaxing start pictures
Normative statement (7.4.2.4.3)
"The first access unit of a CVS is a CVS start access unit, wherein each present layer access unit is a CLVS start layer access unit, which is either an IRAP layer access unit with NoIncorrectPicOutputFlag equal to 1 or a GRA layer access unit with NoIncorrectPicOutputFlag equal to 1.“
"The first access unit of a CVS is a CVS start access unit, wherein at least one present layer access unit is a CLVS start layer access unit, which is either an IRAP layer access unit with NoIncorrectPicOutputFlag equal to 1 or a GRA layer access unit with NoIncorrectPicOutputFlag equal to 1."

## Slide 12: 3. Proposed changes: relaxing start pictures
Normative statement (7.4.2.4.3)
"It is a requirement of bitstream conformance that, when present, each layer access unit in the next access unit after an access unit that contains an end of sequence NAL unit or an end of bitstream NAL unit shall be an IRAP layer access unit, which may be an IDR layer access unit or a CRA layer access unit, or a GRA layer access unit. "
"It is a requirement of bitstream conformance that, when present, at least one layer access unit in the next access unit after an access unit that contains an end of sequence NAL unit or an end of bitstream NAL unit shall be an IRAP layer access unit, which may be an IDR layer access unit or a CRA layer access unit, or a GRA layer access unit. "

## Slide 13: 3. Proposed changes: layer id ordering
Normative statement (7.4.2.4.4)
"An access unit consists of one or more layer access units in increasing order of NuhLayerId.“
Discussion
Since independent baser layers have no hierarchy, ordering of the layer access units in the access unit is artificial . This even complexifies the merging operations of layers to obey this strict ordering.
Proposal
Since this ordering of layers does not seem to be motivated, it is proposed to remove it.

## Slide 14: 3. Proposed changes: layer id ordering
Normative statement (7.4.2.4.4)
"An access unit consists of one or more layer access units in increasing order of NuhLayerId.“
Normative statement (7.4.2.4.4)
"An access unit consists of one or more layer access units starting with NuhLayerId value ‘0’ first, if present.“

## Slide 15: Conclusion
In order to better support immersive media use cases as originally motivated by JVET-N0278 [1], we recommend to adopt the proposed text clarifications as well the technical changes described above which are:
Relaxing constraints on coded layer video sequence start picture alignment
Removing layer ordering by increased value of NuhLayerId in access unit