## Slide 1
Non-CE6: Simplified entropy coding for intra prediction mode
JVET-O0476
The 15th JVET Meeting
Jul. 2019
Dohyeon Park, Yong-Uk Yoon, Jihoon Do Jae-Gon Kim (KAU)
Jinho Lee, Jungwon Kang (ETRI)

## Slide 2: I. Background
Information related to MPM are signaled with and intra_luma_not_planar_flag
  intra_luma_mpm_flag is regular coded with 1 context model
  intra_luma_not_planar_flag is regular coded with 2 context model based on the ISP mode
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
intra_luma_mpm_flag[ ][ ] | 0 | na | na | na | na | na
intra_luma_not_planar_flag[ ][ ] | intra_subpartitions_mode_flag | na | na | na | na | na

## Slide 3: II. Proposed Simplification
Proposed simplification
  The number of context models of intra_luma_not_planar_flag is reduced to one without any condition
  The initial value of the kept context model is the same as that of the regular planar mode in WD5
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
intra_luma_mpm_flag[ ][ ] | 0 | na | na | na | na | na
intra_luma_not_planar_flag[ ][ ] | intra_subpartitions_mode_flag0 | na | na | na | na | na

## Slide 4: III. Experimental Results
Experimental results
  Anchor: VTM5.0 with CTC
  Test: Anchor + proposed method
 | All Intra |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.05% | -0.02% | 84% | 99%
Class A2 | 0.01% | -0.04% | -0.05% | 91% | 100%
Class B | 0.00% | 0.01% | 0.07% | 100% | 100%
Class C | -0.01% | -0.07% | 0.05% | 134% | 100%
Class E | -0.01% | -0.07% | -0.07% | 109% | 99%
Overall | 0.00% | -0.02% | 0.01% | 103% | 100%
Class D | -0.01% | 0.05% | -0.07% | 77% | 99%
Class F | 0.01% | -0.01% | 0.05% | 76% | 99%
Random Access |  |  |  | 
Over VTM-5.0 |  |  |  | 
Y | U | V | EncT | DecT
0.01% | 0.01% | 0.15% | 100% | 103%
0.03% | 0.04% | 0.09% | 100% | 101%
-0.01% | -0.05% | -0.12% | 99% | 101%
-0.02% | -0.05% | -0.05% | 99% | 99%
0.00% | -0.02% | -0.01% | 100% | 101%
0.05% | -0.04% | 0.41% | 98% | 98%
0.01% | 0.01% | 0.14% | 96% | 100%

## Slide 5: IV. Conclusions
Proposed method
  The simplified regular coding method of a planar flag to reduce the number of context models without dependency between ISP flag and planar flag
Experimental results show 0.00% and 0.00% luma BD-rate performance for AI and RA, respectively
The proposed regular coding method is simpler than the current design of without BD-rate loss