## Slide 1: JVET-O0487
Johannes Sauer
RWTH Aachen University

## Slide 2: Uncoded areas for 360°tools
Premise: Code each face with a least one tile
Include padding area for all faces in the reference picture
Green: Coded cube faces
White: Uncoded areas

## Slide 3: 360°coding tools – Geometry padding

## Slide 4: Other applications
Additional reference pictures
  Encoder needs to code different motion vector
Multi layer coding
Scalable coding
Issues:
  Dependencies of tiles on other tiles
Reference picture
Additional reference (empty tile)
Base layer
Upsampled base layer (empty tile)
Enhancement layer
Unused

## Slide 5: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
Tile rows
Green: Coded cube faces White: Uncoded slices

## Slide 6: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
slice_header( ) { | Descriptor
slice_pic_parameter_set_id | ue(v)
if( rect_slice_flag ¦ ¦ NumBricksInPic > 1 ¦ ¦ allow_uncoded_areas_flag ) | 
slice_address | u(v)
… | 
byte_alignment( ) | 
} | 

## Slide 7: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
pic_parameter_set_rbsp( ) { | Descriptor
pps_pic_parameter_set_id | ue(v)
pps_seq_parameter_set_id | ue(v)
output_flag_present_flag | u(1)
single_tile_in_pic_flag | u(1)
if( !single_tile_in_pic_flag ) { | 
uniform_tile_spacing_flag | u(1)
if( uniform_tile_spacing_flag ) { | 
tile_cols_width_minus1 | ue(v)
tile_rows_height_minus1 | ue(v)
} else { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
tile_column_width_minus1[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
tile_row_height_minus1[ i ] | ue(v)
} | 
allow_uncoded_areas_flag | u(1)
if( allow_uncoded_areas_flag ) { | 
for( i = 0; i < NumTilesInPic; i++ ) { | 
tile_is_coded_flag[ i ] | u(1)
} | 
} | 
brick_splitting_present_flag | u(1)
… | 
rbsp_trailing_bits( ) | 
} | 

## Slide 8: Discussion of uncoded areas for 360
Advantages
  All operations can be done / specified at buffer level
    Geometry padding: Uncoded areas are filled with generated geometry padding samples
      Already padded regions of reference pictures can be reused when referenced again
  No arbitrary buffer access at CTU level
    On the fly implementations need to use pixels from up to 3 different locations in the picture (cube corner)
Disadvantages
  Generation of not required samples
    Problem for rather complex geometry padding
      Solution via APS signaling required padding amount

## Slide 9: Signaling geometry padding usage via APS
Enables efficient application of geometry padding at picture level
  Existing padding of reference pictures can be reused
  Only required padding is generated
gp_data () { | Descriptor
incremental_padding_flag | u(1)
for ( list = 0; list < 2; list++ ) { | 
num_ref_idx_minus1[ list ] | u(2)
for ( idx = 0; idx < NumRefIdx[ list ]; idx++ ) { | 
pad_picture_flag[ list ][ idx ] | u(1)
if ( pad_picture_flag[ list ][ idx ] ) { | 
for ( face = 0; face < 6; face++ ) { | 
pad_top_boundary_flag[ list ][ idx ][ face] | u(1)
pad_bottom_boundary_flag[ list ][ idx ][ face ] | u(1)
pad_left_boundary_flag[ list ][ idx ][ face ] | u(1)
pad_right_boundary_flag[ list ][ idx ][ face ] | u(1)
} | 
for ( face = 0; face < 6; face++ ) { | 
if ( pad_top_boundary_flag[ list ][ idx ][ face ] ) { | 
pad_top_boundary_width[ list ][ idx ][ face ] | ue(v)
} | 
if ( pad_bottom_boundary_flag[ list ][ idx ][ face ] ) { | 
pad_bottom_boundary_width[ list ][ idx ][ face ] | ue(v)
} | 
if ( pad_left_boundary_flag[ list ][ idx ][ face ] ) { | 
pad_left_boundary_width[ list ][ idx ][ face ] | ue(v)
} | 
if ( pad_right_boundary_flag[ list ][ idx ][ face ] ) { | 
pad_right_boundary_width[ list ][ idx ][ face ] | ue(v)
} | 
} | 
} | 
} | 
} | 
} | 

## Slide 10: Specification of 360°tools
Operations for enabling 360°tools do not require changes at CTU level
Uncoded areas/slices
  Modified PPS
  Modified slice header
  Or other technology providing uncoded areas
APS for signaling geometry padding usage
Process for generating geometry padding
Signaling of cube face arrangement

## Slide 11: Specification of 360°tools – Geometry padding
Specifciation
  A integer sample location in the padded region is selected
  map to unit cube packing location
  projected to 3D cube location
  back projected to source unit cube packing location
    automatically moves the sample from the padding region inside another face
  Map to fractional sample location in the coded face arrangement
  NN-Interpolation using the found source sample location
Missing
  Specification for chroma

## Slide 12: Implementation status
VTM 5.0
  Picture level geometry padding
  Signaling of cube faces arrangement
  Signaling of geometry padding usage with SEI (since APS types are not properly implemented yet)
  Uncoded areas using uncoded slices
    Not using changes for bricks (can not be configured yet to use multiple slices)
    Code each face as a tile
      Slice mode -> 1 tile per slice

## Slide 13: Results with ALF off
ALF does not support disabling at slices/tiles yet
Geometry padding (1 slice per face) against original (1 slice per picture)
Geometry padding (1 slice per face) against original (1 slice per face)
 | End-to-end WS-PSNR |  |  |  | 
 | Y | U | V | EncT | DecT
Class S1 | -0.42% | 1.56% | 0.66% | 108% | 139%
Class S2 | -0.85% | 4.12% | -0.81% | 102% | 127%
Overall | -0.59% | 2.58% | 0.07% | 106% | 134%
 | End-to-end WS-PSNR |  |  |  | 
 | Y | U | V | EncT | DecT
Class S1 | -1.21% | 1.08% | 0.64% | 104% | 140%
Class S2 | -1.37% | 3.99% | -0.25% | 105% | 127%
Overall | -1.27% | 2.25% | 0.28% | 105% | 135%

## Slide 14: Results with ALF using virtual LF boundaries
Geometry padding (1 slice per face) against original (1 slice per picture)
Geometry padding (1 slice per face) against original (1 slice per face)
 | End-to-end WS-PSNR |  |  |  | 
 | Y | U | V | EncT | DecT
Class S1 | -0.56% | 0.96% | 0.42% |  | 126%
Class S2 | -1.94% | -2.00% | -2.56% |  | 118%
Overall | -1.11% | -0.22% | -0.78% |  | 122%
 | End-to-end WS-PSNR |  |  |  | 
 | Y | U | V | EncT | DecT
Class S1 | -1.39% | 0.23% | 0.07% |  | 120%
Class S2 | -2.55% | -2.08% | -2.18% |  | 114%
Overall | -1.86% | -0.70% | -0.83% |  | 117%

## Slide 15: Conclusion
Further study of geometry padding using uncoded areas
Exploration of other applications of uncoded areas
Recommendation
  Add support for uncoded areas to VVC