## Slide 1
Non-CE4:
Affine and sub-block modes coding clean-up

## Slide 2: Problem statement
In VTM-5.0, sub-block mode is used to signal both SbTMVP and affine modes:
From “7.3.7.7 Merge data syntax”:
From “7.3.7.5 Coding unit syntax”:
but merge_subblock_flag and inter_affine_flag actually both use the same affine flag coding context.
if( MaxNumSubblockMergeCand > 0 && cbWidth >= 8 && cbHeight >= 8 ) | 
merge_subblock_flag[ x0 ][ y0 ] | ae(v)
if( sps_affine_enabled_flag && cbWidth >= 16 && cbHeight >= 16 ) { | 
inter_affine_flag[ x0 ][ y0 ] | ae(v)

## Slide 3: Solutions
To avoid mix between affine and SbTMVP coding, it is proposed to use separate CABAC contexts (test 1):
  the function subblock_merge_flag() is transformed from:
  To:
unsigned ctxID= DeriveCtx::CtxAffineFlag(cu); cu.affine = m_BinDecoder.decodeBin(Ctx::AffineFlag(ctxId));
unsigned ctxID= DeriveCtx::CtxSubblockFlag(cu); cu.subblock = m_BinDecoder.decodeBin(Ctx::SubblockFlag(ctxId));

## Slide 4: Solutions
To further remove dependencies, the affine and sub-block flag coding is simplified (test 2):
  function affine_flag() :
  function subblock_merge_flag() :
unsigned ctxID= 0; cu.affine = m_BinDecoder.decodeBin(Ctx::AffineFlag(ctxId));
unsigned ctxID= 0; cu.subblock = m_BinDecoder.decodeBin(Ctx::SubblockFlag(ctxId));

## Slide 5: Solutions
Test 2 then removes access to neighbouring CUs affine flag during the parsing:
const CodingStructure *cs = cu.cs; unsigned ctxId = 0; const CodingUnit *cuLeft = cs->getCURestricted( cu.lumaPos().offset( -1, 0 ), cu, CH_L ); ctxId = ( cuLeft && cuLeft->affine ) ? 1 : 0; const CodingUnit *cuAbove = cs->getCURestricted( cu.lumaPos().offset( 0, -1 ), cu, CH_L ); ctxId += ( cuAbove && cuAbove->affine ) ? 1 : 0; return ctxId;

## Slide 6: Results (test 1)
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.18% | -0.01% | 102% | 99%
Class A2 | -0.06% | 0.00% | -0.08% | 102% | 100%
Class B | -0.02% | 0.06% | -0.01% | 99% | 101%
Class C | -0.03% | -0.05% | -0.11% | 98% | 96%
Class E |  |  |  |  | 
Overall | -0.05% | -0.03% | -0.05% | 100% | 99%
Class D | -0.01% | 0.06% | -0.05% | 96% | 96%
Class F | 0.01% | 0.01% | -0.02% | 101% | 95%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.12% | 0.18% | 102% | 96%
Class C | 0.03% | 0.12% | -0.12% | 99% | 109%
Class E | 0.00% | 0.03% | 0.02% | 102% | 100%
Overall | 0.01% | 0.10% | 0.04% | 101% | 101%
Class D | 0.05% | -0.18% | 0.53% | 94% | 98%
Class F | 0.03% | 0.55% | 0.19% | 103% | 99%

## Slide 7: Results (test 2)
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.09% | -0.03% | 101% | 101%
Class A2 | -0.04% | 0.07% | 0.00% | 101% | 100%
Class B | -0.01% | -0.09% | -0.13% | 99% | 105%
Class C | -0.03% | -0.15% | 0.01% | 97% | 93%
Class E |  |  |  |  | 
Overall | -0.03% | -0.07% | -0.05% | 99% | 100%
Class D | 0.00% | 0.15% | 0.23% | 97% | 94%
Class F | -0.01% | 0.10% | 0.00% | 100% | 110%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.28% | -0.09% | 98% | 90%
Class C | 0.06% | -0.07% | -0.05% | 98% | 100%
Class E | 0.05% | 0.08% | -0.31% | 100% | 125%
Overall | 0.03% | 0.11% | -0.13% | 99% | 101%
Class D | 0.04% | 0.13% | 0.73% | 94% | 90%
Class F | -0.08% | 0.17% | -0.63% | 99% | 119%

## Slide 8: Summary
It is proposed to clean-up the sub-block/affine flags coding
Parsing is simplified and some contexts are removed
Slight gains for higher classes
Thanks to Qualcomm for crosschecking.

## Slide 9: Thank you