## Slide 1: JVET-O0505 Non-CE9: Simplifying BDOF early termination related cost calculations
S. Sethuraman
Ittiam Systems

## Slide 2: Early termination for BDOF
Current method
  Sub-block level early termination with 4-per sample threshold
  4x4 level early termination with 8-per sample threshold
Drawbacks
  Performed between final MC samples from each reference
    Too late for gating the optical flow estimation related computations
  4x4 level SAD computations themselves increase the average EncT/DecT
Use of costs computed during DMVR for early termination were proposed at the last meeting and are studied in CE9-1
  At the last meeting, it was expressed that having some early termination for BDOF for the cases when DMVR is turned off at the SPS or lower level is preferable to get average DecT reduction for those cases as well
Hardware experts did not want a SAD execution unit dedicated to the BDOF pipeline stage

## Slide 3: Proposed solution
When current CU is eligible to perform both DMVR and BDOF,
  Use costs computed for DMVR using bilinear interpolated samples to perform early termination for BDOF
    Case when the delta MV falls on the boundary of the refinement range
      Use the evaluated SAD cost corresponding to that refinement position
    Case when parametric error surface based refined MV is obtained
      Compute a derived cost using the same parameteric error surface using the following:
        Where E(x,y) are the evaluated integer delta MV SAD costs, (x0, y0) corresponds to the sub-pixel accurate delta MV obtained using error surface
When current CU is not eligible to perform DMVR, but eligible to perform BDOF,
  Compute early termination cost using the integer grid reconstructed reference sample values closest to the desired sub-pixel accurate sample positions
  Compare against a threshold that is slightly higher than the threshold value used with DMVR cost (5 per sample instead of 4 per sample)

## Slide 4: Benefits
Bit-depth used is 10-bits and alternate row SAD is used to align with DMVR
No need for a dedicated SAD computation unit for BDOF
BDOF can be clock-gated in hardware based on cost computed in DMVR pipeline stage
  Average power reduction
Software implementations get almost the same savings as with earlier two-level early exit check

## Slide 5: Test-1
4x4 level early termination for BDOF is diabled
A small BDRATE gain is seen due to the disabling of the 4x4 level early termination
No appreciable change in DecT/EncT ratios (EncT reduces due to removal of 4x4 level early termination that is not optimized well currently)

## Slide 6: Test-2
In this test, the 4x4 early termination check is performed using the same set of samples used for performing the 16x16 early termination check
  DMVR + BDOF – Bilinear interpolated samples corresponding to refined MV (Threshold value – 8 per sample)
  BDOF-only – Integer grid reconstructed reference samples
A small BDRATE loss is seen; DecT/EncT are further reduced relative to VTM5
However, requires hardware execution units to support 4x4 level accumulation

## Slide 7: Conclusions
Use of integer grid reconstructed reference sample values for performing BDOF early termination is proposed when a current CU is not eligible to perform DMVR
  Facilitates re-use of DMVR cost computation units; eliminates need for any cost computation unit within BDOF pipeline stage
It uses CE9-1.5b path when a current CU is eligible to perform both DMVR and BDOF
Results indicate that there is a small BD-RATE impact with a good average decoding time reduction (on par with earlier 2-level early termination check)
  Additional average decoding time reduction in Test-2 with 4x4 level early termination
Allows saving average power as decision is known ahead of time in hardware
It is requested that this method be further studied in CE

## Slide 8: Thanks to KDDI for Cross-checking!