## Slide 1: Extensions to CCLM Reference Sample Filtering in CE3-3.2.1
JVET-O0510
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Steve Keating
Sony Corp.

## Slide 2: Introduction
CE3-3.2.1 tests filtering of chroma reference samples used in CCLM
The filtering was intended to remove outliers from the data
This filtering was originally proposed to be common between CCLM and LIC
The result of CE3-3.2.1 is a loss of 0.03%(Y), 0.32%(U), 0.39%(V) in AI

## Slide 3: Consideration for filtering 1
For small blocks the selected reference samples will be spatially close, maybe adjacent. Applying a low-pass filter to these will cause the values to be partially merged:
E.g., sample 1 and 2 will share data from the sample between them when the (1,2,1)/4 filter is applied. This makes the filtered samples less distinct which could compromise the calculation of alpha and beta.
1
2
3
4
Samples 1,2,3,4 are used for CCLM calculation

## Slide 4: Consideration for filtering 2
Only the chroma samples are filtered, this may give a poor correlation with luma.
Note that the luma samples are pre-filtered (to half bandwidth) before down-sampling (by a factor of 2). This just matches the 4:2:0 chroma samples.

## Slide 5: Proposal
The filtering should only be applied when the reference samples are sufficiently spaced to prevent merging.
  In this case when sample spacing is greater than 2
The luma samples should have the same filtering as the chroma samples.

## Slide 6: Results
Restricting the filtering according to sample spacing and applying the same filtering to luma samples removes the loss:

## Slide 7: Conclusion
If it is desirable to filter the CCLM reference samples (perhaps for common usage with LIC) then:
  Filtering should be restricted according to sample spacing
  Luma and chroma should have the same filtering
Thanks to Huawei for cross-checking