## Slide 1: Non CE3: Intra mode coding of non-MPM modes
Saverio Blasi, André Seixas Dias, Gosala Kulupana
15th JVET Meeting: Gothenburg, SE, 3–12 Jul. 2019
JVET-O0515

## Slide 2
Background
In current VVC draft, if an angular mode is not in the MPM list, its parsing still depends on the computation of the MPM list
An index intra_luma_mpm_remainder is parsed, which identifies one out of all the possible 61 “non-MPM” modes
Decoder logic is needed to go from intra_luma_mpm_remainder to IntraPredModeY:
  Computation of MPM list
  Sorting of MPM list
  Comparisons of intra_luma_mpm_remainder with each element in MPM list to recover the actual intra mode index

## Slide 3
Proposed method
It is proposed to remove this dependency
IntraPredModeY can be computed from intra_luma_mpm_remainder without computing and accessing the MPM list at all
An index intra_luma_mpm_remainder is parsed, which identifies one out of all the possible 65 angular modes (including MPMs)
  No need to compute MPM list for non-MPM modes
  No need for sorting the MPM list
  Logic (and 10 lines of decoder processing) removed from the specs
  Higher flexibility at the encoder side: an angular MPM mode can be encoded as “non-MPM” - fast implementations could be done which completely avoid computing MPMs

## Slide 4
Spec changes
The following changes to Clause 8.4.3 are proposed:
IntraPredModeY[ xCb ][ yCb ] is derived by applying the following procedure:
If intra_luma_mpm_flag[ xCb ][ yCb ] is equal to 1, the IntraPredModeY[ xCb ][ yCb ] is set equal to candModeList[ intra_luma_mpm_idx[ xCb ][ yCb ] ].
Otherwise, IntraPredModeY[ xCb ][ yCb ] is set equal to intra_luma_mpm_remainder[ xCb ][ yCb ] + 2
is derived by applying the following ordered steps:
When candModeList[ i ] is greater than candModeList[ j ] for i = 0..3 and for each i, j = ( i + 1 )..4, both values are swapped as follows:
( candModeList[ i ], candModeList[ j ] ) = Swap( candModeList[ i ], candModeList[ j ] ) (8‑48)
IntraPredModeY[ xCb ][ yCb ] is derived by the following ordered steps:
  IntraPredModeY[ xCb ][ yCb ] is set equal to intra_luma_mpm_remainder[ xCb ][ yCb ].
  The value of IntraPredModeY[ xCb ][ yCb ] is incremented by one two.
  For i equal to 0 to 4, inclusive, when IntraPredModeY[ xCb ][ yCb ] is greater than or equal to candModeList[ i ], the value of IntraPredModeY[ xCb ][ yCb ] is incremented by one.
intra_luma_mpm_remainder[ ][ ] | TB | cMax = 60 64

## Slide 5
Performance results
 |  |  | All Intra |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.10% | -0.02% | 99% | 100%
Class A2 | 0.03% | -0.07% | -0.02% | 99% | 100%
Class B | 0.05% | -0.03% | 0.02% | 99% | 97%
Class C | 0.05% | 0.02% | 0.03% | 100% | 105%
Class E | 0.06% | -0.02% | 0.06% | 99% | 99%
Overall | 0.04% | 0.00% | 0.01% | 99% | 100%
Class D | 0.05% | 0.14% | 0.02% | 101% | 100%
Class F |  |  |  |  | 
 |  |  | Random access |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05% | -0.04% | -0.11% | 99% | 98%
Class C | 0.02% | 0.00% | -0.10% | 100% | 98%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.02% | 0.32% | -0.09% | 100% | 102%
Class F |  |  |  |  | 

## Slide 6
Conclusion
A simple spec change is proposed, to remove the need to compute MPM list for parsing non-MPM modes
Decoder logic is highly simplified
Removal of specs
Less decoder complexity
Higher encoder flexibility (angular MPM mode could be encoded as “non-MPM”)
Marginal compression efficiency losses (0.04% luma BD-rate loss in AI, 0.0x% BD-rate loss in RA) with encoder and decoder complexity savings

## Slide 7: Thank you
www.bbc.co.uk/rd
saverio.blasi@bbc.co.uk
Email: