## Slide 1: Switching between CABAC context coded bins and EP coded bins
JVET-O0519
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Adrian Browne / Steve Keating / Karl Sharman
Sony Corp.

## Slide 2: Introduction – current design
cabac_zero_words are used to guarantee worst-case bit-stream.
  Essential for decoder design, so that worst-case situation is known.
  Threshold defined for maximum number of coded bins based on sum of:
    static quantity computed from picture dimensions and bit depth
    dynamic quantity computed from number of bytes in output stream
  If number of bins greater than threshold, cabac_zero_words are added
JVET-L0274 introduced limits (32 for 4×4, 8 for 2×2 sub-TU) for the number of CABAC coded bins for transform coefficients
JVET-N0280 introduced a limit (2 × block area) for the number of CABAC coded bins for transform skip
Neither of these limits can guarantee cabac_zero_words will not be required.

## Slide 3: Proposal
Modify entropy coding to dynamically switch from CABAC coded bins to EP coded bins
  Code with CABAC bin when this can be done within threshold
  Code with EP bin otherwise
Remove limits on number of CABAC bins introduced in JVET-L0274 and JVET-N0280
Remove cabac_zero_words process/syntax.

## Slide 4: Proposal (extension)
Modified proposal adds an alternative decision point at the beginning of transform unit coding.
  Use CABAC throughout TU coding if enough spare bins exist to code every coefficient in the TU.
  Use EP bins throughout if there is no guarantee threshold will be met
  No need to check threshold during coefficient coding.
Potential of adding similar decision points at other limited places
  e.g. CU, PU.
  Currently, outside TU coding, we revert to per-bin checks.

## Slide 5: Implementation
Original dynamic quantity imposes an effective ratio of 4 / 3 on the number of bins to bits in the data stream
Threshold implemented by counter:
  adds 4 for each bit appended to the data stream
    i.e. during renormalization process of CABAC, or during coding process of EP bins.
  subtracts 3 for each bin (EP, CABAC, TRM)
  initialised with 3× original static quantity of threshold (based on picture size and bit depth based).
Testing whether to use CABAC / EP
  For simple per-bin test, use EP bin when counter is less than 3.
  For extension, use EP bin when count is less than 3x{max bins to code in TU}

## Slide 6: Implementation

## Slide 7: Results
Little change in CTC but gains for classes A and F for low QP
No cabac_zero_word padding required
Almost identical results for extension scheme.
 | AI |  |  |  | 
 | Over VTM5.0-LOWQP |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.42% | -0.60% | -0.63% | 104% | 105%
Class A2 | -0.39% | -0.58% | -0.58% | 104% | 107%
Class B | -0.06% | -0.12% | -0.16% | 103% | 106%
Class C | 0.05% | -0.03% | -0.04% | 106% | 107%
Class E | 0.02% | -0.12% | -0.14% | 102% | 104%
Overall | -0.14% | -0.26% | -0.28% | 104% | 106%
Class D | 0.03% | -0.05% | -0.03% | 102% | 104%
Class F | -0.81% | -0.75% | -0.76% | 102% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over VTM5.0-LOWQP |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.39% | -0.59% | -0.57% | 99% | 100%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.35% | -0.53% | -0.59% | 101% | 102%
Class C | -0.25% | -0.40% | -0.36% | 101% | 103%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.25% | -0.34% | -0.36% | 102% | 103%
Class F | -3.42% | -0.70% | -0.78% | 101% | 101%
 |  |  | AI |  | 
 |  |  | Over VTM |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.10% | -0.02% | 102% | 101%
Class A2 | -0.02% | -0.08% | -0.07% | 99% | 100%
Class B | -0.02% | -0.15% | -0.02% | 100% | 101%
Class C | -0.06% | -0.14% | -0.09% | 100% | 101%
Class E | -0.04% | -0.09% | -0.09% | 99% | 100%
Overall | -0.03% | -0.08% | -0.05% | 100% | 101%
Class D | -0.06% | 0.05% | -0.12% | 100% | 101%
Class F | -0.25% | -0.20% | -0.33% | 102% | 101%
 |  |  | RA |  | 
 |  |  | Over VTM |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.34% | 0.04% | 100% | 100%
Class A2 | 0.00% | -0.04% | -0.04% | 99% | 99%
Class B | 0.00% | -0.08% | -0.19% | 100% | 100%
Class C | -0.05% | -0.23% | -0.14% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.16% | -0.10% | 100% | 100%
Class D | 0.00% | -0.09% | 0.04% | 100% | 100%
Class F | -0.29% | -0.27% | -0.02% | 100% | 100%

## Slide 8: Conclusion
Proposed a modification to the entropy encoder
  Introduces a counter
  Dynamically manages bit / bin ratio ensuring threshold met
  Allows simplification of coefficient coding
  Removes need for cabac_zero_word
No net loss across RA/AI for CTC
BD-rate improvements for RA/AI for low QP
Thanks to Qualcomm for offering to cross-check this contribution.