## Slide 1: JVET-O0534 Non-CE4: Redundancy removal for merge mode signaling
Jing Ye, Xiang Li, and Shan Liu
07/2019

## Slide 2: Introduction
First, the current syntax has some redundancies in signaling the merge mode.
  In current VVC, there are some constraints for merge mode, however, in the current signaling syntax, there isn’t redundancy check for those constrains.
  For example, when Triangle mode is not allowed and regular merge mode, subblock merge mode both are false, it is inferred to be CIIP mode, and it is not necessary to signal it. However, the current syntax still signals that flag.
Second, the current syntax can break in some cases.
  For example, when triangle is not allowed, but all the other modes are all false. In this case, there is no merge mode.

## Slide 3: Proposed method
It is proposed to remove the redundancies.
  Define the conditions of signaling
    allowRegularMerge = MaxNumMergeCand > 0
    allowMMVD = sps_mmvd_enabled_flag
    allowSubMerge = MaxNumSubblockMergeCand>0 && cbWidth>=8 && cbHeight>=8
    allowCIIP = sps_ciip_enabled_flag && !cu_skip_flag && cbWidth*cbHeight >= 64 && cbWidth<128 && cbHeight<128
    allowTriangle = sps_triangle_enabled_flag && slice_type == B && MaxNumTriangleMergeCand >= 2 && cbWidth * cbHeight >=64
  Check the conditions when signaling merge flag

## Slide 4: Text changes
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if ( CuPredMode[ x0 ][ y0 ] = = MODE_IBC ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_mmvd_enabled_flag ¦ ¦ cbWidth * cbHeight != 32 allowRegularMerge&&(allowMMVD ¦ ¦ allowSubMerge ¦ ¦ allowCIIP ¦ ¦ allowTriangle ) ) | 
regular_merge_flag[ x0 ][ y0 ] | ae(v)
if ( regular_merge_flag[ x0 ][ y0 ] = = 1 ){ | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_mmvd_enabled_flag && cbWidth * cbHeight != 32 allowMMVD &&( allowSubMerge ¦ ¦ allowCIIP ¦ ¦ allowTriangle) ) | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
if( mmvd_merge_flag[ x0 ][ y0 ] = = 1 ) { | 
… | ae(v)
} else { | 
if( MaxNumSubblockMergeCand > 0 && cbWidth >= 8 && cbHeight >= 8 allowSubMerge && (allowCIIP ¦ ¦ allowTriangle) ) | 
merge_subblock_flag[ x0 ][ y0 ] | ae(v)
if( merge_subblock_flag[ x0 ][ y0 ] = = 1 ) { | 
if( MaxNumSubblockMergeCand > 1 ) | 
merge_subblock_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 allowCIIP && allowTriangle ) { | 
ciip_flag[ x0 ][ y0 ] | ae(v)
if( ciip_flag[ x0 ][ y0 ] && MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} | 
… | 
} | 
} | 
} | 
} | 
} | 

## Slide 5: Simulation results (1)
CTC with LP results

## Slide 6: Simulation results (2)
Non-CTC case: triangle merge mode is disabled for slices with temporal level 0 and 1 by setting MaxNumTriangleMergeCand to 0 at related slice headers.

## Slide 7: Conclusions
The proposed method removes the redundancy in signaling merge mode
The proposed method fixes a bug in the syntax
It is recommended to adopt the proposed method
Thanks LGE for crosschecking

## Slide 8: Thank you!