## Slide 1: JVET-O0619: Non-CE7: Simplification of transform skip residual coding
Mohammed Golam Sarwer, Yan Ye(Alibaba)

## Slide 2: Problem statements
Major differences between transform and transform skip residual coding
Tools | Transform | Transform-skip
Scanning order | Reverse | Forward
Number of coding passes | 3 | 6
By-pass coded | In worst case, to check availability of context coded bin, 1 comparison/coefficient | In worst case, to check availability of context coded bin, 8 comparisons/coefficient

## Slide 3: Problem statements : by-pass coding
Transform residual coding
Transform skip (TS) residual coding
An illustration of by-pass coding: Left – transform residual coding, Right- transform skip residual coding

## Slide 4: Proposed method : Reverse scan
Both transform and transform skip residuals use reverse scanning order.

## Slide 5
Two methods are proposed:
Pass 1: following flags are signalled
  sig_coeff_flag
  coeff_sign_flag
  greater 1 flag (abs_level_gtx_flag[0])
  parity (par_level_flag) flag
Pass 2: following flags are signalled
  abs_level_gtx_flag[1]
  abs_level_gtx_flag[2]
  abs_level_gtx_flag[3]
  abs_level_gtx_flag[4]
Pass 3: by-pass coding (abs_remainder)
Pass 1: following flags are signalled
  sig_coeff_flag
  coeff_sign_flag
  greater 1 flag (abs_level_gtx_flag[0])
  abs_level_gtx_flag[1]
Pass 2: following flags are signalled
  parity (par_level_flag) flag
  abs_level_gtx_flag[2]
  abs_level_gtx_flag[3]
  abs_level_gtx_flag[4]
Pass 3: by-pass coding (abs_remainder)
Method 1
Method 2
Proposed method : coding pass reduction

## Slide 6
Proposed method : Unified by-pass coding
An illustration of the proposed by-pass coding method of TS residual coding

## Slide 7
Proposed method : Unified by-pass coding
Implemented on top of method 1:

## Slide 8: Simulation results
Test 1: reverse scanning order
Test 2: forward scanning + coding pass reduction– Method 1
Test 3: forward scanning + coding pass reduction– Method 2
Test 4: Test 2 + unified by-pass coding

## Slide 9: Simulation results
Test 1: reverse scanning order
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.01% | 0.02% | 99% | 99%
Class A2 | 0.01% | -0.01% | -0.03% | 99% | 99%
Class B | 0.03% | -0.02% | 0.04% | 99% | 99%
Class C | 0.08% | 0.03% | 0.11% | 100% | 99%
Class E | 0.06% | 0.07% | 0.03% | 99% | 99%
Overall | 0.04% | 0.01% | 0.04% | 99% | 99%
Class D | 0.09% | 0.34% | 0.11% | 99% | 98%
Class F | 0.25% | 0.16% | 0.16% | 99% | 99%
TGM | 0.31% | 0.27% | 0.24% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.08% | 0.11% | 99% | 100%
Class A2 | 0.01% | 0.08% | 0.08% | 99% | 99%
Class B | 0.00% | 0.02% | -0.19% | 99% | 99%
Class C | 0.00% | -0.29% | -0.38% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.07% | -0.13% | 99% | 99%
Class D | 0.04% | 0.14% | 0.02% | 99% | 98%
Class F | 0.17% | 0.14% | 0.23% | 99% | 99%
TGM | 0.13% | 0.13% | 0.04% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.21% | 0.20% | 0.05% | 100% | 100%
TGM | 0.14% | 0.13% | 0.05% | 100% | 100%

## Slide 10: Simulation results
Test 2: forward scanning + coding pass reduction – Method 1
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | -0.04% | 99% | 99%
Class A2 | 0.00% | 0.00% | 0.00% | 99% | 99%
Class B | 0.00% | 0.02% | 0.00% | 99% | 99%
Class C | 0.00% | -0.01% | 0.01% | 99% | 99%
Class E | 0.00% | 0.01% | -0.04% | 99% | 99%
Overall | 0.00% | 0.01% | -0.01% | 99% | 99%
Class D | 0.00% | 0.01% | -0.08% | 98% | 98%
Class F | 0.00% | -0.03% | 0.02% | 99% | 99%
TGM | 0.01% | 0.01% | 0.01% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.03% | 100% | 99%
Class A2 | 0.01% | 0.00% | -0.01% | 100% | 99%
Class B | 0.01% | 0.05% | -0.06% | 99% | 99%
Class C | -0.03% | -0.22% | -0.09% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.04% | -0.05% | 99% | 99%
Class D | 0.05% | -0.02% | 0.18% | 99% | 98%
Class F | -0.01% | -0.17% | 0.08% | 99% | 99%
TGM | -0.09% | -0.02% | -0.05% | 100% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.03% | -0.23% | -0.48% | 100% | 100%
TGM | 0.04% | 0.01% | 0.09% | 100% | 99%

## Slide 11: Simulation results
Test 3: forward scanning + coding pass reduction – Method 2
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | -0.01% | 99% | 99%
Class A2 | 0.00% | -0.01% | -0.01% | 99% | 99%
Class B | 0.00% | 0.01% | -0.01% | 99% | 99%
Class C | 0.00% | 0.02% | -0.01% | 99% | 99%
Class E | 0.00% | 0.04% | 0.04% | 100% | 99%
Overall | 0.00% | 0.02% | 0.00% | 99% | 99%
Class D | -0.01% | 0.07% | -0.13% | 98% | 98%
Class F | -0.04% | 0.09% | 0.13% | 99% | 99%
TGM | -0.04% | -0.01% | 0.00% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | 0.01% | 99% | 99%
Class A2 | 0.00% | 0.15% | 0.08% | 99% | 99%
Class B | 0.00% | 0.00% | -0.04% | 99% | 99%
Class C | -0.04% | -0.21% | -0.22% | 99% | 99%
Class E |  |  |  |  | 
Overall | -0.01% | -0.03% | -0.06% | 99% | 99%
Class D | 0.01% | -0.05% | -0.13% | 99% | 97%
Class F | -0.01% | -0.04% | 0.19% | 99% | 99%
TGM | 0.00% | 0.04% | -0.09% | 99% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.05% | -0.10% | -0.16% | 100% | 100%
TGM | 0.09% | 0.07% | 0.16% | 100% | 99%

## Slide 12: Simulation results
Test 4: Test 2 + unified by-pass coding
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | 0.00% | 99% | 100%
Class A2 | 0.00% | 0.01% | -0.01% | 99% | 99%
Class B | 0.00% | -0.01% | 0.02% | 99% | 100%
Class C | 0.02% | 0.00% | 0.03% | 99% | 99%
Class E | 0.00% | 0.06% | 0.03% | 99% | 99%
Overall | 0.00% | 0.01% | 0.01% | 99% | 99%
Class D | 0.02% | 0.12% | -0.01% | 99% | 97%
Class F | 0.14% | 0.12% | 0.20% | 99% | 99%
TGM | 0.34% | 0.30% | 0.30% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | 0.04% | 99% | 100%
Class A2 | 0.01% | -0.08% | 0.06% | 99% | 99%
Class B | 0.00% | -0.02% | -0.22% | 99% | 100%
Class C | -0.03% | -0.13% | -0.06% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.05% | -0.07% | 99% | 99%
Class D | 0.00% | 0.17% | 0.20% | 99% | 98%
Class F | 0.11% | 0.09% | 0.14% | 99% | 99%
TGM | 0.15% | 0.23% | 0.12% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0.03% | -0.09% | -0.28% | 100% | 100%
TGM | 0.07% | 0.04% | 0.09% | 99% | 100%

## Slide 13: Conclusions
Reverse scanning order ( test 1):
    0.04% (AI) and 0.00% luma BD-rate of CTC sequences
    0.31% (AI) and 0.13% luma BD-rate of TGM sequences
Coding pass reduction:
  Method 1 (test 2):
    0.00% (AI) and 0.00% luma BD-rate of CTC sequences
    0.01% (AI) and -0.09% luma BD-rate of TGM sequences
  Method 2 (test 3):
    0.00% (AI) and -0.01% luma BD-rate of CTC sequences
    -0.04% (AI) and 0.00% luma BD-rate of TGM sequences
Coding pass reduction + unification (test 4):
    0.00% (AI) and 0.00% luma BD-rate of CTC sequences
    0.34% (AI) and 0.15% luma BD-rate of TGM sequences