## Slide 1: Cross-Component Adaptive Loop Filter for chroma (JVET-O0636)
K. Misra, F. Bossen, A. Segall (Sharp Labs of America)

## Slide 2: Overview
Overview
  Description of Cross Component ALF (CC-ALF)
    Sample operations
    Signaling
  Experimental Results
  Summary

## Slide 3: Cross-component Adaptive Loop Filter (CC-ALF)
Cross-component Adaptive Loop Filter
  Generates improvement of chroma channel from filtered version of the luma channel
  Operates in parallel with the existing luma ALF operation
  Motivation: Luma may contain details that are lost in chroma inside the coding loop

## Slide 4: Description of CCALF
CC-ALF
Uses luma sample values as input
Applies a linear filter operation
Outputs a correction value for each chroma sample

## Slide 5: Diamond shaped filter
Filter
One filter per color component
Each coefficient is scaled by 210 and rounded for fixed point representation
Uses same coefficient derivation functions as in VTM5

## Slide 6: Application of control mask
Local Control
  CC-ALF is enabled/disabled on a block basis
  Block size is signaled in the bit-stream (slice header)

## Slide 7: Example Improvement

## Slide 8
Signaling

## Slide 9: Slice Header Syntax Changes
slice_header( ) { | Descriptor
… | 
if( sps_cross_component_alf_enabled_flag ) { | 
slice_cross_component_alf_cb_enabled_flag | u(1)
if( slice_cross_component_alf_cb_enabled_flag ) { | 
slice_cross_component_alf_cb_reuse_temporal_layer_filter | u(1)
if (!slice_cross_component_alf_cb_reuse_temporal_layer_filter) | 
slice_cross_component_alf_cb_aps_id | u(5)
slice_cross_component_alf_cb_log2_control_size_minus4 | ue(v)
} | 
slice_cross_component_alf_cr_enabled_flag | u(1)
if( slice_cross_component_alf_cr_enabled_flag ) { | 
slice_cross_component_alf_ct_reuse_temporal_layer_filter | u(1)
if (!slice_cross_component_alf_cr_reuse_temporal_layer_filter) | 
slice_cross_component_alf_cr_aps_id | u(5)
slice_cross_component_alf_cr_log2_control_size_minus4 | ue(v)
} | 
} | 
… | 
} | 

## Slide 10: APS Syntax Changes
alf_data( adaptation_parameter_set_id ) { | Descriptor
… | 
if (sps_cross_component_alf_enabled_flag) { | 
alf_cross_component_cb_filter_signal_flag | u(1)
alf_cross_component_cr_filter_signal_flag | u(1)
} | 
if( alf_luma_filter_signal_flag ) { | 
… | 
} | 
if( alf_chroma_filter_signal_flag ) { | 
… | 
} | 
if( alf_cross_component_cb_filter_signal_flag ) { | 
alf_cross_component_cb_min_eg_order_minus1 | ue(v)
for( i = 0; i < 3; i++ ) | 
alf_cross_component_cb_eg_order_increase_flag[ i ] | u(1)
for ( j = 0; j < 14; j++ ) { | 
alf_cross_component_cb_coeff_abs[ j ] | uek(v)
if( alf_cross_component_cb_coeff_abs[ j ] ) | 
alf_cross_component_cb_coeff_sign[ j ] | u(1)
} | 
} | 
if( alf_cross_component_cr_filter_signal_flag ) { | 
alf_cross_component_cr_min_eg_order_minus1 | ue(v)
for( i = 0; i < 3; i++ ) | 
alf_cross_component_cr_eg_order_increase_flag[ i ] | u(1)
for ( j = 0; j < 14; j++ ) { | 
alf_cross_component_cr_coeff_abs[ j ] | uek(v)
if( alf_cross_component_cr_coeff_abs[ j ] ) | 
alf_cross_component_cr_coeff_sign[ j ] | u(1)
} | 
} | 
} | 

## Slide 11
Results

## Slide 12: Experimental Results
CTC Results
  Average gains in chroma of:
    AI: 7.6%
    RA: 13.8%
    LDB: 17.8%
  Negligible increase in encoder run-time (2-3%)
  5-10% increase in decoder run-time
    Likely due to non-vectorized implementation
 |  |  | All Intra Main10 |  | 
 |  |  | Over |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.08% | -3.66% | -4.62% | 103% | 105%
Class A2 | 0.12% | -8.98% | -9.46% | 103% | 105%
Class B | 0.10% | -11.49% | -9.68% | 102% | 105%
Class C | 0.14% | -5.15% | -4.59% | 102% | 104%
Class E | 0.21% | -12.58% | -3.59% | 102% | 104%
Overall | 0.13% | -8.54% | -6.65% | 102% | 105%
Class D | 0.16% | -3.91% | -4.28% | 101% | 101%
Class F | 0.23% | -7.64% | -7.99% | 102% | 102%
 |  |  | Random access Main10 |  | 
 |  |  | Over |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.16% | -8.96% | -7.59% | 103% | 106%
Class A2 | 0.09% | -14.72% | -19.43% | 103% | 108%
Class B | 0.24% | -23.01% | -18.32% | 104% | 106%
Class C | 0.13% | -7.34% | -6.18% | 102% | 103%
Class E |  |  |  |  | 
Overall | 0.16% | -14.36% | -13.16% | 103% | 105%
Class D | 0.14% | -6.69% | -5.38% | 103% | 102%
Class F | 0.30% | -7.80% | -7.45% | 104% | 103%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.20% | -26.96% | -24.33% | 102% | 115%
Class C | 0.24% | -10.68% | -8.72% | 105% | 108%
Class E | 0.21% | -21.27% | -9.37% | 107% | 102%
Overall | 0.21% | -20.11% | -15.39% | 104% | 109%
Class D | 0.17% | -11.09% | -6.98% | 104% | 105%
Class F | 0.36% | -14.15% | -12.35% | 105% | 110%

## Slide 13: Experimental Results
Supplemental Results
  Shift of gains from chroma to luma
  Initial results (proof of concept)
  Luma gains of:
    AI: .93%
    RA: .95%
 |  |  | All Intra Main10 |  | 
 |  |  | Over |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.20% | 7.35% | 4.69% | 103% | 105%
Class A2 | -1.88% | 0.69% | 0.29% | 101% | 104%
Class B | -0.72% | -1.67% | 0.34% | 102% | 104%
Class C | -0.67% | 3.48% | 4.01% | 101% | 103%
Class E | -0.41% | -4.99% | 4.37% | 102% | 103%
Overall | -0.93% | 0.82% | 2.55% | 102% | 104%
Class D | -0.62% | 4.57% | 4.35% | 101% | 101%
Class F | -0.62% | -1.09% | -1.57% | 101% | 102%
 |  |  | Random access Main10 |  | 
 |  |  | Over |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.43% | -0.26% | 0.64% | 101% | 106%
Class A2 | -1.88% | -5.91% | -11.28% | 101% | 106%
Class B | -0.36% | -13.10% | -8.01% | 102% | 105%
Class C | -0.64% | 1.98% | 3.67% | 102% | 103%
Class E |  |  |  |  | 
Overall | -0.95% | -5.07% | -3.82% | 102% | 105%
Class D | -0.53% | 2.99% | 4.42% | 103% | 102%
Class F | -0.69% | -1.53% | -1.17% | 103% | 103%

## Slide 14: Recommendations
Summary
  Proposed Cross-Component Adaptive Loop Filter
  Operates in parallel to luma ALF
  Predicts correction for chroma channel from filtered luma samples
  Average chroma gains of 7.6%, 13.8% or 17.8% (for AI, RA, LDB)
  Thanks to Canon for cross-check
Propose formal study in Core Experiment

## Slide 16: Application of control mask
Picture with CTU boundaries
Derive 32x32 control mask ( gray is OFF, green is ON )
Samples that are filtered
x
Block size of mask is signaled in slice header