## Slide 1: Non-CE5: On chroma line selection for gradient computation in deblocking (JVET-O0637)
K. Misra, P. Cowan, A. Segall (Sharp Labs of America)
Y. Morigami, M. Ikeda, T. Suzuki (Sony Corp)

## Slide 2: Overview
Background and Motivation
Proposed Solution
Experimental Results
Recommendations

## Slide 3: Background (VVC WD5) – Issue 1
When luma and chroma dimension match, as in example shown to left:
Gradient is computed for line 0 and line 3 in luma but at line 0 and line 1 in chroma
4:4:4

## Slide 4: Proposal 1
When Chroma is same size as luma (along a dimension), compute chroma gradient for line 0 and line 3 (same as luma)

## Slide 5: Background (VVC WD5) – Issue 2
When SubHeightC = 2
(4:2:0)
In worst case, chroma gradient is computed for every line, whereas luma gradient is computed twice every four lines
When SubWidthC = 2
(4:2:0, 4:2:2)

## Slide 6: Proposal 2
When Chroma is one-half the size of luma (along a dimension), compute gradient for line 0 only, to reduce worst case gradient computation

## Slide 7: Proposed Chroma Line Selection
4:2:0
4:2:2
4:4:4

## Slide 8: 4:2:0 Objective impact
The BD-Rate number for Y/U/V reportedly shows:
0.00%/ 0.09%/ 0.10% at AI, 0.00%/ 0.11%/ 0.12% at RA, 0.00%/ 0.18%/-0.03% at LDB and 0.01%/ 0.15%/ 0.03% at LDP over VTM-5.0 with ALF switched on
The BD-Rate results for Y/U/V reportedly shows:
-0.01%/ 0.06%/ 0.06% at AI, -0.01%/ 0.14%/ 0.14% at RA, 0.01%/-0.02%/-0.33% at LDB and 0.02%/-0.14%/-0.13% at LDP over VTM-5.0 with ALF switched off

## Slide 9: 4:4:4 and 4:2:2 Objective impact
Thank You LGE and Huawei for crosscheck. WD changes provided with contribution
The BD-Rate number for 4:4:4 RGB reportedly shows:
0.00%/ 0.00%/ 0.00% at AI, x.xx%/ x.xx%/ x.xx% at RA, x.xx%/ x.xx%/ x.xx% at LDB
The BD-Rate results for 4:4:4 YUV reportedly shows:
0.00%/-0.04%/-0.05% at AI, -0.01%/-0.02%/-0.03% at RA, x.xx%/ x.xx%/ x.xx% at LDB
The BD-Rate results for 4:2:2 YUV reportedly shows:
0.00%/ 0.02%/ 0.01% at AI, 0.01%/ 0.01%/ 0.01% at RA, x.xx%/ x.xx%/ x.xx% at LDB

## Slide 10: Recommendation
It is recommended that the approach be adopted in the next version of the VVC Draft and VTM.