## Slide 1: JVET-O0641 AHG 8: JVET Common test conditions for adaptive resolution change
Mohammed Golam Sarwer, Ruling Liao, Jie Chen, Daniel Luo, Yan Ye(Alibaba)

## Slide 2: Introduction
Supporting ARC with high coding efficiency is very important for video conferencing applications.
In order to evaluate different ARC-related coding technology proposals, the first step should be defining common test conditions,
This contribution proposes common test conditions for ARC.

## Slide 3: Proposed test conditions
Sequences
  Class B, C, and E (Mandatory)
  Class D, F (Optional)
Configurations
  LDB (Mandatory)
  LDP (Optional)
  Resolution change switch the resolution multiple times, and include both upscaling and downscaling in the test conditions.

## Slide 4: Proposed test conditions
Resampling ratio
  Straightforward scaling ratios such as 2:1 or 1:2, and 1.5:1 or 1:1.5.
  The same scaling ratio in both dimensions.

## Slide 5: Test pipeline
PSNR computations
const int srcDownSampleFilter[8][13] =
{
{0, 0, 5, -6, -10, 37, 76, 37, -10, -6, 5, 0, 0},
{0, -1, 5, -3, -12, 29, 75, 45, -7, -8, 5, 0, 0},
{0, -1, 4, -1, -13, 22, 73, 52, -3, -10, 4, 1, 0},
{0, -1, 4, 1, -13, 14, 70, 59, 2, -12, 3, 2, -1},
{0, -1, 3, 2, -13, 8, 65, 65, 8, -13, 2, 3, -1},
{0, -1, 2, 3, -12, 2, 59, 70, 14, -13, 1, 4, -1},
{0, 0, 1, 4, -10, -3, 52, 73, 22, -13,-1, 4, -1},
{0, 0, 0, 5, -8, -7, 45, 75, 29, -12,-3, 5, -1}
};
Const int upSampleFilter[16][8] =
{
{ 0, 0, 0, 64, 0, 0, 0, 0 },
{ 0, 1, -3, 63, 4, -2, 1, 0 },
{ -1, 2, -5, 62, 8, -3, 1, 0 },
{ -1, 3, -8, 60, 13, -4, 1, 0 },
{ -1, 4, -10, 58, 17, -5, 1, 0 },
{ -1, 4, -11, 52, 26, -8, 3, -1 },
{ -1, 3, -9, 47, 31, -10, 4, -1 },
{ -1, 4, -11, 45, 34, -10, 4, -1 },
{ -1, 4, -11, 40, 40, -11, 4, -1 },
{ -1, 4, -10, 34, 45, -11, 4, -1 },
{ -1, 4, -10, 31, 47, -9, 3, 1 },
{ -1, 3, -8, 26, 52, -11, 4, -1 },
{ 0, 1, -5, 17, 58, -10, 4, -1 },
{ 0, 1, -4, 13, 60, -8, 3, -1 },
{ 0, 1, -3, 8, 62, -5, 2, -1 },
{ 0, 1, -2, 4, 63, -3, 1, 0 }
};

## Slide 6: Block-based vs. picture-based resampling
 | Picture-based | Block-based
Pros | Resampling before decoding and no/little need for block-level changes | On-the-fly resampling, only resample when needed Can combine the filtering process of resampling and MC
Cons | Increase memory footprint When reference picture is downsampled, information of some samples is lost before current picture is decoded (this is the same for block-based if MC and resampling filtering is performed separately) | Block level changes are needed Some tools need to be modified or disabled Increase the block area to be fetched from the reference picture when downsampling the reference Interpolation filter phases could change per sample position in the block when the filtering process of resampling and MC is combined For encoder, motion search could become more complicated if combined MC/resampling filtering is used

## Slide 7
Anchor: VTM5.0 with TMVP, SbTMVP and affine mode turned off.
Test 1: The collocated picture is set to the first reference picture in L0. When the resolution of first reference picture in L0 is not the same as that of current picture, TMVP is disabled.
Test 2: The collocated picture is set to the first reference picture in L0 whose resolution is the same as that of current picture. If all reference pictures have different resolution from the current one, TMVP is disabled.
Test 3: motion field of a reference picture with different resolution is resampled in the same way as in SHVC. TMVP is performed without any further changes to VVC draft 5.
Preliminary results on picture-based resampling

## Slide 8
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.81% | -3.64% | -3.82% | 125% | 106%
Class C | -3.03% | -2.22% | -2.68% | 116% | 103%
Class E | -4.31% | -3.01% | -2.72% | 129% | 102%
Overall | -4.09% | -3.01% | -3.16% | 123% | 104%
Class D | -3.92% | -2.98% | -2.41% | 113% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.81% | -3.64% | -3.82% | 125% | 106%
Class C | -3.03% | -2.22% | -2.68% | 116% | 103%
Class E | -4.31% | -3.01% | -2.72% | 129% | 102%
Overall | -4.09% | -3.01% | -3.16% | 123% | 104%
Class D | -3.92% | -2.98% | -2.41% | 113% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.81% | -3.82% | -3.61% | 124% | 106%
Class C | -3.03% | -2.27% | -2.65% | 115% | 103%
Class E | -4.40% | -3.03% | -2.81% | 128% | 103%
Overall | -4.11% | -3.11% | -3.09% | 122% | 104%
Class D | -3.91% | -2.48% | -2.74% | 111% | 101%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Preliminary results on picture-based resampling
Test 1 (PSNR1)
Test 2 (PSNR1)
Test 3 (PSNR1)

## Slide 9
Preliminary results on picture-based resampling
Test 1 (PSNR2)
Test 2 (PSNR2)
Test 3 (PSNR2)
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.98% | -3.77% | -3.92% | 125% | 106%
Class C | -3.21% | -2.28% | -2.78% | 116% | 102%
Class E | -4.55% | -3.00% | -2.77% | 130% | 103%
Overall | -4.28% | -3.08% | -3.25% | 123% | 104%
Class D | -4.13% | -3.03% | -2.40% | 113% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.98% | -3.77% | -3.92% | 125% | 106%
Class C | -3.21% | -2.28% | -2.78% | 116% | 102%
Class E | -4.55% | -3.00% | -2.77% | 130% | 103%
Overall | -4.28% | -3.08% | -3.25% | 123% | 104%
Class D | -4.13% | -3.03% | -2.40% | 113% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.98% | -3.93% | -3.71% | 125% | 106%
Class C | -3.21% | -2.32% | -2.76% | 116% | 103%
Class E | -4.54% | -3.02% | -2.83% | 130% | 103%
Overall | -4.28% | -3.16% | -3.18% | 123% | 104%
Class D | -4.13% | -2.61% | -2.74% | 113% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 10: Discussion
Selection of resampling ratios: the same resampling ratios for all sequences, or adjust the resampling ratios according to the input video resolution?
Selection of resampling time instances: For example, the input 10-second video may be partitioned into 3 equal chunks (3.3 seconds per chunk), and downsampled at the start of the second chunk and upsampled at the start of the third chunk.
Selection of PSNR computation method(s): include using just one of the two PSNR computation methods, or using both of them?
This contribution further suggests to test both modes of resampling, i.e. picture-based and block-based, in a core experiment before selecting the solution that offers better performance vs. complexity trade-off.