## Slide 1: JVET-O0656 Non-CE5: Boundary strength derivation for transform skipped block
Shunsuke Iwamura, NHK

## Slide 2: Current derivation process of bS
Conditions | bS
At least one of the adjacent blocks is intra | 2
At least one of the adjacent blocks has non-zero transform coefficients | 1
Absolute difference between the motion vectors that belong to the adjacent blocks is greater that or equal to one integer luma sample | 1
Motion prediction in the adjacent blocks refers to vectors is different | 1
Otherwise | 0
Skip
Skip
Skip
Skip
Non-zero
Skip
Skip/
Non-zero
Intra
bS=2
bS=1
bS=0
JVET-O0656

## Slide 3
Skip
Skip
Reference picture
Reconstruction
Current picture
Both skipped case
bS=0
Both of the blocks near the boundary are skipped,
No discontinuity on the reconstruction might be observed.
JVET-O0656

## Slide 4
Skip
Non-zero
Reference picture
Reconstruction
Current picture
Skipped + Non-zero case
bS=1
At least one of the blocks near the boundary has non-zero coeffs, residual energy might be distributed in a whole block by applying inverse transform, which may cause discontinuity.

## Slide 5
Skip
Transformskipped
Reference picture
Reconstruction
Current picture
Skipped + Transform skipped case
bS=1
One of the blocks near the boundary is skipped and the other is transform-skipped, residual energy is not distributed in a whole block since inverse transform is not applied, however, boundary filter is applied to the boundary
JVET-O0656

## Slide 6
non-zero
skip
TS
TS
non-zero
non-zero
TS
skip
bS=1
bS=0
TS
non-zero
skip
skip
At least one of the adjacent blocks satisfies both of the following conditions
  The block has non-zero transform coefficients
  The block is not transform-skipped block
Proposed modification
JVET-O0656

## Slide 7
 |  |  | RA |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.02% | 100% | 100%
Class A2 | 0.01% | -0.02% | 0.03% | 100% | 99%
Class B | 0.01% | 0.07% | 0.02% | 100% | 101%
Class C | -0.03% | -0.04% | -0.09% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.02% | 100% | 100%
Class D | 0.00% | 0.13% | 0.06% | 100% | 100%
Class F | -0.02% | 0.08% | 0.03% | 100% | 101%
 |  |  | LB |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | 0.14% | 0.11% | 100% | 100%
Class C | 0.04% | 0.05% | -0.01% | 100% | 103%
Class E | 0.02% | -0.28% | -0.32% | 100% | 102%
Overall | 0.01% | 0.01% | -0.04% | 100% | 101%
Class D | -0.04% | 0.21% | 0.57% | 100% | 100%
Class F | 0.00% | -0.75% | -0.81% | 100% | 101%
Transform-skipped block
Over-smoothed
Simulation results
Thanks Sony for crosschecking
JVET-O0656