## Slide 1: JVET-O0662: Non-CE5: Modified ALF filtering for Slice, Brick and Virtual Boundaries
Anand Meher Kotra, Semih Esenlik, Biao Wang, Han Gao, Elena Alshina

## Slide 2: VTM-5.0 ALF design at different boundaries
All the following boundaries are handled as picture boundaries in the current ALF design when filtering is chosen to be turned off across
  Slice boundaries
  Tile/Brick boundaries
  360 video virtual boundaries
  For picture boundaries samples are just padded “outwards” and ALF is operated without any further changes
ALF virtual boundaries
  Modified block classification (re-scaled activity value) calculation and symmetric padding is used during ALF filtering
  Main motivation here is better objective and subjective quality

## Slide 3: ALF virtual boundary processing
Modified block classification at virtual boundaries
Modified ALF filtering for Luma component at virtual boundaries

## Slide 4: Subjective analysis from JVET-N meeting
Picture boundary handling (one-side padding)
ALF virtual boundary processing mechanism

## Slide 5: Our proposal
Use “ALF virtual boundary processing method” also for Slice/Tile/Brick boundaries as they are located “inside a given picture”
Advantage:
Better subjective quality when filtering across Slices/ Tiles/ Bricks is chosen to be turned off.

## Slide 6: Conclusion
Propose to use ALF virtual boundary processing mechanism when filtering is turned off at Slice/Tile/Brick boundaries as they occur inside a given picture
No BD-Rate changes expected in CTC conditions
Specification text changes are attached along with the contribution
Suggest to test this proposal in a core experiment with “well defined test conditions (non-CTC)”

## Slide 7
Thank You
www.huawei.com