## Slide 1: JVET-O0669 Non-CE5: A Simplification of ALF Coefficient Signalling
Hilmi E. Egilmez, Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: VTM-5.0 – Signaling in ALF
ALF coefficients for luma can be
  Signalled directly
  Signalled after prediction
Two mechanisms for prediction
  Prediction based on previous coeffs.: alf_luma_coeff_delta_prediction_flag
  Prediction based on fixed-filter coeffs: alf_luma_use_fixed_filter_flag
This proposal: Simplify by removing the prediction signaling.

## Slide 3: Proposed simplifications
Remove two existing prediction processes for signaling
alf_data( adaptation_parameter_set_id ) { | Descriptor
alf_luma_filter_signal_flag | u(1)
alf_chroma_filter_signal_flag | u(1)
if( alf_luma_filter_signal_flag ) { | 
alf_luma_clip_flag | u(1)
alf_luma_num_filters_signalled_minus1 | tb(v)
if( alf_luma_num_filters_signalled_minus1 > 0 ) { | 
for( filtIdx = 0; filtIdx < NumAlfFilters; filtIdx++ ) | 
alf_luma_coeff_delta_idx[ filtIdx ] | tb(v)
} | 
alf_luma_use_fixed_filter_flag | u(1)
if( alf_luma_use_fixed_filter_flag ) { | 
alf_luma_fixed_filter_set_idx | tb(v)
alf_luma_fixed_filter_pred_present_flag | u(1)
if( alf_luma_fixed_filter_pred_present_flag ) { | 
for( i = 0; i < NumAlfFilters; i++ ) | 
alf_luma_fixed_filter_pred_flag[ i ] | u(1)
} | 
} | 
alf_luma_coeff_signaldelta_flag | u(1)
if( !alf_luma_coeff_delta_flag && alf_luma_num_filters_signalled_minus1 > 0 ) | 
alf_luma_coeff_delta_prediction_flag | u(1)
alf_luma_min_eg_order_minus1 | ue(v)
for( i = 0; i < 3; i++ ) | 
alf_luma_eg_order_increase_flag[ i ] | u(1)
Removing two flags
  alf_luma_coeff_delta_prediction_flag
  alf_luma_use_fixed_filter_flag
Remove associated predictions

## Slide 4: Experimental results
Alternatives applied for both ALF coefficients and clip values
Remove prev. coefficient based
Remove fixed-filter based
Remove both

## Slide 5: Conclusions
Prediction process in signaling ALF coefficients has no significant benefit
Recommendation: to remove both prediction processes in VTM.
Cross-checker: X. Meng (PKU)