## Slide 1: Non-CE3: On signalling for intra coding mode in the MPM list
L. Pham Van, G. Van der Auwera, A. K. Ramasubramonian, V. Seregin, H. Huang, M. Karczewicz
@qualcomm
07/2019
AV

## Slide 2: Test 1: Planar flag is encoded using one context.
VTM5.0 :
unsigned ctx = (pu->cu->ispMode == NOT_INTRA_SUBPARTITIONS ? 1 : 0);
Test 1:
unsigned ctx = 1;
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.05% | -0.02% | 100% | 98%
Class A2 | 0.01% | -0.04% | -0.05% | 98% | 97%
Class B | 0.00% | 0.01% | 0.07% | 101% | 100%
Class C | -0.01% | -0.07% | 0.05% | 101% | 104%
Class E | -0.01% | -0.07% | -0.07% | 99% | 103%
Overall | 0.00% | -0.02% | 0.01% | 100% | 101%
Class D | -0.01% | 0.05% | -0.07% | 100% | 98%
Class F | 0.01% | -0.01% | 0.05% | 100% | 104%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.01% | 0.15% | 100% | 100%
Class A2 | 0.03% | 0.04% | 0.09% | 97% | 95%
Class B | -0.01% | -0.05% | -0.12% | 101% | 101%
Class C | -0.02% | -0.05% | -0.05% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | -0.02% | -0.01% | 100% | 100%
Class D | 0.05% | -0.04% | 0.41% | 100% | 101%
Class F | 0.01% | 0.01% | 0.14% | 100% | 100%

## Slide 3: Test 2: Planar flag is encoded using 3 contexts
Planar check of a block is unified with MPM list derivation:
A neighbor block is Planar if: not Intra || (is Intra and Planar) || is MIP
Context index (0, 1, 2) for Planar flag coding:
ctxIdx = left is Planar + top is Planar
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | 0.01% | -0.09% | 101% | 98%
Class A2 | -0.03% | -0.02% | -0.08% | 99% | 97%
Class B | -0.03% | -0.08% | -0.06% | 102% | 104%
Class C | -0.03% | -0.06% | -0.02% | 102% | 104%
Class E | -0.07% | -0.13% | -0.29% | 100% | 103%
Overall | -0.04% | -0.06% | -0.10% | 101% | 102%
Class D | -0.02% | 0.10% | -0.13% | 101% | 100%
Class F | -0.02% | 0.01% | -0.01% | 101% | 104%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.14% | 0.16% | 100% | 101%
Class A2 | 0.01% | 0.09% | -0.04% | 97% | 95%
Class B | 0.00% | -0.04% | -0.15% | 101% | 101%
Class C | -0.04% | -0.07% | -0.14% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.01% | -0.04% | -0.06% | 100% | 100%
Class D | 0.03% | -0.13% | 0.38% | 100% | 101%
Class F | 0.02% | -0.03% | 0.08% | 101% | 101%

## Slide 4: Test 3: Planar flag and first bin of MPM index are encoded using 3 contexts
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.01% | -0.03% | 94% | 111%
Class A2 | -0.08% | -0.09% | -0.09% | 101% | 103%
Class B | -0.09% | -0.16% | -0.09% | 99% | 101%
Class C | -0.07% | -0.08% | -0.09% | 77% | 102%
Class E | -0.11% | -0.18% | -0.13% | 76% | 98%
Overall | -0.09% | -0.11% | -0.09% | 89% | 103%
Class D | -0.06% | 0.13% | -0.02% | 77% | 98%
Class F | -0.11% | -0.08% | -0.09% | 82% | 98%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.29% | 0.08% | 98% | 99%
Class A2 | -0.02% | 0.12% | -0.01% | 100% | 98%
Class B | -0.03% | -0.03% | -0.28% | 101% | 100%
Class C | -0.03% | -0.15% | -0.05% | 83% | 97%
Class E |  |  |  |  | 
Overall | -0.03% | -0.08% | -0.09% | 95% | 99%
Class D | 0.01% | 0.00% | 0.05% | 86% | 96%
Class F | -0.05% | 0.00% | 0.02% | 86% | 98%

## Slide 5: Test 4:
Planar flag is encoded using 3 contexts (Test 2)
+ JVET-O0925
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.18% | -0.18% | -0.20% | 90% | 97%
Class A2 | -0.12% | -0.14% | -0.18% | 92% | 101%
Class B | -0.15% | -0.19% | -0.14% | 77% | 85%
Class C | -0.15% | -0.07% | -0.07% | 69% | 102%
Class E | -0.27% | -0.27% | -0.25% | 67% | 97%
Overall | -0.17% | -0.17% | -0.16% | 78% | 95%
Class D | -0.09% | 0.10% | -0.25% | 77% | 77%
Class F | -0.10% | 0.05% | 0.01% | 79% | 86%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 (2contexts for Planar flag) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.24% | -0.14% | 92% | 93%
Class A2 | 0.01% | 0.10% | 0.19% | 97% | 98%
Class B | 0.03% | 0.08% | -0.02% | 74% | 77%
Class C | -0.03% | -0.06% | -0.13% | 78% | 89%
Class E |  |  |  |  | 
Overall | -0.01% | -0.02% | -0.03% | 83% | 87%
Class D | 0.09% | 0.26% | 0.23% | 81% | 79%
Class F | -0.02% | 0.04% | 0.08% | 76% | 79%

## Slide 6: Test 5:
Planar flag and first bin MPM index are encoded using 3 contexts (Test 3)
+ JVET-O0925
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.21% | -0.21% | -0.25% | 91% | 97%
Class A2 | -0.17% | -0.24% | -0.23% | 92% | 96%
Class B | -0.20% | -0.23% | -0.25% | 93% | 103%
Class C | -0.17% | -0.18% | -0.12% | 94% | 103%
Class E | -0.29% | -0.27% | -0.30% | 93% | 104%
Overall | -0.21% | -0.22% | -0.23% | 93% | 101%
Class D | -0.10% | 0.09% | -0.10% | 94% | 101%
Class F | -0.22% | 0.03% | -0.16% | 98% | 104%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.23% | -0.07% | 95% | 100%
Class A2 | 0.00% | 0.31% | 0.21% | 95% | 96%
Class B | -0.01% | -0.05% | -0.14% | 96% | 100%
Class C | -0.01% | -0.06% | -0.06% | 95% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | -0.02% | -0.03% | 95% | 99%
Class D | 0.08% | 0.13% | 0.07% | 96% | 101%
Class F | -0.07% | -0.07% | 0.04% | 97% | 101%

## Slide 7: Comparison in AI
Test |  | Number contexts | Y(%) | U(%) | V(%)
JVET-O0484 PL flag coding only |  | 4 contexts for PL flag | -0.04% | -0.06% | -0.03%
JVET-O0748 | Test 1 | 1 context for PL flag | 0.00% | -0.02% | 0.01%
 | Test 2 | 3 contexts for PL flag | -0.04% | -0.06% | -0.10%
 | Test 3 | 3 contexts for PL flag 3 for first bin MPM | -0.09% | -0.11% | -0.09%
 | Test 4 | 3 for PL flag | -0.17% | -0.17% | -0.16%
 | Test 5 | 3 for PL flag 3 for first bin MPM | -0.21% | -0.22% | -0.23%

## Slide 8: Conclusion
Improvement of signalling for MPM modes has been proposed
Test 3 provides notable gains on top of JVET-O0925
It is recommended to adopt Test 3 + Regular intra flag (JVET-O0647) and JVET-O0925
Thanks LGE for cross-checking!