## Slide 1: Core Experiment Viewing Test Procedure and Results
JVET-O1118
Mathias Wien
Status: 2019-07-07 13:00h

## Slide 2: Test Setup
Procedure as CE11 test at last meeting [JVET-N0835]
LG OLED 55” display used, three test subjects per session at 1.6 × screen height distance
A-B-A-B presentation, assessment:
  “A was much better than B”
  “A was better than B”
  “B was better than A”
  “B was much better than A”.
Test cell design
  “A” – Video A – “B” – Video B – “A” – Video A – “B” – Video B – “Vote N”
  “A” / “B” presentation for 0.5sec
  Voting for 5sec

## Slide 3: Test Design
Placement of anchor and proposal as “A” and “B” randomized over test cells
Fixed order of sequences, looped over available test cells
Cell order (QP values, sub-CEs) randomized
Mix of (few) sequences which have various resolutions
  Decision to present all sequences up-scaled to UHD screen resolution using nearest neighbor interpolation

## Slide 4: Test Evaluation
Viewing votes mapping
  +3 : “Proposal much better than anchor”
  +1 : “Proposal better than anchor”
  -1 : “Anchor better than proposal”
  -3 : “Anchor much better than proposal”
Calculation of Mean Opinion Score (MOS) on this scale
Calculation of 95% confidence intervals based on MOS and standard deviation

## Slide 5: Overview on viewing sessions
CE05-3 (15 viewers, 12 cases) [completed]
CE05-2 (12 viewers, 60 cases) [completed]
Bilateral Filtering (12 cases) [completed]
NN-Filtering: Demo only – TBD

## Slide 6: JVET-O0548 Bilateral Filter Viewing Results
Test conducted Sun. 2019-07-07 09:30h
Sequences selected by proponents
5 groups of three experts = 15 test subjects
Presentation in one session with 12 test cells
  09:30 min viewing time per test cell (and group)

## Slide 7: CE05-2 Sequences under test
# | Class | Sequence name | Frame rate | Cod.str.
S01 | B | Cactus | 50 | RA
S02 | F | ArenaOfValor | 60 | LD
S03 | C | BasketballDrill | 50 | RA
S04 | A2 | CatRobot | 60 | RA
S05 | E | KristenAndSara | 60 | LD
S06 | B | BQTerrace | 60 | RA
S07 | C | PartyScene | 50 | RA
S08 | A2 | DaylightRoad2 | 60 | RA

## Slide 8: Bilateral Filter Results

## Slide 14: Closing
Thanks to all volunteers who participated in the tests
Thanks to Andrew Segall for providing the test PC, video player, and support
Thanks to Ericsson for providing OLED display
Thanks to Vittorio Baroncini for his guidance